## Slide 1: WF on Dynamic Blockage
Qualcomm, Intel, Interdigital, Nokia, ALU, ASB, Ericsson, [Samsung?, Mitsubishi] …
R1-161xxx
3GPP TSG RAN1 #AH Channel Model
Ljubljana, Slovenia, March 14 - 16, 2016
Agenda Item: 7

## Slide 2: Background
In R1-161150, below working assumption is agreed:
  The blockage caused by the static objects and moving objects such as human body and vehicle: The blockage attenuation generally increases with frequency
Further, in R1-161142 the following underlined agreements are also relevant towards the blockage modeling
  Channel model SI should take into account the outcome of RAN-level discussion in the ‘5G’ requirement study item
  Complexity in terms of Description, Generating channel coefficients, development complexity and Simulation time should be considered.
  Support frequency range up to 100 GHz.
    The critical path of the SI is 6 – 100 GHz
    Take care of mmW propagation aspects such as blocking and atmosphere attenuation.
  The model should be consistent in space, time and frequency
  Support large channel bandwidths (up to 10% of carrier frequency)
  Aim for the channel model to cover a range of coupling loss considering current typical cell sizes, e.g. up to km-range macro cells. Note: This is to enable investigation of the relevance of the 5G system using higher frequency bands to existing deployments.
  Accommodate UE mobility
    Mobile speed up to [500] km/h.
    Develop a methodology considering that model extensions to D2D and V2V may be developed in future SI.
  Support large antenna arrays

## Slide 3: Scope
The following blockage aspects are considered for modeling
  Far-field blocking:
    Effects due to human/small object blockage;
    Effects due to large objects like vehicles blockage
  Near-field blocking:
    Blocking effects due to the user operating his device (shadowing the region behind the user or blocking specific angles due to hand blocking the UE antennas)
The following are the modeling considerations:
  Human and small object blockers for InH
  Large and small object blocking in UMI and UMA scenarios
  Allowing for rotational and translational movement at the UE
  Allowing for spatial consistency in blocking
  Allowing for temporal evolution of blocking
  Allowing for frequency band dependent blocking

## Slide 4: WF Proposal
Propose a stochastic model for human and vehicle blocking:
Proposal A1: The blockers are modeled as (multiple) an angular blocking region as applied to the AoA/ZoA around the UE.
Proposal A2: One of the angular blocking regions represents self-blocking (i.e. human/hand holding the UE); this blocking region is not spatially consistent and UE specifically generated.
Proposal A3: The angles and sizes of the angular blocking region are generated according to a statistical process
  The center of the blocking region is uniformly chosen in the azimuth angle. Fixed in elevation
  Example 1: Size of the blocking region is x deg in azimuth and y deg in elevation, where x and y are constants.
  Example 2: A screen of fixed size is simulated at a randomly chosen distance ‘r’ and the angular blocking corresponding to this screen is chosen as the size of the angular blocking region
  The dependence of the parameters on the scenario (UMi, UMA and InH) is FFS
Example of Angular blockage: A solid angle (angular region) is considered as a blocked region undergoing additional attenuation
Example: One angular blocking to model self-blockage
Example: Second angular blocking to model human/vehicle blocking
UE
UE

## Slide 5: WF Proposal
Proposal A4: On number of angularly blocked regions (excluding self-blocking)
  The number of angularly blocked regions is a constant K (e.g. [1]) .
  FFS: The dependence on the number of angular blocked regions as a function of user density
Proposal A5:
  The clusters within the angular blocking regions are attenuated assuming a statistical model
  Example 1: A modified version of the knife edge based shadowing can be used
    The UE picks a random distance r and computes the knife edge shadowing corresponding to the size of blocking screen
  Example 2: Shadowing is chosen from a statistical distribution F(.) – exponential (lambda)
  FFS: The frequency dependence of lambda as a function of frequency

## Slide 6: WF Proposal
Proposal A6: The blocking model is made spatially consistent
  Example:
    Choice of grid size is assumed and blocking parameters for grid points are generated using above methods
    For intermediate points, the blocking parameters are generated using the same methods utilized for spatial consistency
Proposal A7: The blocking model is made temporally consistent
  Example:
    Parameters such as angular blocking width and position are temporally made consistent through similar techniques as used for spatial consistency
Proposal A8:
  Companies are encouraged to check one example modeling approach R1-161623 is in the framework of the above proposals A1-A7.
Note: The blockage does not change LOS/NLOS state of a link.
Temporal variability is on-demand.
Note: Blockage modeling is add-on feature.