## Slide 1: WF on LOS Pathloss Modeling
Huawei, HiSilicon, Samsung, Ericsson, DOCOMO, CMCC, Keysight, Fraunhofer HHI
R1- 161744
3GPP TSG RAN WG1 Ad Hoc meeting for Channel Model
Ljubljana, Slovenia, March 14-16, 2016
Agenda Item: 5.2

## Slide 2: Background
Offline discussion
  To be compatible to 3GPP 3D pathloss model
  Equation only, no CI or ABG discussion for LOS
The exsiting 3GPP(TR 36.876)/ITU(M.2135) models are below for information.
Note: the background information about the measurements campaigns that led to the model proposed in this WF will be provided in future meeting for information.
3D-UMi LOS | PL = 22.0log10(d3D) + 28.0 + 20log10(fc) PL = 40log10(d3D)+28.0+20log10(fc) –9log10((d'BP)2+(hBS - hUT)2) | σSF=3 σSF =3 | 10m < d2D < d'BP1) d'BP < d2D < 5000m1) hBS = 10m1), 1.5m ≦ hUT≦ 22.5m1)
3D-UMa LOS | PL = 22.0log10(d3D) + 28.0 + 20log10(fc) PL = 40log10(d3D)+28.0+20log10(fc) –9log10((d'BP)2+(hBS - hUT)2) | σSF =4 σSF =4 | 10m < d2D < d'BP4) d'BP < d2D < 5000m4) hBS = 25m4), 1.5m ≦ hUT ≦ 22.5m4)
ITU IMT-A InH LOS | PL = 16.9 log10(d) + 32.8 + 20 log10(fc) | σSF =3 | 3 m< d < 100 m hBS = 3-6 m hUT = 1-2.5 m
Scenarios | Models | Shadowing | Range

## Slide 3: Proposal
Scenarios |  | Pathloss (dB, d in m and f in GHz.) | σSF(dB) | Range
UMa |  |  | 4.1 4.1 | 10m < d2D < d‘BP* d'BP < d2D <5000m
UMi | Street canyon |  | 3.76 3.76 | 10m < d2D < d‘BP* d'BP < d2D <5000m
InH | Indoor office |  | 3.02 | 1-73m
 | Shopping mall |  | 2.01 | 0.5-149m
The below pathloss models for LOS are agreed
  The applicable frequency range of the PL formula is fL < fc < 100 GHz, where fL = 0.8 GHz.
* As defined in 36.873, d‘BP = 4 h’BS h‘UT fc/c, where fc is the centre frequency in Hz, c = 3.0108 m/s is the propagation velocity in free space, and h’BS and h‘UT are the effective antenna heights at the BS and the UT, respectively. In UMi scenario the effective antenna heights h’BS and h‘UT are computed as follows: h’BS = hBS – 1.0 m, h‘UT = hUT–1.0 m, where hBS and hUT are the actual antenna heights, and the effective environment height is assumed to be equal to 1.0 m. In UMa scenario the effective antenna heights h’BS and h‘UT are computed as follows: h’BS = hBS – hE, h‘UT = hUT – hE, where hBS and hUT are the actual antenna heights, and the effective environment height hE is a function of the link between a BS and a UT. In the event that the link is determined to be LOS, hE=1m with a probability equal to 1/(1+C(d2D, hUT)) and chosen from a discrete uniform distribution uniform(12,15,…,(hUT-1.5)) otherwise.