## Slide 1: WF on link-level model for high frequency spectrum up to 100GHz
Samsung, Huawei, HiSilicon, Ericsson
R1-161746
3GPP TSG RAN1 #AH Channel Model
Ljubljana, Slovenia, March 14 - 16, 2016
Agenda Item: 8

## Slide 2: Proposal
Agree on R1-161743 with the following modifications:
  Revise scenario names to CDL-A,B,C and TDL-A,B,C.
  Normalize delays in the tables so that RMS delay spread is 1 sec.
  Provide examples of delay spreads in terms of a scaling parameter
    The example scaling parameters are selected such that the RMS delay spreads are aligned with the typical 5G evaluation scenarios. Exact values are FFS
  For modeling effect of beamforming in a simplified way, an antenna pattern of brick wall (a rectangular mask) is introduced.
    This will give a TDL model from a CDL model
    Power should be normalized after the masking
    Angle scaling FFS
    Details FFS