## Slide 1: WF on NB-PSS
Intel Corporation, Acorn Technologies, CEWiT, ETRI, IITH, InterDigital, ITL, KT Corporation, Lenovo, Reliance-Jio, Samsung, Sequans Communications, Sierra Wireless, WILUS Inc.
R1-162016
3GPP TSG RAN WG1 NB-IoT Ad-Hoc Meeting
Sophia Antipolis, France, 22nd - 24th March 2016
Agenda item: 2.2.5

## Slide 2: Backgrounds
Agreements in RAN1 #84
  The periodicity of NB-PSS transmission is 10ms.
  The sequence for NB-PSS is generated at each OFDM symbol
    Length-11 Zadoff-Chu Sequence in frequency domain is used for sequence generation for each OFDM symbol and 11 REs are used per OFDM symbol.
    The 11 root sequence indices are FFS.
  NB-PSS is transmitted in subframe 5

## Slide 3: Backgrounds
In RAN1 NB-IoT Ad-Hoc2, it has been studied and evaluated for the proposal (next slide) by R1-161863, R1-161897, R1-161898, R1-161961, R1-161968 under both small (1.8kHz FO) and large frequency offsets (18kHz, 25.5kHz) in standalone and inband operation modes, according to the agreed simulation assumptions.
  The good cell search performances are depicted
  The good auto-correlation profiles are observed
  Various algorithms are supported with good performances and low detection complexity

## Slide 4: Proposal
10 different root sequence indices among 11 NB-PSS OFDM symbols
  Root index combination from symbol 0 to symbol 10 is [1 10 2 9 3 8 4 7 5 6 5]