## Slide 1
Summary of off-line discussion
Mini-slots
ZTE, ZTE Microelectronics
R1-1701343
3GPP TSG RAN1 NR_AH
Skopane, USA, 16th – w20th January 2017
Agenda item 5.1.4

## Slide 2: Overview
Following mini-slot properties have been discussed during the off-line discussion 2017-01-17, 13:30 – 14:30
  Mini slot length
  Mini-slot starting position
No time to discuss
  Control monitoring periodicity

## Slide 3: Current Agreements
Agreements:
NR-PDCCH monitoring at least for single-stage DCI design,
  NR supports the following minimum granularity of the DCI monitoring occasion:
    For slots: once per slot
    When mini-slots are used: FFS if every symbol or every second symbol
      FFS with respect to which numerology if slot and mini-slot have different numerology (e.g. SCS, CP overhead)
      Note: slot/mini-slot alignment is not assumed here
      Note: This may not apply in all cases
Agreements:
Mini-slots have the following lengths
  At least above 6 GHz, mini-slot with length 1 symbol supported
    FFS below 6 GHz including unlicensed band
    FFS for URLLC use case regardless frequency band
  FFS whether DL control can be supported within one mini-slot of length 1
  Lengths from 2 to slot length -1
    FFS on restrictions of mini-slot length based on restrictions on starting position
    For URLLC, 2 is supported, FFS other values
  Note: Some UEs targeting certain use cases may not support all mini-slot lengths and all starting positions
  Can start at any OFDM symbol, at least above 6 GHz
    FFS below 6 GHz including unlicensed band
    FFS for URLLC use case regardless frequency band
A mini-slot contains DMRS at position(s) relative to the start of the mini-slot

## Slide 4: 2 options for Mini-slot length
Option 1: 1-symbol is also supported for below 6 GHz
  Originally proposed by: ZTE, Ericsson, Nokia, Qualcomm, Convida Wireless,
  Also supported by CATT and Samsung, Sony
Option 2: The current agreement is sufficient for now
  Supported by LGE, Panasonic
Discussion:
  Pro option1: For the specification, we need to specify the 1-symb MS anyway, no gain to restrict ito above 6 GHz
  Pro option 2: No obvious need a for 1-symb below 6 Ghz
  In order to make progress, option-1 supporters (except Samsung) would accept to adopt option 2 for phase 1
Status: No consensus
  Most option 1 supporters could adopt option 2 in order to make progress
  Samsung: Want to introduce the 1 symbol mini-slot for below 6 GHz
  Panasonic, and LGE: Do not want to compromise and adopt Option 1
Suggestion how to move on:
  It is inefficient to raise the technical concerns orally .
  Samsung,LGE and Panasonic should write down their concerns and share them with the other companies, then these concerns can be compared in their relevance and hopefully an acceptable agreement can be reached.

## Slide 5: 3 options for Mini-slot starting position
Option 1: Adopt possibility of floating starting position also below 6GHz, possibility to configure a fixed grid is also given.
  Supported by: ZTE, Ericsson, Nokia, Qualcomm, Convida Wireless, Sony
Option 2: Adopt a fixed grid for for mini-slots
  Supported by: LGE, Panasonic
Option 3: Keep the existing agreements
  Supported by Panasonic
Status: No Consensus - continue discussion
  No time to discuss possible compromises
Suggestion how to move on
  Most companies support Option 1
  Supporters for options 2 and 3 could write down and send out their concerns for option 1.
  Then, we could compare them and hopefully find an agreement

## Slide 6: Mini-slot control monitoring periodicity
Current agreement
Control monitoring periodicity is configurable

## Slide 7: Proposal on control monitoring periodicity
Companies could then their comments on the following proposal for control monitoring of mini-slot:
Already agreed: The control monitoring is configurable Requirements for mmW: At least once per slot Requirements for unlicensed: Any symbol Requirements for mini-slots: Once per mini-slot, thus every second symbol
Thus we need the possibility to configure control monitoring every 2nd symbol in phase 1. It is easy to extend the RRC configuration to every symbol if needed in next release. Proposal 3: Minimum control monitoring periodicity on a fixed grid every second symbol. Note, this does not apply to all UEs.