## Slide 1: WF on beam-related indication for CSI-RS measurement
3GPP TSG RAN WG1 NR Ad-Hoc Meeting R1-1701381
Spokane, USA, 16th – 20th January 2017
Agenda Item: 5.1.2.3.1/5.1.2.3.5
ZTE, ZTE Microelectronics, ASTRI, Xinwei, vivo, NTT DOCOMO, Ericsson, Samsung, Intel, Huawei, HiSilicon, LG Electronics, Nokia

## Slide 2: Background
  Regarding beam related indication, it has been agreed that
    For downlink, NR supports beam management with and without beam-related indication
      When beam-related indication is provided, information pertaining to UE-side beamforming/receiving procedure used for data reception can be indicated through QCL to UE
        FFS: Information other than QCL

## Slide 3: Proposal
  Indication of QCL between the antenna ports of two CSI-RS resources is supported.
    By default, no QCL should be assumed between antenna ports of two CSI-RS resources.
    Partial QCL parameters (e.g., only spatial QCL parameter at UE side) should be considered.
  For downlink, NR supports CSI-RS reception with and without beam-related indication,
    When beam-related indication is provided, information pertaining to UE-side beamforming/receiving procedure used for CSI-RS-based measurement can be indicated through QCL to UE
    QCL information includes spatial parameter(s) for UE side reception of CSI-RS ports
      FFS: information other than QCL

## Slide 4: Example
  Two different CSI-RS resources corresponding CSI-RS in P-1 and P-2 respectively. Rx beams for P-2 is determined based on QCL information from P-1.Two CSI-RS resources correspond to two level CSI-RS for P-1 and P-2 respectively. Same RX beam at UE side is for this two level CSI-RS.