## Slide 1: WF on NR-LTE co-existence
CMCC, Softbank, CATT, Nokia, ASB
3GPP TSG RAN WG1 NR Ad Hoc Meeting R1-1701390
Spokane, USA, 16th – 20th January 2017
Agenda item: 5.1.9

## Slide 2: Background
In RAN1#87, the following agreements were reached on LTE-NR adjacent channel intra/inter operator co-existence
  For adjacent channel/band operation of NR and LTE in the unpaired spectrum
    Design at least one semi-statically assigned DL/UL transmission direction configuration for NR that avoids DL/UL interference with at least one LTE TDD DL/UL configuration and special subframe configuration
    This does not preclude at most one semi-statically DL/UL transmission direction configuration in NR specification
    Note: DL/UL interference also can be avoided by using dynamically assigned DL/UL transmission direction in some cases
    FFS: Backhaul signaling between NR and LTE for interference coordination
  FFS: Other mechanisms
In LTE TDD networks, various TDD UL/DL transmission configurations and special subframe configurations have been deployed or possible to be deployed.
For synchronized TDD network with all aligned UL/DL transmission direction of all cells, strong uplink interference caused by the downlink signal of remote base station could be observed in some atmospheric conditions that is favorable for producing tropospheric bending of VHF, UHF and/or microwave radio waves. It is expected by NR to be efficiently handle this issue.

## Slide 3: Proposal
NR supports efficient adjacent channel co-existence with LTE-TDD using UL-DL configurations 0,1,2,3,4,5 in unpaired spectrum
NR supports efficient adjacent channel co-existence with LTE-TDD using all the special subframe configurations in unpaired spectrum
NR supports longer maximum GP length and more flexible GP length compared to LTE TDD