## Slide 1: WF on Synchronization and Channel Raster
Qualcomm, CATT, Samsung
R1-1701409
3GPP TSG RAN WG1 NR Ad-hoc Meeting
Spokane, USA, 16th – 20th January 2017
Agenda item: 5.1.1.1.2

## Slide 2: Background
NR is expected to have deployments in wide frequency bands
In NR, DL cell-specific reference signal similar to LTE CRS might not be broadcast or not often enough, additionally working assumption is SYNC may not be in the center of carrier, this makes frequency scan impossible.
Potential NR/LTE waveform confusion since both NR and LTE employ OFDM-based waveforms in DL
In RAN1#87, the following was agreed:
Agreements:
The raster for NR synchronization signals can be different per frequency range. At least for frequency ranges where NR supports a wider carrier bandwidth and operation in a wider frequency spectrum (e.g. above 6 GHz), the NR synchronization signals raster can be larger than the 100 kHz raster of LTE.
A joint decision should be made on:
  the supported minimum carrier bandwidth for a NR carrier
  the supported bandwidths of synchronization signals for NR
  the frequency raster for synchronization signals for NR
  the frequency raster for the center of NR carrier (if applicable)
Working assumptions:
For a NR cell, the center frequency for the synchronization signal can be different from the center frequency of the NR carrier
  FFS: Relationship between the center frequency of the NR carrier and the center frequency of synchronization signals and investigate tradeoff between UE complexity and flexibility

## Slide 3: Proposal
Both channel raster and synchronization signal frequency raster should be integer multiple of all data/control subcarrier spacings supported for each NR frequency band
  For example of how this condition can be met, 60*n kHz (n being positive integer, i.e. 1, 2, 3 …) of channel raster in 2GHz will be a integer multiple of 15kHz, 30kHz, and 60kHz, and will satisfy the above condition
When the sync bandwidth is smaller than the minimum system bandwidth for a given frequency band that UE searches, synchronization signal frequency raster is sparser than the channel raster
When the sync bandwidth is the same as the minimum system bandwidth for a given frequency band that UE searches, synchronization signal frequency raster is the same as the channel raster
  FFS If UE is required to search for all the synchronization signal rasters