## Slide 1: WF on PRACH preamble numerology
ZTE, ZTE Microelectronics, Samsung, Nokia, ASB, NTT DOCOMO, CATT, Ericsson, LGE, Huawei, HiSilicon, MediaTek, Qualcomm, Sony, Intel, Sharp, Fujitsu
3GPP TSG RAN WG1 adhoc R1-1701458
Spokane, Washington, USA, 16th – 20th January 2017
Agenda item: 5.1.1.4.1

## Slide 2: Background
The Zadoff-Chu sequence that is used in LTE has good correlation properties and reasonable PAPR
At the RAN1#87 meeting it was agreed that the bandwidth for RACH is no wider than:
  5 MHz for carrier frequency below 6GHz
  [5, 10, 20] MHz for carrier frequency above 6GHz
In order to meet the timing accuracy and be robust against Doppler frequency a bandwidth larger than 5MHz is needed in the above 6GHz carrier frequency case
It can be observed from several contributions that in order to support extreme high speed case (>500 km/h) a SCS of at least 5KHz is needed, for the below 6GHz carrier frequency case
  For below 6GHz case a sequence length of 839 can meet the bandwidth requirement (839*5KHz = 4.195MHz)

## Slide 3: Proposal on: PRACH preamble numerology
For down selection purpose, until the next meeting do evaluation of the following RACH SCS alternatives at least considering
  Robustness towards Doppler frequency, Beam sweeping latency, Link budget, Cell size, RACH capacity, frequency offset
RACH SCS alternatives
  SCS = [1.25 2.5 5 7.5 10 15 20 30 60 120 240] kHz
    Note: in case RACH SCS = [15 30 60 120 240] there are two design options:
      use the same SCS as the UL data and control reference numerology
      use different SCS than the UL data and control reference numerology

## Slide 4: Proposal on: RACH preamble sequence type
The following RACH preamble sequence types are considered
  Zadoff-Chu
  m-sequence
  Zadoff-Chu with cover extension using m-sequence