## Slide 1: WF on Frozen Set Selection of Polar Codes
NTT DOCOMO, InterDigital, MediaTek, Qualcomm, ZTE, ZTE Microelectronics
R1-1701488
3GPP TSG RAN WG1 NR Ad-Hoc Meeting
Spokane, USA 16th - 20th January 2017
Agenda item 5.1.5.2.1

## Slide 2: Background
Agreement in RAN1#87
  UL eMBB data channels:
    Working Assumption to adopt flexible LDPC as the single channel coding scheme for small block sizes (to be confirmed unless significant issues are identified by the RAN1 Jan adhoc in relation to performance, implementation complexity and flexibility)
    (Note that it is already agreed to adopt LDPC for large block sizes)
  DL eMBB data channels:
    Adopt flexible LDPC as the single channel coding scheme for all block sizes
  UL control information for eMBB
    Adopt Polar Coding (except FFS for very small block lengths where repetition/block coding may be preferred)
  DL control information for eMBB
    Working Assumption to adopt Polar Coding (except FFS for very small block lengths where repetition/block coding may be preferred)
      To be confirmed unless significant issues are identified by the RAN1 Jan adhoc in relation to performance, latency, power consumption and implementation complexity

## Slide 3: Proposal
Nested sequence for ordered bit index sequence of information bits should be considered for polar codes
  e.g. For two codes with different mother code lengths, the positions of information bits can be selected based on the shortened version or nested extension of the mother sequence
  The length of the nested sequence is FFS