## Slide 1
3GPP TSG-RAN WG1 NR Ad-Hoc meeting R1-1701529
Spokane, USA 16th - 20th January 2017
Way Forward on CSI-RS for Beam Management
Intel, Qualcomm, Ericsson, Nokia, Alcatel-Lucent Shanghai Bell, [Samsung], Verizon Wireless, CATT, MTK, NTT Docomo, CMCC, ZTE, ZTE Microelectronics, KT, LG, vivo
Agenda item: 5.1.2.3.1

## Slide 2: Background
  The following agreements have been achieved in RAN1 87:
    NR CSI-RS supports the following mapping structure
      NP CSI-RS port(s) can be mapped per (sub)time unit
      Across (sub)time units, same CSI-RS antenna ports can be mapped
      Values of NP is FFS
      Here, “time unit” refers to n>=1 OFDM symbols in a configured/reference numerology, where the value of n is FFS
      FFS whether OFDM symbols comprising a time unit is consecutive or not
    Each time unit can be partitioned into sub-time units
      FFS Partitioning method, e.g., TDM, IFDMA, OFDM symbol-level partition with same/shorter OFDM symbol length(i.e. larger subcarrier spacing) as/than the reference OFDM symbol length (subcarrier spacing), and other methods are not precluded
  The following agreements have been achieved in RAN1 86:
    Specification supports multiplexing numerologies in TDM and/or FDM within/across (a) subframe duration(s) from a UE perspective

## Slide 3: Proposal
  One sub-time unit for CSI-RS can be equal or shorter than 1 OFDM symbol in a reference numerology.
    FFS: support one or both options for sub-time unit.
  If it is shorter than 1 OFDM symbol, support at least one of the following options:
      Opt1. IFDMA
      Opt2. Larger subcarrier spacing
      FFS: whether the above structure should be utilized for P-1, P-2 and/or P-3.
  If it is equal to 1 OFDM symbol, beam sweeping can be supported across multiple OFDM symbols.
  Consider overhead savings when combining P-3 with P-1 or P-2 CSI-RS beam sweeps.
  Consider UE beam switch latency and UE implementation complexity (e.g. AGC training time).