## Slide 1
3GPP TSG RAN WG1 NR Ad-Hoc Meeting R1-1701549 Spokane, USA, 16th - 20th January 2017
Agenda item: 5.1.6
WF on Enhanced Modulation Schemes
Sony, InterDigital, Samsung

## Slide 2: Background
In RAN1#86b, the following was agreed on modulation :
  The same constellation mapping as used in LTE (QPSK, 16QAM, 64QAM and 256QAM)
  is introduced, while not precluding other constellation mappings
    Note that there might be possibility to exclude some of above constellation mapping based on the further study
Enhancement modulation schemes for further study include
  Higher order modulation in conjunction with MIMO
  Constellation mapping among subcarriers
  Other constellations (e.g., non-uniform QAM)
  Coded modulations
  Spatial modulation
  Mappings of bits to symbol(s)
  Rotated-QAM up to BPSK, QPSK
-QAM (0<k<=1)
      FFS k (e.g., k = 0.5 for BPSK, 0.25 for QPSK)
  Constellation Interpolation
  Note: Other modulation schemes or combinations of the above schemes are not precluded
Note: Proponents should describe the details of the receivers

## Slide 3: Proposal
Capture in the evaluation section of the TR a description of, and observations on, the following enhanced modulation schemes proposed for NR:
  Higher order modulation e.g. 1024QAM
  Shaped Modulation
  Spatial Modulation
  Diversity enhancing modulation schemes
  Multi-level coding and natural mapping schemes
Draft TP in appendix

## Slide 4: Appendix
Higher-order Modulation
These schemes proposed the use of more bits to modulate each constellation point than in LTE such as 1024QAM which carries 10 bits per constellation point.
R1-1609632, “On modulation schemes for NR”, Ericsson, Lisbon, Portugal, October 10 – 14, 2016.

## Slide 5: Appendix
Shaped Constellations
It is well known that the use of uniformly distributed QAM symbols in coded communications leads to a shaping loss of up to 1.53dB for high order constellations. If shaping was used to make the distribution of the modulation symbols more Gaussian, this loss can be significantly reduced. During the SI, constellation shaping schemes proposed included non-uniform constellations (NUC) and probabilistically shaped coded modulation (PSCM). Companies observed significant gains over uniformly distributed QAM especially for high order constellations such as 256QAM and 1024QAM.
R1-164653, “Consideration of NU-QAM for the NR”, Sony, Nanjing, China, May23-27, 2016.
R1-1611284, “Performance of NU-QAM with LPDC codes for NR”, ETRI, Reno, USA, Nov 14 – 18, 2016
R1-1611214, “Signal Shaping for QAM Constellations”, Huawei, HiSilicon, Reno, USA, Nov 14 – 18, 2016

## Slide 6: Appendix
Spatial Modulation
Spatial modulation exploits both spatial and signal domains to achieve higher data rates by jointly mapping a block of information bits to a symbol in the signal-constellation diagram (e.g., QAM) and the spatial positions of the transmit-antenna in the antenna-array (e.g., SSK). Spatial modulation provides the benefit of lower power consumption, lower complexity/cost and performance advantage.
R1-165061, “Evaluation of Spatial Modulation for New Radio”, InterDigital Communications, Nanjing, China, May23-27, 2016

## Slide 7: Appendix
Diversity enhancing modulation
The basic underlying idea is to induce dependency among modulation symbols carried on different transmission resources. This provides additional gains derived from diversity and/or spreading. The schemes proposed during this SI include: signal space diversity (SSD) wherein after constellation rotation, the quadrature components of each QAM symbol are separated and mapped in different transmission resources thereby converting each M-QAM symbol into the Cartesian product of two Pulse-amplitude modulations (PAM). Another scheme proposed in this family augments linear spreading with multi-dimensional modulation and superposition to achieve both spreading and diversity gain. A third scheme proposed in this family was dual carrier modulation (DCM) and multi-carrier modulation (MCM) which modulate the same N bits to two or more symbols based on different mappings of 2N constellation points. These modulated symbols are allocated to different resource blocks to achieve diversity gain.
R1-1611544, “Signal Space Diversity use in NR”, Sony, Reno, Nevada, USA, November 14 – 18, 2016
R1-167570, “Performance Evaluation of Dual-Carrier Modulation for New Radio”, InterDigital Communications, Gothenburg, Sweden August 22-26, 2016.
R1-162163, “Applying Multi-Dimensional Modulation to Non-Orthogonal Multiple Access”, Huawei, HiSilicon, Busan, Korea, April 11-15, 2016.

## Slide 8: Appendix
Multi-level coding and natural mapping
Multi-level coding (MLC) and natural mapping were introduced as coded modulation and bits-to-symbol(s) mapping for higher order modulation in conjunction with MIMO. MLC and natural mapping enables an enhanced MIMO receiver, namely an integer forcing MIMO receiver, which can achieve higher spectral efficiency gain at comparable complexity over conventional MIMO schemes such as MMSE and MMSE-SIC consisting of BICM and Gray labeling for MIMO transmission
R1-166777, “Modulation scheme for MIMO”, Samsung, RAN1 #86.
R1-1612557, “Transmission and reception for high-order modulation in conjunction with MIMO”, Samsung, Reno, Nevada, USA, November 14 – 18, 2016.
R1-1613041, “Impact of channel estimation error on the performance of high spectral efficiency MIMO schemes”, Samsung, Reno, Nevada, USA, November 14 – 18, 2016.