## Slide 1: WF for Open Issues on CSI Reporting
Samsung, Ericsson, Huawei, HiSilicon, ZTE, Sanechips, Mediatek, NTT DOCOMO, Nokia, Nokia Shanghai Bell, KDDI, Vodafone, CEWiT, IITH, IITM, Tejas Networks, Verizon, Deutsche Telekom, Softbank, CHTTL, NEC, WILUS, Sharp, China Unicom, ITL, KRRI, CMCC, ASTRI, KT Corporation, BT
3GPP TSG-RAN WG1 NR-AH3 R1-1716726
Nagoya, Japan, 18th – 21st September 2017
Agenda: 6.2.2.2

## Slide 2: Procedures and UCI multiplexing
Refinement on R1-1715288

## Slide 3: Encoding for short PUCCH-based reporting
    Background:
      Maximum payload for short PUCCH is not yet fixed, but ~ 20-25 bits.
      Assuming delta CQI is not used, worst-case for a complete report CRI/CQI/PMI/RI is 3+8+PMI+3 = 14+PMI  short PUCCH is sufficient for containing P-CSI report for all scenarios
    Proposal:
      Short PUCCH is only used for the following cases:
        Wideband and partial-band reporting (one CSI for all the subbands in the CSI reporting band)
      The same information payload irrespective of RI/CRI in a given slot (to avoid blind decoding)
        Note: the size of information payload can be different according to the largest number of CSI-RS ports of the CSI-RS resources configured within a CSI-RS resource set
        Details to be decided in the uplink control channel coding session. For example:
          When PMI+CQI payload varies with RI/CRI, padding bits are added to RI/CRI/PMI/CQI prior to encoding to equalize the payload associated with different RI/CRI values
          RI/CRI/PMI/CQI, along with padding bits when necessary, is jointly encoded

## Slide 4: Encoding for long PUCCH-based reporting
    Background:
      Long PUCCH is used for subband reporting  differences in payload for different RI/CRI values tend to be large
        If padding bits are used to equalize the payload, too many padding bits may be needed
    Proposal:
      For wideband or partial-band reporting, use the same solution as short PUCCH
        The same payload irrespective of RI/CRI
      For subband reporting
        Use solution as for PUSCH (two-part encoding): slide 4 of R1-1715288
        Note: CRI/RI can be decoded first to determine the payload of PMI/CQI

## Slide 5: Encoding for PUSCH-based reporting
    Background: For Type II,
      The size of wideband amplitude info depends on RI and the size of PMI depends on both RI and wideband amplitude info
      The difference in payload between RI=1 and 2 is larger than that in Type I
    Proposal: For Type II,
      CSI parameters of a Type II CSI report are not multiplexed across multiple PUSCH transmissions
      Use a two-part scheme with
        Part 1 contains RI, CQI and indication of the number of non-zero wideband amplitude coefficients per layer
        Fixed payload size used for part 1; part 2 contains remaining CSI
          Indication of the number of non-zero wideband amplitude coefficients per layer in part 1

## Slide 6: Encoding for PUSCH-based reporting
    Proposal: Separately encoded parts of a CSI report on PUSCH carrying UL-SCH have different transmission priority
      Part 1 (used to identify the number of information bits in part 2) has higher priority
        Part 1 is first included in a transmission in their entirety before part 2
      Information bits and/or channel coded bits of part 2 can only be partially transmitted
        Omit CSI parameters corresponding to at least one subbands for part 2
          TBD by RAN1#90bis: if all of part 2 can be dropped as a special case
          TBD by RAN1#90bis: specify one of the following omission rules:
            Omitted subbands are determined based on a decimation ratio and/or a priority pattern used to order subband CSI (defined in specification)
            Omitted subbands are determined based on the measured subband CQI included in part 1

## Slide 7: CSI reporting characteristics
    Proposal:
      Type II CSI can be configured to be carried both on long PUCCH and on PUSCH
        CSI parameters of a report are not multiplexed across PUCCH or PUSCH transmissions
        Type II CSI reports carried on long PUCCH consist only of part 1
        Type II CSI reports carried on PUSCH consist both of part 1 and part 2,
          Taking into account CSI part priority in slide 6 on encoding for PUSCH-based reporting
        CSI reports on long PUCCH and on PUSCH are calculated independently
        Note: Whether a UE can be configured with Type II CSI reports on both long PUCCH and PUSCH is a UE capability
      Either a long or short PUCCH resource can be configured to carry a CSI report
        As long as payload size of long or short PUCCH is sufficient to avoid multiplexing a CSI report across multiple PUCCH transmissions
        Note: this allows a small CSI payload to be transmitted on long PUCCH e.g. for coverage
      Support S-CSI on PUSCH using similar mechanism to LTE SPS
        Resources/MCS for S-CSI on PUSCH are allocated semi-persistently using DCI
        S-CSI supports Type II with minimum periodicity of 5ms
      Support A-CSI on long and short PUCCH using higher-layer PUCCH resource configuration and DCI-based triggering

## Slide 8: Frequency granularity
Subband, partial band, wideband, and CSI reporting band
Subband sizes

## Slide 9: Proposal
Subband
CSI reporting band
2 Subbands
Partial band CSI-RS
Active bandwidth part
Carrier bandwidth
For CSI reporting, a subband is defined as N contiguous PRBs, the value of N depends on the bandwidth of the active bandwidth part
  FFS if value of N is fixed for a certain bandwidth or configurable from a set of values or if it depends on RBG /PRG size
A CSI reporting setting configuration defines a CSI reporting band as a subset of subbands of the bandwidth part, and following information is configured in CSI reporting setting
  Single / Multiple CQI:
    Single CQI is reported per CW for the entire CSI reporting band, if single CQI is configured
    CQI per CW per subband is reported for each subband in the CSI reporting band if multiple CQI is configured
  Single / Multiple PMI:
    Single PMI is reported for the entire CSI reporting band, if single PMI is configured
    PMI (only i2 for > 2 TX) is reported for each subband the CSI reporting band, if multiple PMI is configured
  The UE is not expected to be configured with a CSI reporting band which contains subbands where RSs for channel and interference are not present
  The subset of subbands can be configured to be contiguous or non-contiguous
Example

## Slide 10: CSI reporting content
Joint support for hybrid mechanism 1 and semi-open-loop [cf. R1-15008]

## Slide 11: Proposal
  A CSI report can contain only PMI consisting of only i1 using Type I single panel codebook and CRI/RI
    Note: i1 identifies a combination of variables {i1,1 and i1,2} or {i1,1 , i1,2, and i1,3} in 38.214 section 5.2.1.2
  A CSI report can contain only PMI consisting of only i1 using Type I single panel codebook, CQI and CRI/RI, computing CQI assuming PDSCH transmission with Np≥1 precoders, where
    UE can assume that one precoder is randomly selected from the set of Np precoders for each PRG on PDSCH
      The PRG size in CSI feedback is RRC configured
    The set of Np precoders for CQI calculation are indicated by codebook subset restriction

## Slide 12: Remaining codebook issues
Type II beam reporting [cf. R1-1714748]
Type II overhead reduction [cf. R1-1715002]
Codebook subset restriction for Type II + pending details for Type I SP/MP

## Slide 13: Type II beam reporting: background
Draft 38.214 defines the beam reporting index as follows
, ,
,
Joint beam reporting can save up to 8 bits (R1-1713590)
Joint beam reporting is proposed by at least three companies (R1-1713590, R1-1713764, R1-1714285)
Beams can be reported jointly using combinatorial numbering (R1-1713590, R1-1714285)
  Similar to how UE-selected subbands reports are defined in 36.213

## Slide 14: Proposal: Type II CSI beam reporting
is reported using a combinatorial coefficient table
  Given L and (N1,N2), rows and cols are used
to mapping
  Beam sorting: (assign indices such that increases as increases)
  where
to mapping
  For obtain using and the table
  ,
Note: to obtain , the following procedure can be used:
  Iterate over
    Find the largest s. t.
    , ,
Example of beam sorting

## Slide 15: Type II overhead reduction
Background:
  The Type II NR codebook was agreed at RAN1#89 as described in R1‑1709232
  The agreement includes the following in reference to the wideband (WB) amplitude feedback:
    PMI payload can vary depending on whether an amplitude is zero or not
      Details are FFS
  This WF proposes the details for achieving the reduced payload, where the payload reduction occurs in the feedback of subband (SB) differential amplitude and subband phase.
    A detailed description of the rationale behind the proposal can be found in R1-1716505
Proposal: For coefficients where the reported wideband amplitude is zero, the corresponding subband amplitude (if configured) and phase coefficients are not reported, with details defined on the next two slides.
  Apply the proposal to the NR Type II single-panel codebook and the NR Type II codebook for beamformed CSI-RS.

## Slide 16: Proposal: CBSR for Type II
Support RI restriction
Support DFT beam restriction based on DFT beam groups
  Partition DFT beams into beam groups comprising adjacent beams
    is the bottom-left DFT beam of the group, ,
    The group is defined as:
  CBSR is configured via and
    is a length- indicator which selects P beam groups for further restriction
      beam groups are selected
      is a length- bitmap and restricts DFT beams and associated maximum WB amplitude coefficients in for the i-th restricted (r1, r2) value in
      For each of the beams, a 2-bit indicator is used for amplitude restriction
      The associated WB amplitude coefficients for each layer and polarization of a beam shall be at most the indicated value
    Total length of and =
CSI reporting payload size is not impacted
Value of bit pair | Max WB beam power
00 | 0
01 | 
10 | 
11 | 1
Value of bit pair | 
00 | 0
01 | 
10 | 
11 | 1

## Slide 17: Proposal: Remaining details for Type I SP/MP CBSR
Type I SP, rank 3-4 codebooks for 16, 24, and 32 ports
  Use single bitfield, determine restricted depending on restricted
    FFS details
Type I MP
  Restrict DFT beams (defined in 38.214)
CSI reporting payload size is not impacted
No CBSR for 2Tx CB

## Slide 18: [Informative] Type II overhead reduction: definitions for specification
Let () be the wideband amplitude coefficient indicators for layer , where is the RI.
Let the strongest coefficient on layer be identified by ()
Let and () be the subband phase coefficient indicators and the subband amplitude coefficient indicators for layer , respectively, where is the RI.
is the configured PSK constellation size used for SB phase reporting (4 or 8).
is the number of full resolution subband coefficients when SB amplitude feedback is configured.
SubbandAmplitude is the higher layer parameter used to configure the amplitude feedback of the Type II codebook. It may be set to ‘OFF’ for no SB amplitude feedback or to ‘ON’ to report differential SB amplitude feedback.

## Slide 19: [Informative] Type II overhead reduction: specification text for the proposal
The reporting procedure for the amplitude and phase coefficients is modified as follows to include payload reduction for the subband indicators (changes in red). The proposal applies to both the Type II codebook and the Type II codebook extension for beamformed CSI-RS.
  The indicators , , and (). , , and are not reported for .
  The remaining elements of () are reported, where . Let () be the number of elements of that satisfy
  The remaining elements of and () are reported as follows:
    When SubbandAmplitude is set to ‘OFF’,
      for , and . is not reported for .
      For , the elements of corresponding to the coefficients that satisfy , as determined by the reported elements of , are reported, where and the remaining elements of are not reported and are set to .
    When SubbandAmplitude is set to ‘ON’,
      For , the elements of and corresponding to the strongest coefficients (excluding the strongest coefficient indicated by ), as determined by the corresponding reported elements of , are reported, where and . The values of are given in Table 5.2.1.2-21. The remaining elements of are not reported and are set to . The elements of corresponding to the weakest non-zero coefficients are reported, where . The remaining elements of are not reported and are set to .
      When two elements, and of the reported elements of are identical (), then element is prioritized to be included in the set of the strongest coefficients for and () reporting.