## Slide 1: Discussion Points on remaining details about RACH Procedure
Qualcomm
3GPP TSG RAN WG1 Meeting #NR-AH3 R1-1716810
Nagoya, Japan,
18th – 21th September 2017
Agenda item: 6.1.4.2
Document for decision

## Slide 2: Background
Following issues are essential features for RACH procedure, at least for single Msg1 perspective:
  SS block to RACH resource/preamble mapping
  UE’s SS block selection and corresponding RACH resource determination during handover
    Whether UE has to prioritize contention-free RACH resources over contention-based RACH resources
    Whether/which a network signaled parameter(s) to assist UE’s selection is supported
      E.g. If a contention-free RACH opportunity is within X time units of a contention-based RACH opportunity, the UE transmits the RACH preamble on the contention-free RACH resource
  RACH resource configuration
    Option 1: Semi-static configuration (similar to LTE)
    Option 2: Semi-static configuration + dynamic indication
  Timeline of RACH procedure (e.g. minimum gap between different RACH messages)
  Msg2 and Msg3 format
  RA-RNTI determination
  QCL assumptions in RACH Procedure
  Threshold for SS block selection
  RA-RNTI calculation

## Slide 3: Possible Agreement from Offline Discussion on 9/18/2017
At least for initial access,
  The PDSCH for RAR is confined within NR UE minimum DL BW for a given frequency band
  The PDSCH for Msg4 is confined within NR UE minimum DL BW for a given frequency band.
  FFS: If PDSCH for RAR and Msg4 are confined within initial active DL BWP.
Send an LS to RAN4 informing tone spacing and bandwidth of different RACH preamble formats
  Check if these RACH preamble formats are confined within UE’s minimum UL BW
  Assigned to Dhiraj (Samsung), r1-1716805

## Slide 4: Possible Proposals for Discussion/Agreement

## Slide 5: SS Block to RACH Resource/Preamble Mapping
At least for initial access, the association between SS blocks and RACH preamble indices and/or RACH resources is based on the actually transmitted SS blocks indicated in RMSI

## Slide 6: RACH Procedure Timeline - I
For RAR, X can be supported for the timing gap between the end of MSg1 transmission and the starting position of the CORESET
  Option 1: Value of X = 0 Ts
    Sufficient Tx-Rx transmission time is guaranteed on top of 0 Ts
      FFS whether the Tx-Rx transmission is 624 Ts or less (for 15KHz subcarrier spacing)
  Option 2: Value of X = 1 symbol using the RAR numerology
  Option 3: Value of X = 1 slot using the RAR numerology
  Other options
  Note: RAR window includes Gnb processing time

## Slide 7: RACH Procedure Timeline - II
Minimum required gap between Msg2 reception and Msg3 transmission, and between retransmission of Msg1 of RACH procedure, is X Ts
  Option 1: Value of X varies according to RACH preamble numerology
  Option 2: Value of X is same for all RACH preamble numerologies
  Exact value of X is FFS

## Slide 8: Threshold for SS Block Selection
Threshold for SS block selection configurable by network or fixed in the spec
  Option 1: Configurable by network
    1.1: RSRP based
    1.2: Msg1 transmission power based
  Option 2: Fixed in the spec
  Other options?

## Slide 9: Transmit Power for SS Blocks
Can RMSI indicate the transmit power for SS blocks?
  Option 1: Yes. See detailed proposal in the appendix
  Option 2: No

## Slide 10: Msg2 and Msg3 Formats
Support of mini-slots during RACH procedure
  Option 1: NR supports Msg2 and Msg 3 transmission in mini-slots or slots.
  Option 2: For contention free random access, NR supports gNB configuring Msg2 transmission in mini-slots based on UE capability
  Other options

## Slide 11: QCL Assumptions during RACH Procedure
As a baseline, support the QCL associations in contention based RACH procedure as follows:
  Message 2 is transmitted using the same TX beam as was used to transmit SS block the preamble the UE sent is associated to
  Message 3 is transmitted assuming the same RX beam at gNB as was used for PRACH preamble reception to which received RAR is associated to
  Message 4 is transmitted assuming the same TX beam as was used to transmit Message 2 if no beam reporting procedure was applied before Message 4

## Slide 12: Appendix (Proposals from Other Companies that can be discussed Offline)

## Slide 13: Huawei’s Proposal on SS Block Transmit Power
The initial preamble power (preambleInitialReceivedTargetPower) in RACH configuration and “SS block transmit power” is configured based on group.
  [4] groups, Tx power PTx, 0 (i.e., reference Tx power) of a first group with [8] bits and [3] relative power offsets (regarding to the reference Tx power PTx, 0 of the first group) with [2] bits, i.e., total [8+2*3 =14] bits
  [4] groups, Rx power PRx, 0 (i.e., reference Rx power of preambleInitialReceivedTargetPower) of a first group with [4] bits and [1] relative power offsets (regarding to the reference Rx power PRx, 0 of the first group) with [1] bits, i.e., total [4+1*3=7] bits
  FFS the groups definition, e.g., whether based on the group definition of the actually transmitted SS block indication in RMSI

## Slide 14: ZTE’s Proposals on Conveying Different Transmit Power for SS Blocks in RMSI
•RMSI can indicate transmit power offsets between different SS blocks
For below 6 GHz, the bitmap of actually transmitted SS blocks is expanded to X>1 bits
  The X bits per SS block indicate power offsets {0 dB, ..., OFF}
    E.g. X=2 bits per SS block indicate offsets {0 dB, -10 dB, -20 dB, OFF}
For above 6 GHz, the indication method is down-selected from the following options
  Option 1: The Bitmap-in-Group is expanded to X>1 bits per SS block.
    The X bits per SS block indicate power offsets {0 dB, ..., OFF}
    The same offsets are applied to all actually transmitted Groups
  Option 2: The Group-Bitmap is expanded to X>1 bits per Group.
    The X bits per Group indicate power offsets {0 dB, ..., OFF}
    The offset is applied to all actually transmitted SS blocks in the group
  Combination of Option 1 and Option 2
  FFS power offset indication if Alt.5 is selected
Note: SS blocks, except those with OFF indicated, are actually transmitted.

## Slide 15: Mediatek’s Proposal on RA-RNTI Calculation
In addition to f_id, NR down-selects one of the following alternatives for RA-RNTI calculation
  Alt.1: The slot number within a frame and the starting symbol index within a slot
  Alt.2: The RACH transmission occasion (RO) index in a radio frame
  Alt.3: The slot number in a radio frame
    Note: Besides RAPID, RAR indicates information of RO or symbol index within the slot when more than one RO is allocated within a slot
  Alt.4: The slot number in a radio frame and the index of SS blocks within a slot
    Note: RAPID in RAR should be redefined accordingly as the preamble index within the subset of RACH preamble indices and/or resources associated with one SS block
  Note: f_id is the index of RACH resources in the frequency dimension
  Other options?

## Slide 16: Qualcomm’s Proposal on Joint Encoding between Msg3 Waveform and Duration
Relationship between Msg3 duration and Msg3 waveform
  Option 1: NR supports joint encoding between Msg3 duration and Msg3 waveform (e.g. different sets of Msg3 duration are supported for CP-OFDM and DFT-S-OFDM)
  Option 2: Msg3 duration does not depend on Msg3 waveform (e.g. same sets of Msg3 duration are supported for CP-OFDM and DFT-S-OFDM)

## Slide 17: Qualcomm’s Proposal on Beam Reporting in RACH Procedure
NR supports gNB configuring reporting of additional SS block index, e.g., strongest SS block index, through Msg3 of contention based random access.
NR supports gNB configuring reporting of multiple SS block indices through Msg1 during CFRA procedure of handover

## Slide 18: Ericsson’s Proposals on Different Mapping From SS Block Index to RACH Resources/Preambles
With requirement on time separation of NR-RACH preambles corresponding to different SS-blocks, the set of NR-RACH preamble sequences in a cell is determined in the order of 1. the available cyclic shifts of a root Zadoff-Chu sequence 2. increasing root index 3. increasing NR-RACH preamble time instances within a slot 4. increasing slot index 5. increasing frequency allocation
With no time separation of NR-RACH preambles corresponding to different SS-blocks, the set of NR-RACH preamble sequences in a cell is determined in the order of 1. the available cyclic shifts of a root Zadoff-Chu sequence 2. increasing NRR-RACH preamble time instances within a slot 3. increasing root index 4. increasing frequency allocation 5. increasing slot index

## Slide 19: RACH Resource Group
Proposal: Define RACH resource group as a set of RACH resources sharing the same RA-RNTI
    DCI(s) scheduling RAR(s) on the PRACH preamble on each of the RACH resources within the RACH resource group is masked with the same RA-RNTI
    Network signals the number of RACH resources per RACH resource group
    Network signals the number of RAPIDs
    UE calculates the number of preambles per RACH resource within a RACH resource group

## Slide 20: LGE’s Proposal on RACH resource configuration - I
RACH configuration in RMSI provides time-frequency domain information on RACH resource
Time domain information of RACH resource
  RACH slot configuration is provided
    If a slot is reserved for RACH resource(s) in partial or full, it is called RACH slot
    RACH slot configuration within one radio frame
  RACH resource within the RACH slot(s)
    Starting symbol index within the RACH slot
    RACH resources are consecutive within the configured RACH slot, as baseline
  Specify [M] states on the RACH slot configuration (similar to LTE, see the appendix) per PRACH preamble subcarrier spacing
    For long sequence, RACH slot configuration is provided based on the SCS with either of [30, 15]khz
    For short sequence, RACH slot configuration is provided based on the SCS of PRACH preamble
    Note : each state has its own RACH slot intensity and/or periodicity
    Exact value of M is FFS

## Slide 21: LGE’s Proposal on RACH resource configuration - II
The number of RACH resource per slot and the total number of RACH resources are calculated based on the configured PRACH preamble format, i.e. RACH preamble length
  For example,
    If the configured format is one of {A0, B0, C0}, there are 12 RACH resources per RACH slot
    If the configured format is one of {A1, B1, C1}, there are 6 RACH resources per RACH slot
    If the configured format is one of {A2, B2}, there are 3 RACH resources per RACH slot
    If the configured format is one of {A3, B3}, there are 2 RACH resources per RACH slot
    If the configured format is 1, there is one RACH resource per slot (1ms long)
    If the configured format is 2, there is one RACH resource consuming two slots (2ms long)
    …..

## Slide 22: LGE’s Proposal on RACH resource configuration - III
Frequency domain information of RACH resource is indicated by following parameters
  UL initial BWP
  Offset from the center of the UL initial BWP or resource allocation information within the BWP

## Slide 23: CATT’s Proposals on for NR Contention-Free PRACH Procedure
For contention-free RA procedure trigger by PDCCH order
  SCS for Msg 1
    Configured in the RACH configuration in RMSI.
  SCS for Msg 2
    The same as the SCS of the PDCCH order that triggers the RACH event