## Slide 1: WF of joint proposal on SUL
Huawei, HiSilicon, BT Group, CMCC, CATR, China Telecom, China Unicom, Deutsche Telekom, Intel, LGE, MediaTek, Nokia, Nokia Shanghai Bell, NTT DOCOMO, OPPO, Orange, Vivo, Vodafone
3GPP TSG RAN WG1 meeting NR#3 R1- 1716885
Nagoya, Japan, 18– 21 September, 2017
Agenda item: 6.6

## Slide 2: Background
Agreements:
Specify mechanisms for supporting supplementary Uplink frequency
  Note: SUL herein refers to the case when there is only UL resource for a carrier from NR perspective
  Use SUL as complimentary access link (including from random access point of view) to NR TDD and to NR FDD, where the UE may select PRACH resources either in the NR TDD/FDD uplink frequency or the SUL frequency.
  Note: The SUL frequency can be a frequency shared with LTE UL(at least for the case when NR spectrum is below 6 Ghz).
    Minimize impact to NR physical layer design to enable this co-existence
  Note: whether or not UE has to support simultaneous transmission on uplink frequencies is a separate discussion

## Slide 3: Background
Agreements:
For NR standalone operation for a UE,
  NR supports that the UE is allowed to transmit on UL carriers on different frequency ranges but the UE has the capability to only transmit on one of the carriers at a given time in the following case:
    case of SRS carrier switching with at least one of the frequency ranges agreed for LTE-NR UL sharing by RAN4 (e.g. refer to R4-1704411)

## Slide 4: Proposal
A SUL carrier associated with a DL carrier can use a subcarrier spacing smaller than or equal to the subcarrier spacing of the DL carrier.
Note:
  The SUL carrier can carry UCI for the associated DL carrier
  The SUL carrier is scheduled from the associated DL carrier