## Slide 1: Summary on CA Aspects
Samsung
R1-1801088
3GPP TSG RAN WG1 NR AH1801
Vancouver, Canada, Jan. 22 – 26, 2018
Agenda item 7.3.4.2

## Slide 2: Semi-static HARQ-ACK Codebook
DL association set determination for HARQ-ACK transmission in slot n needs to be defined/agreed
  Text currently used in 38.213 is not correct
DL association set for slot n is determined by
  PDSCH in slot(s) n-K1 corresponding to configured K1 values (by HARQ-timing-value-K1)
    May need to consider interaction with semi-static UL/DL configuration
  PDCCH occasions in slot(s) n-K0-K1 corresponding to configured K1 values and K0 values (by PDSCH-SymbolAllocation)
    Can be more than one PDCCH in one PDCCH occasion, e.g., cross-slot/cross-CC scheduling

## Slide 3: Semi-static HARQ-ACK Codebook
For ‘slot-based’ scheduling (PDSCH mapping type A), up to one PDSCH occasion for each valid slot in DL association set.
For ‘non-slot-based’ scheduling (PDSCH mapping type B), up to X PDSCH occasion(s) for each valid slot in DL association set.
X = all non-overlapped PDSCH mapping type B symbols (by pdsch-symbolAllocation)
Configuration is per BWP which can dynamically vary  HARQ-ACK codebook needs to be independent of BWP
 HARQ-ACK codebook needs to be determined from superset of possible PDSCH occasions over all configured BWPs
Observation 1: The above may be used to describe the DL association set
Observation 2: The resulting HARQ-ACK codebook can be very over-dimensioned and large particularly with CBG or CA configuration

## Slide 4: Semi-static HARQ-ACK Codebook
Offline outcome: Provide draft specification text assuming semi-static HARQ-ACK codebook determination based on configured K1 values (by HARQ-timing-value-K1) and non-overlapped PDSCH mapping type B symbols (by pdsch-symbolAllocation)
  Consider super-set over all configured DL BWPs
  Consider semi-static UL/DL configuration
    FFS for dynamic SFI affecting HARQ-timing-value-K1 and by pdsch-symbolAllocation)
Clarify how many PDSCHs a UE can simultaneously receive in a same BWP

## Slide 5: HARQ-ACK Codebook
Fallback DCI
  Should it include counter/DL total DAIs or UL total DAI?
Offline outcome: Few inputs, no progress
PUSCH selection for HARQ-ACK multiplexing in case of UL CA
  According to cell index
  By indication in UL DCI
Offline outcome: Few inputs, no progress

## Slide 6: HARQ-ACK Codebook
SPS PDSCH – Location of HARQ-ACK bits in HARQ-ACK codebook is as in LTE
Offline outcome: There seems to be consensus to “place HARQ-ACK bits in response to SPS PDSCH prior to ones in response to dynamic PDSCH in the HARQ-ACK codebook”.
Semi-static HARQ-ACK codebook: HARQ-ACK feedback in response to fallback DCI for cell with CBG configuration
  For dynamic HARQ-ACK codebook, agreement is to use TB-based HARQ-ACK (works due to DAI)
  For semi-static HARQ-ACK codebook, CBG-based HARQ-ACK seems needed as there is no DAI
Offline outcome: There seems to be consensus that “for semi-static HARQ-ACK codebook, the UE provides CBG-based HARQ-ACK in response to detecting DCI format 1_0 for PDSCH reception on a cell with configuration for CBG-based HARQ-ACK”

## Slide 7: HARQ-ACK Codebook - Misc
Dynamic HARQ-ACK bundling when minimum achievable code rate is larger than configured code rate
  Across CBGs of same TB
  Across TBs of same PDSCH
  Across TBs of different PDSCHs in same cell (time domain) or different cells (cell domain)
Offline outcome: Continue discussion whether, when a HARQ-ACK code rate is larger than the configured code rate, to (a) support dynamic HARQ-ACK bundling, (b) specify that the UE transmits HARQ-ACK with the minimum achievable code rate, or (c) capture that UE is not expected to handle this case
Semi-static HARQ-ACK codebook: Should ‘fallback’ PUCCH be used when UE receives only a single PDSCH for corresponding DL association set?
  i.e. semi-static HARQ-ACK codebook is either 1-2 bits or maximum number of bits
Offline outcome: All (limited) opinions were in favor. Details FFS

## Slide 8: References