## Slide 1: WF on LTE HARQ-ACK resource determination in EN-DC
Nokia, Nokia Shanghai Bell, NTT DoCoMo, ZTE
3GPP TSG RAN WG1 Meeting AH 1801
Vancouver, Canada, January 22nd -26th, 2017
Agenda item 7.5
R1-1801111

## Slide 2: Background
Agreements in RAN1#90:
When the UE is configured with multiple UL carriers on different frequencies (where there is at least one LTE carrier and at least one NR carrier of a different carrier frequency), but the UE operates on only one of the carriers at a given time among a pair of LTE and NR carriers
  For LTE carrier, UE can be configured with
    Case 1: DL-reference UL/DL configuration defined for LTE-FDD-SCell in LTE-TDD-FDD CA with LTE-TDD-PCell
      For scheduling/HARQ timing of LTE FDD carrier, DL-reference UL/DL configuration defined for LTE-FDD-SCell in LTE-TDD-FDD CA with LTE-TDD-PCell is applied
      UE is allowed to transmit NR UL signals at least in the subframe(s) where LTE UL transmission is not allowed according to the DL-reference UL/DL configuration
      FFS whether or not a UE-specific subframe offset for the DL-reference UL/DL configuration can be configured considering system resource utilization and potential spec impact
    Case 2: Release 15 LTE-FDD HARQ timing
      No impact on LTE RAN1 specifications
    Note: it doesn’t necessarily imply that UE has to support both cases

## Slide 3: Background
It was agreed in email discussion thread [90b-NR-39] UL TDM in single Tx EN-DC that the HARQ subframe offset can be configured per UE
In case UE is configured with PUCCH format 1b with channel selection for HARQ-ACK feedback, in legacy release, FDD PUCCH resource can be derived
  Implicitly: via lowest CCE. And FDD is the Pcell, or the PDSCH on SCell is cross-carrier scheduled by Pcell
  Explicitly: via RRC configuration. And FDD is Scell in FDD CA or FDD-TDD CA, TDD is Pcell and PDSCH is self-scheduled
In legacy Release, If UE is configured with PUCCH format 3/4/5 for HARQ-ACK feedback, PUCCH resources are configured by RRC signalling

## Slide 4: Proposal:
If UE is configured with EN-DC, for case 1 DL-reference UL/DL configuration is configured for LTE FDD carrier
  If PUCCH format 1b with channel selection is configured for HARQ-ACK feedback with DL-reference UL/DL configuration #0/#1/#6
    PUCCH resource is implicit derived from lowest CCE for PDSCH scheduled/cross carrier scheduled by Pcell
    PUCCH resources are explicitly configured by RRC signaling for PDSCH on Scell and self-scheduled
  If PUCCH format 3/4/5 is configured for HARQ-ACK feedback, four PUCCH resources are explicitly configured by RRC signaling for LTE carrier, fallback operation is supported