## Slide 1: Agenda Item: 7.3.2.1 Source: Huawei, HiSilicon Title: Further analysis on re-ordering of length-12 CGS Document for: Discussion and decision
3GPP TSG RAN WG1 Ad Hoc Meeting R1-1801232
Vancouver, Canada, January 22nd – 26th, 2018

## Slide 2: Performance Analysis
 | Length-36 | Length-48 | Length-60 | Length-72 | Length-96 | Length-192
Length-12 | 9 | 7 | 10 | 9 | 10 | 9
Max.Corr. | 0.872 | 0.8677 | 0.8949 | 0.8749 | 0.8782 | 0.8759
Table 1 number of sequences pair with cross-correlation higher than 0.8 before re-ordering
Table 2 number of sequences pair with cross-correlation higher than 0.8 after re-ordering
 | Length-36 | Length-48 | Length-60 | Length-72 | Length-96 | Length-192
Length-12 | 1 | 2 | 2 | 1 | 1 | 1
Max.Corr. | 0.831 | 0.8111 | 0.8241 | 0.8074 | 0.8131 | 0.8599
Note: the ordering proposed in R1-1800088 is used in Table 2.
Note: Sequences for length>72 shows similar result of cross-correlations due to the grouping function for sequences >=36

## Slide 3: Performance Analysis
For cross-correlation in page 2, for each pair of sequences, all cyclic shifts of the short sequence and all cyclic shifts of long sequence(ZC sequence) are considered with time shift granularity 1/(32*N_length), where N_length is the length of the long sequence.
  cross-correlation is between a shift version of a short sequence and a shift version of a long sequence
For cross-correlation in page 2, all possible frequency positions of short sequence are considered. For example, for length-12 CGS and length-36 sequence, following overlap scenarios are all considered:
  Note: cross-correlation evaluation result is same for all possible overlap scenarios because of the property of ZC sequences.

## Slide 4: Example for all frequency positions of short sequence
For length-12 CGS {1,-1,3,1,1,-1,-1,-1,1,3,-3,1} and length-36 sequence with u=1, maximum cross-correlations and CDF of cross-correlation for the possible overlap scenarios are shown below
The cross-correlation evaluation results are almost same for all possible overlap scenarios.
Scenario 1 | Scenario 2 | Scenario 3
0.56957 | 0.56985 | 0.56983
Table 3 maximum cross-correlations
Chart: Cross-correlation
Note: three curves are almost overlapped

## Slide 5
Proposal :
Support CGS re-ordering for CGS length-12, length-18 and length-24 in NR with the following revision in section 5.2.2.2 of 38.211
  Replace Table 5.2.2.2-2 with table 6 in R1-1800088
  Replace Table 5.2.2.2-3 with table 5 in R1-1800088
  Replace Table 5.2.2.2-4 with table 4 in R1-1800088