## Slide 1: Way forward on provision of time reference
Huawei, HiSilicon, Ericsson, Vodafone, China Telecom
3GPP TSG-RAN2 Meeting #101b
Sanya, China, 16 – 20 April 2018
R2-1806429

## Slide 2: Background
The WI LTE HRLLC targets June 2018 (RAN#80) for completion. There are only two RAN2 meetings (RAN2#101b and RAN2#102) before completion of the WI.
Provision of time reference is a second priority item for Rel-15 as identified in RAN plenary endorsed RP-180586.
At RAN2#101b, under AI 9.15.4, there is an email discussion report of [101#45] and some contributions on time granularity design and solutions.

## Slide 3: Proposed WF (1/2)
Based on email report R2-1805476, it is proposed to agree on the following compromise solution on time granularity:
Proposal 1: About time granularity:
eNB transmits a time reference information with a sufficiently fine granularity value
  for further discussion: choose only one granularity value (either 0.25 us or 1us)
In addition to the above time reference information, eNB can optionally transmit an inaccuracy indication of the time reference information
  The indication indicates inaccuracy of a time reference information
  If the inaccuracy indication is not transmitted, then the inaccuracy of the time reference information is not specified (i.e., the inaccuracy is implementation related).
  The encoding of the inaccuracy indication can be for further discussion. One example is:
    Inaccuracy = 0.25 * (k+1) us, in which k is an integer and the range is {0, 1, 2, ..., 3999}, and thus the range of inaccuracy is {0.25us, 0.5us, 1us, …, 1ms}

## Slide 4: Proposed WF (2/2)
Based on contributions other than the above email report, it can be seen that GPS time is a good reference for indicating time reference information. Regarding solutions, basically there are broadcast solution and unicast solution, and both solutions are useful depending on scenarios and operators’ requirements. So it is proposed:
Proposal 2: GPS time (continuous time) is used to indicate different granularities. FFS on details.
Proposal 3: Agree on both broadcast solution (via SIB16) and unicast solution (via dedicated RRC signalling) to transmit the time reference information (in proposal 1). FFS on solution details.
Considering there is only one meeting left for this WI, it will be helpful to have an email discussion to agree on the WF, so it is proposed:
Proposal 4: Agree on an email discussion to agree on the WF (i.e. proposal 1, 2 and 3).

## Slide 5: References
R2-1804939 | Time Synchronization for URLLC | Qualcomm Incorporated
R2-1805142 | UE Time Synchronization | Ericsson
R2-1805143 | Draft CR for introduction of Granular UE Time Reference for LTE | Ericsson
R2-1805476 | Email discussion summary on [101#45][LTE/HRLLC] The granularity of time reference discussion | Huawei
R2-1805477 | Discussion on time reference information | Huawei, HiSilicon
R2-1805478 | Discussion on solutions on transmission of time reference information | Huawei, HiSilicon
R2-1805479 | Introduction of providing sufficiently granular time reference information | Huawei, HiSilicon
R2-1805480 | Introduction of providing sufficiently granular time reference information | Huawei, HiSilicon