## Slide 1: WF for TD-LTE CP latency
CATT, CMCC, MediaTek Inc.
R2-1808796
3GPP TSG-RAN WG2 Meeting #102
Busan, Korea, 21st - 25th May 2018

## Slide 2: Back ground – evaluation for FDD
Component | Description | Latency [ms]
1 | Average delay due to RACH scheduling period (1TTI) | 0.5
2 | Transmission of RACH Preamble | 1
3 | Preamble detection and processing in eNB | 2
4 | Transmission of RA response | 1
5 | UE Processing Delay (decoding of scheduling grant, timing alignment and C-RNTI assignment + L1 encoding of RRC Connection Resume Request) | 4
6 | Transmission of RRC Connection Resume Request | 1
7 | Processing delay in eNB (L2 and RRC) | 3
8 | Transmission of RRC Connection Resume | 1
9 | 9.1 Processing delay in the UE (L2 and RRC), i.e., from reception of RRC Connection Resume to the reception of UL grant | 6
 | 9.2 transmission of UL grant by eNB | 1
 | 9.3 processing delay in the UE (processing of UL grant and preparing for UL tx) | 3
10 | Transmission of RRC Connection Resume Complete and UP data | 0
 | Total delay [ms] | Not more than 23.5
Notes |  | 
1 | In step 5, the latency of 4ms has been agreed by RAN1, see LS in R2-1806411 | 
2 | In step7, the processing delay in eNB (L2 and RRC) has been reduced to 3ms. | 
3 | In step 9.1, RRC connection resume message only include MAC and PHY configuration. No DRX, SPS, CA, or MIMO re-configuration will be triggered by this message. | 
4 | In step 10, the latency associated to the Transmission of RRC Connection Resume Complete and UP data is assumed to be 0ms | 
Note: for FDD, C9 would be further reduced and C1 is proposed to be 0ms.

## Slide 3: Average latency for TDD UL
Component | Average TD-LTE CP Latency for UL Data Transmission [ms] |  |  |  |  |  | 
 | Config 0 | Config 1 | Config 2 | Config 3 | Config 4 | Config 5 | Config 6
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2 | 1 | 1 | 1 | 1 | 1 | 1 | 1
3 | 3 | 2 | 2 | 2.7 | 2 | 2 | 2.5
4 | 1 | 1 | 1 | 1 | 1 | 1 | 1
5 | 4.8 | 5.4 | 5.8 | 4.8 | 5.7 | 5.9 | 4.5
6 | 1 | 1 | 1 | 1 | 1 | 1 | 1
7 | 3 | 3 | 3 | 3 | 3 | 3 | 3.3
8 | 1 | 1 | 1 | 1 | 1 | 1 | 1
9 | 7/6 | 7/6 | 10/6 | 7/6 | 7/6 | 15/6 | 7/6
10 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Total delay [ms] | 21.8/20.8 | 21.4/20.4 | 24.8/20.8 | 21.5/20.5 | 21.7/20.7 | 29.9/20.9 | 21.3/20.3

## Slide 4: Average latency for TDD DL
Component | Average TD-LTE CP Latency for DL Data Transmission [ms] |  |  |  |  |  | 
 | Config 0 | Config 1 | Config 2 | Config 3 | Config 4 | Config 5 | Config 6
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2 | 1 | 1 | 1 | 1 | 1 | 1 | 1
3 | 3 | 2 | 2 | 2.7 | 2 | 2 | 2.5
4 | 1 | 1 | 1 | 1 | 1 | 1 | 1
5 | 4.8 | 5.4 | 5.8 | 4.8 | 5.7 | 5.9 | 4.5
6 | 1 | 1 | 1 | 1 | 1 | 1 | 1
7 | 3 | 3 | 3 | 3 | 3 | 3 | 3.3
8 | 1 | 1 | 1 | 1 | 1 | 1 | 1
9 | 4 | 3 | 2/3 | 0/1/2/3 | 0/1/2/3 | 0/1/2/3 | 0/3.8
10 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Total delay [ms] | 18.8 | 17.4 | 16.8/17.8 | 14.5/15.5/ 16.5/17.5 | 14.7/15.7/ 16.7/17.7 | 14.9/15.9/ 16.9/17.9 | 14.3/18.1
Note: for DL transmission, multiple subframes could be used during step 9, it depends on when the network can transmit DL data after Msg 4 transmission. In this table, it assumes the DL data can be transmitted after 0/1/2/3 subframes.

## Slide 5: Way forward for TD-LTE for ITU submission
For DL data transmission, all TDD UL/DL configurations can achieve the IMT-2020 requirements.
For UL data transmission, the best average latency is 20.3ms (if C9 is 6ms) / 21.3ms (if C9 is 7ms) of TDD UL/DL configuration 6 which is almost 20ms. And it is ok for TDD to provide some best cases of some UL/DL configuration to achieve the IMT-2020 latency requirement for UL data transmission.

## Slide 6: Proposals
C1 is removed from the evaluation table (or kept as 0ms).
C5 is kept as 4ms.
C7 is kept as 3ms.
C9 is reduced to [6/7]ms (would be the same value as FDD) which UL grant should be transmitted earlier, e.g. together with Msg 4, or two subframes later than Msg 4 transmission.

## Slide 7: CP Latency of TD-LTE (in case of C9 is 7ms)
Component | Description | TD-LTE CP Latency [ms]
 |  | Con 0 SF 2,7 Con 1 SF 2,7 Con 3 SF 1, 2 Con 4 SF 2 Con 6 SF 2,7
1 | Average delay due to RACH scheduling period (1TTI) | 0
2 | Transmission of RACH Preamble | 1
3 | Preamble detection and processing in eNB | 2
4 | Transmission of RA response | 1
5 | UE Processing Delay (decoding of scheduling grant, timing alignment and C-RNTI assignment + L1 encoding of RRC Connection Resume Request) | 4
6 | Transmission of RRC Connection Resume Request | 1
7 | Processing delay in eNB (L2 and RRC) | 3
8 | Transmission of RRC Connection Resume | 1
9 | 9.1 Processing delay in the UE (L2 and RRC), i.e., from reception of RRC Connection Resume to the reception of UL grant | 7
 | 9.2 transmission of UL grant by eNB | 
 | 9.3 processing delay in the UE (processing of UL grant and preparing for UL tx) | 
10 | Transmission of RRC Connection Resume Complete and UP data | 0
 | Total delay [ms] | 20
Notes |  | 
1 | In step 5, the latency of 4ms has been agreed by RAN1, see LS in R2-1806411 | 
2 | In step7, the processing delay in eNB (L2 and RRC) has been reduced to 3ms. | 
3 | In step 9.1, RRC connection resume message only include MAC and PHY configuration. No DRX, SPS, CA, or MIMO re-configuration will be triggered by this message. | 
4 | In step 10, the latency associated to the Transmission of RRC Connection Resume Complete and UP data is assumed to be 0ms | 

## Slide 8: CP Latency of TD-LTE (in case of C9 is 6ms)
Component | Description | TD-LTE CP Latency [ms] |  | 
 |  | Con 0 SF 1,6 Con 1 SF 1,6 Con 2 SF 1,6 Con 3 SF 1 Con 4 SF 1 Con 5 SF 1 Con 6 SF 1,6 | Con 0 SF 2,7 Con 1 SF 2,7 Con 3 SF 2,3 Con 4 SF 2 Con 6 SF 2,7 | Con 6 SF 4,5
1 | Average delay due to RACH scheduling period (1TTI) | 0 | 0 | 0
2 | Transmission of RACH Preamble | 1 | 1 | 1
3 | Preamble detection and processing in eNB | 2 | 2 | 2
4 | Transmission of RA response | 1 | 1 | 1
5 | UE Processing Delay (decoding of scheduling grant, timing alignment and C-RNTI assignment + L1 encoding of RRC Connection Resume Request) | 5 | 4 | 4
6 | Transmission of RRC Connection Resume Request | 1 | 1 | 1
7 | Processing delay in eNB (L2 and RRC) | 3 | 3 | 4
8 | Transmission of RRC Connection Resume | 1 | 1 | 1
9 | 9.1 Processing delay in the UE (L2 and RRC), i.e., from reception of RRC Connection Resume to the reception of UL grant | 6 | 6 | 6
 | 9.2 transmission of UL grant by eNB |  |  | 
 | 9.3 processing delay in the UE (processing of UL grant and preparing for UL tx) |  |  | 
10 | Transmission of RRC Connection Resume Complete and UP data | 0 | 0 | 0
 | Total delay [ms] | 20 | 19 | 20
Notes |  |  |  | 
1 | In step 5, the latency of 4ms has been agreed by RAN1, see LS in R2-1806411 |  |  | 
2 | In step7, the processing delay in eNB (L2 and RRC) has been reduced to 3ms. |  |  | 
3 | In step 9.1, RRC connection resume message only include MAC and PHY configuration. No DRX, SPS, CA, or MIMO re-configuration will be triggered by this message. |  |  | 
4 | In step 10, the latency associated to the Transmission of RRC Connection Resume Complete and UP data is assumed to be 0ms |  |  |