## Slide 1: Detail of number of cell
Intel
R2-1808808

## Slide 2: Example: event A4 + N = 3
Time | Events | CellTriggeredList | Option 1 | Option 2 | Option 3 | Option 4 (timer)
T1 | Cell A TTT expires | A |  |  |  | 
T2 | Cell B TTT expires | A, B |  |  |  | 
T3 | Cell A leaves | B |  |  |  | 
T4 | Cell C TTT expires | B, C | MR |  |  | 
T5 | Cell D TTT expires | B, C, D |  | MR | MR | MR (timer starts)
T6 | Cell E TTT expires | B, C, D, E |  |  | MR | 
T7 | Cell F TTT expires | B, C, D, E, F |  |  | MR | 
T8 | Cell B, C, D, E leaves | F |  |  |  | (timer expires)
T9 | Cell G TTT expires | F, G | MR |  |  | 
T10 | Cell H TTT expires | F, G, H |  | MR | MR | MR
Option 1: every N cell TTT expires, UE sends measurement report
Option 2: N cells TTT expires at the same time, the UE sends measurement report
- enter condition: number of cells TTT expires >= N
- exit condition: number of cells TTT expires < N
Option 3: For every added cell, UE sends measurement report when cellTriggeredList > N (current TP)
Option 4: N cells TTT expires at the same time, the UE sends measurement report
- enter condition: number of cells TTT expires >= N
- exit condition: after timer expires

## Slide 3: Number of cell should not apply to first cell
If event A3+N=3 is configured to the UE
  HO performance is proven to be degraded in simulation
If additional event A3 without N is also configured to the UE for HO
  This result A3+N is no use
1 2 3 4
Proposal to NOT CHANGE the GREEN area

## Slide 4: What event to support?
It is now clear that number of cell is not as simple, each supporting event would require UE implementation
We propose only support the event that is useful
Proposal: number of cell supports only A3 and A4