## Slide 1: Summary of discussion on remaining issues on TX profile
Qualcomm Incorporated
R2-1808925

## Slide 2: Issue 1: Basic TX profile
At least the following TX profiles are supported:
  TX profile 1: UE shall use Rel-14 compatible format (use Rel-14 MCS table, not to use Rel-15 feature)
  TX profile 2: UE shall use Rel-15 format (rate matching is used) which is not compatible with Rel-14 (use Rel-15 MCS table)
  Observation 1: the above two provide two “orthogonal” choices to UE so UE will not be ambiguous about what to do with the PDU associated with the TX profile.
  Observation 2: As we agree that RAN1 parameter PSSCH_TXformat is included in the TX profile. Only the above TX profile conforms to the RAN1 meaning of PSCCH_Txformat (0/1): “Indicates if the UE shall use Rel-14 format or the format introduced in Rel-15 “ in RAN1 LS (R1-1805620).
Company-view of the proposal: (majority view)

## Slide 3: Issue 2: Additional TX profiles
RAN1 agrees that (May 24 morning)
  support of 64QAM reception is mandatory for Rel-15 UEs supporting the rate matching.
  support of 64QAM transmission is optional for Rel-15 UEs supporting the rate matching.
Do you support have another TX profile to mandate the UE to use “R15 64QAM ?
  not compatible with R14 UE, but compatible with R15 UE supports rate matching”
Company view?
  Yes (Huawei, need for high data rate service)
  No (majority view)

## Slide 4: Issue 3: TX profile signaling design
If each of the available basic TX profiles are “orthogonal” to each other, shall we have the signaling to support a combinatory “OR” relationship of multiple TX profiles?
  No. This may not need to be supported, or can be out of the scope of RAN2. (upper layer can decide by associate multiple pointers with a PDU).
  Yes, RAN2 can provide a signaling so such a “TX profile X or TX profile Y” pointer which can be used by upper layer to associate with a PDU.
    Some companies have doubts about what is the usage scenario for this “OR” case.
Observation:
  No  Table-based approach(majority view)
  Yes  Bitmap-based approach.

## Slide 5: Summary of Proposals
Proposal 1: At least the following TX profiles are supported:
  TX profile 1: UE shall use Rel-14 compatible format (use Rel-14 MCS table, not to use Rel-15 feature)
  TX profile 2: UE shall use Rel-15 format which is not compatible with Rel-14 (rate matching is used. use Rel-15 MCS table)
Proposal 2: No 64QAM TX profile is needed.
Proposal 3: Table-based approach is used to support the two profiles.