## Slide 1: [V2X CB-704] SidelinkUEInformation Correction

## Slide 2: Observations
The main diff between the two scenarios is: in scenario-1, one can have a PC5-carrier in SIB21-only but not in SIB-26
Scenario-1 and Scenario-2 means one can have a PC5-carrier in SIB26-only but not in SIB-21, which anyway will happen due to the SIB21 size limitation
NOTE:
  The R15-specific configurations (for CA, duplication..) are in SIB26 only!
  The Release-specific carrier issue is only for R15 Ues, since anyway R14 UE can only operate in R14 manner
  The Release-specific carrier issue is only for RRC_IDLE UE, since R14 and R15 configuration can be included in dedicated RRC signaling anyway.
SIB21
SIB26
SIB26
SIB21
Scenario-1
Scenario-2

## Slide 3: SIB-21-only carrier
If TX-pool configuration is provided for the SIB-21-only carrier
  For RRC_IDLE, R14 UE and R15 UE can make use of it, but only using R14 format, i.e., R14-only carrier
  The impact of release-specific carrier is: When a PSID is mapped to carrier A, R15 TX-profile is configured, but the UE would realize that the carrier is R14-only (I.e., either SA2/CT1 to ensure there is no misalignment between NAS/AS configuration, or RAN2 to handle the error case).
If TX-pool configuration is not provided for the SIB-21-only carrier
  For RRC_IDLE UE, R14 and R15 UE cannot use the carrier directly
  But would trigger RRC connection establishment to get configuration for the carrier, i.e., R14 and R15 UE cannot operate in this carrier under RRC_IDLE state

## Slide 4: Solution (4354, HW)
Option 1: Jointly indexing all the carrier frequencies included in SIB21 and SIB26 by the ordinal position of their entries. A value in carrierFreqCommTx/v2x-CommRxInterestedFreqList refers to the carrier frequency that corresponds to the entry with the corresponding index in SIB21 or SIB26.
Option 2: Jointly indexing the carrier frequencies included in SIB21 and the carrier frequencies which are not included in SIB21 but only in SIB26, by the ordinal position of their entries. A value in carrierFreqCommTx/v2x-CommRxInterestedFreqList refers to the carrier frequency that corresponds to the entry with the corresponding index in SIB21 or SIB26.
Option 3: Place a restriction for the eNB configuration that SIB26 must include all the carrier frequencies in SIB21. A value in carrierFreqCommTx/v2x-CommRxInterestedFreqList needs only to indicate the carrier frequency by indicating the corresponding entry SIB26

## Slide 5: Discussion
Q1: Do u think scenario-1 is valid?
  [HW, E///, Idt, ITL] SIB21-only carrier should not be configured together with TX pool [QC] no need for scenario-1? [HW] NW would like to have the flex to have sce-1 to put all Ues into connected mode [Intel] supports HW
Q2: Which solution to choose?
  [HW] option-1/2 allows sce-1, but option-3 does not.

## Slide 6: Proposal
RAN2 to further down-select between the two alternatives
  Alt-A: to allow SIB-21 only carrier, but only allows that for the case that no TX pool configured in SIB-21 for these carriers, i.e., Option-1 or Option-2 of HW proposal is used
  Alt-B: not to allow SIB-21 only carrier, i.e., Option-3 of HW proposal is used