## Slide 1: Report of Offline #702: Explicit PC5 RRC Connection Establishment
LG Electronics Inc. (Rapporteur)
3GPP TSG-RAN WG2 Meeting #105bis
Xi’an, China, 8-12 April 2019
R2-1905327

## Slide 2: Challenging issues for PC5-RRC message exchange
PC5-RRC connection is needed to establish SL UE context
  Synchronization of SL UE context between two UEs is supported by the concept of PC5-RRC connection
    Need for PC5-RRC state is FFS.
      Option 1: Define PC5-RRC state for unicast operation
      Option 2: Refer to PC5-S state for unicast operation
    SL UE context may include at least SL UE capability of the destination UE.
      FFS whether AS configuration information can be also stored in SL UE context.
    UE context is per destination UE
      It is considered that UE may store UE capability of the destination UE for a newly coming service between UEs in unicast.
      It may depend on SA2 discussion related to layer-2 ID allocation. RAN2 will come back if there is a problem based on SA2 progress.
    FFS whether explicit PC5-RRC connection establishment procedure is needed or not.
Security aspect may not be a key issue for selecting the identified options.
  We can come back after SA3 progress.