## Slide 1: UL-TX-Switch Capabilities – Alternative to parallel list of BCs
Source: Ericsson
Agenda item: 6.15
3GPP TSG-RAN WG2 Meeting #111 electronic R2-2008415
Online, August 17th - 28th, 2020

## Slide 2: Problems with current solution (separate BC-list for UL-TX-Switch)
Undefined relation to other fields: In the current specification the supported UL-TX-Switch patterns (1+0/0+1 or 1+1/2+0/0+2) seem to be determined only by the "uplinkTxSwitching-OptionSupport-r16".
  How is the UE meant to set e.g. "UL BW classes" in BC and "MIMO layers" in FSUpCC? And how does the NW interpret those field in the context of UL-TX-Switching? Does the NW ignore the latter?
  Unclear whether all other parameters in the BC/FSD/FSU/FSUpCC (SRS, CSI, ...) apply for the 1+1 and/or 0+2/2+0 case. Current structure does not allow distinguishing those, i.e., UE cannot support e.g. more SRS ports for 2+0 than for 1+1.
Not extensible to e.g. 2+2/4+0/0+4. Would one introduce yet another list of BCs for that?
Unclear what "uplinkTxSwitching-OptionSupport-r16" = "Both" means. A UE supporting "DualUL" (1+1/2+0/0+2) should always support SwitchedUL (1+0/0+1).
Procedural text to fill the new BC is ambiguous: All BCs (including those for UL-TX-Switch) are added to the legacy BC list and duplicates to the new list.
Need to maintain two structures in specs and products. Likely to forget extensions of the UL-TX-Switch list (as it happened repeatedly for the capability filters prior to structural change).
Significant overhead since ...
  UE must include BCs in new list and in the legacy list, even though BC content is usually the same.
  Each BC contains a list of pairs of BandParameters and associated parameters. Likely, a UE supporting UL-TX-Switching will support the same "pattern" across several similar BC.

## Slide 3: Proposed Alternative: New FSC in existing BandCombination structure
Summary of proposal
Introduce additional FeatureSetCombination ID in the legacy BandCombination structure (as proposed by Huawei for DAPS)
Add parameters to FeatureSetUplink indicating whether the carriers configured according to this FSU share TX-chains (ports) with other carriers.
  Add here also the other UL-TX-Switch parameters (interruption delay, impacted carriers)
Add a field in the BC to indicate how many shared TX-chains the UE has when operating according to this BC.
Advantages
No need to maintain two BC lists
No need to duplicate BCs, i.e., legacy gNB and new gNB use same BCs. New gNB determines based on new FSC whether UE supports UL-TX-Switching
Avoid large "BandParameter pairs" in each BC.
Re-Use UL-TX-Switch capabilities by established Feature-Set concept.
Setting and interpretation of legacy fields (e.g. Max-MIMO layers) remains unchanged for legacy and new UEs and gNBs.
No issues with "implicit fallback" BCs. No risk to omit BC that legacy gNB's require
Extensible for more UL MIMO layers.

## Slide 4: ASN.1 changes Compared to 16.1.0
BandCombination:
    BandCombination-v16xy ::= SEQUENCE {
    uplinkTx-Switch SEQUENCE {
    featureSetCombination-ULTXSwitch FeatureSetCombinationId,
    nrofSharedTxChains INTEGER(1..8)
    } OPTIONAL
    }
BandCombination-v16xy field descriptions
nrofSharedTxChains The total number of TX chains shared across the uplink serving cells configured according to a FeatureSetUplink with uplinkTx-Switch present.
uplinkTx-Switch If present, the UE supports UL-TX-Switching in this BandCombination, i.e., it can share one or more TX chains among several UL carriers.

## Slide 5: ASN.1 changes Compared to 16.1.0
FeatureSetUplink:
  FeatureSetUplink-v16xy ::= SEQUENCE {
  uplinkTX-Switch SEQUENCE {
  switchingPeriod-r16 ENUMERATED {us35, us140, us210},
  switching-DL-Interruption-r16 BIT STRING (SIZE(1..maxSimultaneousBands)) OPTIONAL
  } OPTIONAL
  }
FeatureSetUplink-v16xy field descriptions
switching-DL-Interruption If present, each bit in the bitmap indicates whether the downlink serving cells configured in accordance with the associated FeatureSetPerBand experience an interruption during the UL-TX-Switching operation. The first/left-most bit in the bitmap corresponds to the first FeatureSetPerBand in the FeatureSetCombination, and so on.
switchingPeriod indicates the length of UL Tx switching period when dynamic UL Tx switching is configured, as specified in TS 38.101-1 [15] and TS 38.101-3 [34]. UE shall not report the value us210 for EN-DC band combinations. us35 represents 35 us, us140 represents 140 us, and so on, as specified in TS 38.101-1 [15] and TS 38.101-3 [34].
uplinkTX-Switch The UE may only include this field if this FeatureSetUplink is referred to from featureSetCombination-ULTXSwitch. If this field is present, it indicates that the UE supports a serving cell configured according to this FeatureSetUplink shares its TX chain(s) (as indicated by nrofSharedTxChains in BandCombination-v16xy) with other serving cells configured according to other FeatureSetUplinks in the same FeatureSetEntry in which this field also is present.

## Slide 6: Example: "Option 2" UE Supporting 1+1, 2+0 and 0+2
BandCombination
featureSetCombination = 11
uplinkTx-Switch
featureSetCombination-ULTXSwitch = 42,
nrofSharedTxChains = 2
FeatureSetCombination #42
FeatureSetCombination #11
BandParameter#1
bandNR = 1
ca-BandwidthClassDL-NR = A
ca-BandwidthClassUL-NR = A
BandParameter#2
bandNR = 3
ca-BandwidthClassDL-NR = A
ca-BandwidthClassUL-NR = A
FeatureSetDownlink
...
FeatureSetUplink
uplinkTX-Switch
switchingPeriod-r16 = n140us,
switching-DL-Interruption-r16 ...
FeatureSetUplinkPerCC
maxMIMO-Layers = 2
FeatureSetDownlink
...
FeatureSetUplink
uplinkTX-Switch
switchingPeriod-r16 = n140us,
switching-DL-Interruption-r16 ...
FeatureSetUplinkPerCC
maxMIMO-Layers = 2
FeatureSetDownlink
...
FeatureSetUplink
FeatureSetUplinkPerCC
maxMIMO-Layers = 1
FeatureSetPerBand
FeatureSetPerBand
From BandCombination + FeatureSetCombination#11 the legacy gNB comprehends that the UE supports
1 UL layer on each carrier, or
2 UL layers on band 1, or
2 UL layers on band 3...
by RRC reconfiguration
(signaled by 3 Feature-Set-Entries in the legacy FSC)
From the same BandCombination and the (new) FeatureSetCombination#42 the new gNB comprehends that the UE supports UL TX switching and that it may hence use either... 1 UL layer on each carrier, or
2 UL layers on the carrier in band 1 or 2 UL layers on the carrier in band 3...
by DCI switching.
FeatureSetDownlink
...
FeatureSetUplink
FeatureSetUplinkPerCC
maxMIMO-Layers = 2
FeatureSetDownlink
...
FeatureSetUplink
FeatureSetUplinkPerCC
maxMIMO-Layers = 0
FeatureSetDownlink
...
FeatureSetUplink
FeatureSetUplinkPerCC
maxMIMO-Layers = 1
FeatureSetDownlink
...
FeatureSetUplink
FeatureSetUplinkPerCC
maxMIMO-Layers = 0
FeatureSetDownlink
...
FeatureSetUplink
FeatureSetUplinkPerCC
maxMIMO-Layers = 2
blue text: new fields in ASN.1
orange text: existing fields that are important for the new functionality.
Feature
Set
Entry
Feature
Set
Entry
Feature
Set
Entry

## Slide 7: Example: "Option 1" UE Supporting 1+0 and 0+1
BandCombination
featureSetCombination = 11
uplinkTx-Switch
featureSetCombination-ULTXSwitch = 42,
nrofSharedTxChains = 1
FeatureSetCombination #42
FeatureSetCombination #11
BandParameter#1
bandNR = 1
ca-BandwidthClassDL-NR = A
ca-BandwidthClassUL-NR = A
BandParameter#2
bandNR = 3
ca-BandwidthClassDL-NR = A
ca-BandwidthClassUL-NR = A
FeatureSetDownlink
...
FeatureSetUplink
uplinkTX-Switch
switchingPeriod-r16 = n140us,
switching-DL-Interruption-r16 ...
FeatureSetUplinkPerCC
maxMIMO-Layers = 1
FeatureSetDownlink
...
FeatureSetUplink
uplinkTX-Switch
switchingPeriod-r16 = n140us,
switching-DL-Interruption-r16 ...
FeatureSetUplinkPerCC
maxMIMO-Layers = 1
FeatureSetDownlink
...
FeatureSetUplink
FeatureSetUplinkPerCC
maxMIMO-Layers = 1
FeatureSetPerBand
FeatureSetPerBand
From BandCombination + FeatureSetCombination#11 the legacy gNB comprehends that the UE supports either
1 UL layer on band 1, or
1 UL layer on band 3...
by RRC reconfiguration
From the same BandCombination + FeatureSetCombination#42 the new gNB comprehends that the UE supports UL TX switching and that it may hence use
1 UL layer on band 1, or
1 UL layer on band 3...
by DCI switching
FeatureSetDownlink
...
FeatureSetUplink
FeatureSetUplinkPerCC
maxMIMO-Layers = 0
FeatureSetDownlink
...
FeatureSetUplink
FeatureSetUplinkPerCC
maxMIMO-Layers = 0
FeatureSetDownlink
...
FeatureSetUplink
FeatureSetUplinkPerCC
maxMIMO-Layers = 1
Feature
Set
Entry
Feature
Set
Entry
blue text: new fields in ASN.1
orange text: existing fields that are important for the new functionality.
Feature
Set
Entry

## Slide 8: Conclusion
Proposal 1: Abandon the existing design with the parallel BandCombination list (BandCombinationList-UplinkTxSwitch-r16).
Proposal 2: Extend the legacy BandCombination list and FeatureSets according to the changes described in this contribution.
The full text proposal to 38.331 can be found as a separate file attached.