## Slide 1: Design Targets for Ambient IoT
T-Mobile USA
R2-2403561
RAN2#125-bis Changsha, China April 2024
Agenda Item 8.2

## Slide 2: General Aspects
Both RAN and SA completed study items in TR 22.840 and TR 38.848
This presentation highlights the design targets that are most important to T-Mobile USA
R19 should focus on indoor inventory and indoor command use cases
Security must be a key design consideration from day 1

## Slide 3: Important design considerations from TR 22.840 – For Approval
Reference | Requirement from TR 22.840
CPR 7.1.1-2 | The 5G system shall be able to support 5G network or an Ambient IoT capable UE to communicate with a group of Ambient IoT devices simultaneously.
CPR 7.1.1-3 | The 5G network shall support a mechanism to authorize an Ambient IoT capable UE to communicate with an Ambient IoT device.
CPR 7.1.2-1 | The 5G system shall support location services for Ambient IoT devices (e.g., to locate Ambient IoT devices using absolute or relative positioning methods) Note: The intention is not to use Ambient IoT devices to locate other Ambient IoT devices.
CPR 7.1.3-2 | The 5G system shall support a mechanism to: - disable the capability to transmit RF signals for one or more Ambient IoT device that is / are currently able to transmit RF signals - enable the capability to transmit RF signals for one or more Ambient IoT device that is / are currently disabled to transmit RF signals
CPR 7.1.3-3 | Based on operator policy, the 5G system shall provide a suitable mechanism to permanently disable the capability of an Ambient IoT device or a group of Ambient IoT devices to transmit RF signals.
CPR. 7.1.5-1 | The 5G system shall be able to collect charging information in a suitable way for using Ambient IoT services on per Ambient IoT device basis or a group of Ambient IoT devices (e.g., total number of communications per charging period).
CPR 7.1.6-1 | The 5G system shall be able to provide a mechanism to protect the privacy of information (e.g., location and identity) exchanged during communication between an Ambient IoT device and the 5G network or an Ambient IoT capable UE.
CPR 7.1.6-2 | The 5G system shall enable security protection suitable for Ambient IoT, without compromising overall 5G security protection.
CPR 7.1.6-3 | Based on subscription and operator policies, the 5G system shall authorize an Ambient IoT capable UE to communicate with a specific Ambient IoT device.

## Slide 4: KPI’s of Indoor Inventory and Indoor Command from TR 22.848
Use Case Category | Use Cases | Maximum End-to-End Latency | Comm. Service Availability | User-Experienced Data Rate | Message Size | Device density | Communication Range (Note 1) | Service area dimension | Device speed | Transfer interval | Positioning Accuracy
Indoor Inventory | Automated Warehousing | 1s | 99% | < 128 bit/s | 96 bits or 128 bits | 1 – 2 per | 30 m | NA | 5 – 10 km/hr | NA | 2 -3 m (3D positioning)
 | Medical Instruments Inventory Management and Positioning | Several seconds | 99% | < 2 kb/s | 176 bits | 1000 per | 50 m | NA | < 6 km/hr | NA | 3 – 5 m
 | Ambient IoT in Non-Public Network for Logistics | 1s | 99% | < 128 bit/s | 96 bits or 128 bits | 1 – 2 per | 50 m | NA | 5 – 10 km/hr | NA | 3 -5 m
 | Automobile Manufacturing | 10 s | 99% | < 1 kb/s | 96 bits | < 1.5 millions per | 30 m | 600,000 | Up to 5 km/hr | NA | 3 m
 | Real time Inventory Management on Airport Terminals and Shipping Port | 1 – 10 s | 99% | 2.6 kb/s | 256 bits | 100 devices per | 50 m | 1 – 10 | 3 – 10 km/hr | NA | Cell level
 | Automated Supply Chain Distribution | 10 s | 99% | < 100 bits/s | < 100 bytes | < 1.5 millions per | 30 m | 600,000 | NA | NA | 3 m
 | Fresh Food Supply Chain | 1 min | NA | < 0.12 bits/s | 100 bits | < 1.5 millions per | 50 m | 30,000 | 1 m / s | 15 min | NA
 | Electronic Shelf Label | 1 s | 99% | 0.8 kb/s | 100 bytes | < 1.5 millions per | 50 m | 15,900 | stationary | 20 min – 2 hrs | NA
Indoor Command | Online modification of medical instruments status | Several seconds | 99% | < 2 kb/s | 176 bits | 1000 per | 50 m | NA | Stationary or 6 km/hr | NA | 3 - 5 m
 | Device activation and deactivation in greenhouse | 1 s | 99.9% | < 1 kb/s | < 1000 bits | 1 per | 30 m | NA | Stationary | NA | NA
 | Elderly heath care (send alerts and request feedback) | 1s | NA | < 1 kb/s | < 100 bits | < 20 per 100 | 20 m | < 250 | Stationary | NA | NA
 | Electronic Shelf Label (send alert signal and get feedback) | 1s | 99% | 0.8 kb/s | 100 bytes | 1000 per | 50 m | NA | Stationary or 6 km/hr | NA | NA
NOTE 1: The communication range is the communication distance between the ambient IoT device and the 5G network or between the ambient IoT device and an ambient IoT capable UE. |  |  |  |  |  |  |  |  |  |  | 
Use Case Category | Use Cases | Maximum End-to-End Latency | Comm. Service Availability | User-Experienced Data Rate | Message Size | Device density | Communication Range (Note 1) | Service area dimension | Device speed | Transfer interval | Positioning Accuracy
Indoor Inventory | Automated Warehousing | 1s | 99% | < 128 bit/s | 96 bits or 128 bits |  | 30 m | NA | 5 – 10 km/hr | NA | 2 -3 m (3D positioning)
 | Medical Instruments Inventory Management and Positioning | Several seconds | 99% | < 2 kb/s | 176 bits |  | 50 m | NA | < 6 km/hr | NA | 3 – 5 m
 | Ambient IoT in Non-Public Network for Logistics | 1s | 99% | < 128 bit/s | 96 bits or 128 bits |  | 50 m | NA | 5 – 10 km/hr | NA | 3 -5 m
 | Automobile Manufacturing | 10 s | 99% | < 1 kb/s | 96 bits |  | 30 m |  | Up to 5 km/hr | NA | 3 m
 | Real time Inventory Management on Airport Terminals and Shipping Port | 1 – 10 s | 99% | 2.6 kb/s | 256 bits |  | 50 m |  | 3 – 10 km/hr | NA | Cell level
 | Automated Supply Chain Distribution | 10 s | 99% | < 100 bits/s | < 100 bytes |  | 30 m |  | NA | NA | 3 m
 | Fresh Food Supply Chain | 1 min | NA | < 0.12 bits/s | 100 bits |  | 50 m |  | 1 m / s | 15 min | NA
 | Electronic Shelf Label | 1 s | 99% | 0.8 kb/s | 100 bytes |  | 50 m |  | stationary | 20 min – 2 hrs | NA
Indoor Command | Online modification of medical instruments status | Several seconds | 99% | < 2 kb/s | 176 bits |  | 50 m | NA | Stationary or 6 km/hr | NA | 3 - 5 m
 | Device activation and deactivation in greenhouse | 1 s | 99.9% | < 1 kb/s | < 1000 bits |  | 30 m | NA | Stationary | NA | NA
 | Elderly heath care (send alerts and request feedback) | 1s | NA | < 1 kb/s | < 100 bits |  | 20 m |  | Stationary | NA | NA
 | Electronic Shelf Label (send alert signal and get feedback) | 1s | 99% | 0.8 kb/s | 100 bytes |  | 50 m | NA | Stationary or 6 km/hr | NA | NA
NOTE 1: The communication range is the communication distance between the ambient IoT device and the 5G network or between the ambient IoT device and an ambient IoT capable UE. |  |  |  |  |  |  |  |  |  |  | 

## Slide 5: T-Mobile’s proposed KPI’s for Ambient IoT – For Approval
Use Case Category | RAN Latency | User-Experienced Data Rate | Message Size | Device density | Communication Range (Note 1) | Device speed | Positioning Accuracy
~1 µW Ambient IoT Device | 1s | 1 kbps | 128 bits | 1 - 2 per | 20 m | Up to 6 km/hr | 3 – 5 m
100’s µW Ambient IoT Device | 1s | Up to 2 kb/s | < 1000 bits | 1 -2 per | 50 m | Up to 6 km/hr | 3 - 5 m
NOTE 1: The communication range is the communication distance between the ambient IoT device and the 5G network or between the ambient IoT device and an ambient IoT capable UE. |  |  |  |  |  |  | 
Use Case Category | RAN Latency | User-Experienced Data Rate | Message Size | Device density | Communication Range (Note 1) | Device speed | Positioning Accuracy
~1 µW Ambient IoT Device | 1s | 1 kbps | 128 bits |  | 20 m | Up to 6 km/hr | 3 – 5 m
100’s µW Ambient IoT Device | 1s | Up to 2 kb/s | < 1000 bits |  | 50 m | Up to 6 km/hr | 3 - 5 m
NOTE 1: The communication range is the communication distance between the ambient IoT device and the 5G network or between the ambient IoT device and an ambient IoT capable UE. |  |  |  |  |  |  | 

## Slide 6: Proposals for Approval
1) Approve KPI’s on page 5 and add to TR 38.769 section 4.1
2) Approve design considerations on slide 3 and add to TR 38.769 section 4.1
3) Approve LS to SA3 requesting security requirements
  See draft LS in R2-2403563