## Slide 1
Further investigations on cell barring due to reception failure of MIB or SIB1 Source: Cassidian
Agenda Item: 6.2.1.1
3GPP TSG-RAN WG2 #86 R2-142393
Seoul, South Korea, 19 – 23 May 2014

## Slide 2: Background & Objectives
  Background
    Loss of service due to the cell considered as barred for 5 min by UE was presented in [1] and was discussed at RAN2#85 meeting
      Issue was found in “real life” situation (drive test) with Airbus DS LTE UE
      Single 3-sector LTE eNodeB
    The topic was further discussed in RAN2#85bis meeting in [2] and in offline discussions
    It was clarified that the barring of the cell shall only occurred when both conditions are met:
      The cell can be detected (e.g. by acquisition of PSS & SSS)
      The MIB/SIB1 cannot be acquired
  Objectives of this contribution
    Present results of lab tests aiming at:
      Checking Airbus D&S UE complies with the expected behaviour described above in lab
      Checking and comparing with a commercially available Band 20 UE
      Assess how probable the two above conditions are met at the same time
        On Commercial networks
        On Public Safety networks
    Conclusion and recommendations

## Slide 3: Test set-up: General description
Phone
Server
Diff
15:53:02
15:53:00
2s
LTE
eNodeB
(Band 20)
Fixed attenuator
30
dB
x10dB
x1dB
Phone
Server
Diff
15:53:02
15:53:00
2s
Commercial LTE UE supporting Frequency Band 20
Remote display of the screen of the smartphone captured by the webcam inside the Faraday shield.
webcam
variable attenuator
Antenna
Faraday shield

## Slide 4: Test set-up – General overview
Commercial LTE UE supporting Frequency Band 20
External PC connected to the webcam displaying the screen of the smartphone
eNodeB feeder going through the variable attenuator

## Slide 5: Test set-up – Band 20 LTE UE & Webcam in the Faraday Shield
Commercial LTE UE supporting Frequency Band 20
Webcam
eNodeB antenna

## Slide 6: Test set-up – Band 20 LTE UE & Webcam in the Faraday Shield
Commercial LTE UE supporting Frequency Band 20
Webcam
LTE 10MHz Band 20 eNodeB feeder
eNodeB antenna
Webcam USB connection to external PC

## Slide 7: Test Setup
The UE runs Internet browser displaying an HTML page running two JavaScript functions called every seconds:
Displays the local UE clock
Sends an Ajax query that retrieves the server clock. This operation needs a running LTE connection to be successful
The difference between the two clocks is displayed:
it is fixed when the connection is up
It increases when the LTE connection to the server is lost. If disconnection is larger than 4s, the duration is displayed on the third line.
Phone Clock | Server Clock | Time difference
18:35:42 | 18:35:02 | 40s
Phone Clock | Server Clock | Time difference
18:35:52 | 18:35:02 | 50s
Connection loss: 10s |  | 
LTE connection is running
LTE connection is lost

## Slide 8: Test Results with LTE Band 20 commercial UE
10dB
RRC connected
RRC connected
Variable attenuator
~20s
~329s
QCI 7
≥20dB
RRC connected
RRC connected
Variable attenuator
~20s
~35s
QCI 7
The cell can be detected but acquisition of MIB/SIB1 failed => the cell is barred for 300s
The cell cannot be detected => the cell is not barred

## Slide 9: Test Results
  Tests were performed with two LTE UEs
    Commercial Band 20 UE (as shown on the previous slides)
    Aribus DS LTE UE (used during drive tests described in [1])
  Same behavior was observed on both UEs
    Cell is considered as barred when the power of the received downlink signals is in a range where:
      The cell can be detected
      The MIB/SIB1 cannot be acquired
    The cell is not considered as barred when the power of the received downlink signal is low enough so that the cell is not detected anymore
  The above observed behaviors during tests are compliant with 3GPP RAN2 specifications
  The power range of the received signals where the cell is considered as barred as been assessed to 4~5dB
    Tests described in the previous slides where repeated for different attenuation steps

## Slide 10: Impact on service
  The power range of 4~5dB where the cell can be detected but the MIB/SIB1 cannot be read creates some areas at the border of the cells where there is an increased risk of 5 minutes LTE service unavailability
  This risk exists for any type of LTE network
    Commercial network
    Public Safety network
  The risk is particularly high at the coverage edge, where there is no neighbour LTE cells to re-select. Examples of situation where the cell can be barred for users close the edge:
    Returning into cell coverage after reaching the cell edge
    Shadowing inside the cell
    Any fast decrease of propagation(in/out car, building…)
  The risk can be reduced at in inter-cell border if the engineering of the network ensures sufficient overlap between neighbouring cells
1
2
3

## Slide 11: Benefits of controlling the cell barring duration for a commercial LTE network
For a commercial network, there are some fall-back mechanisms that makes the issue less visible:
  High cell density with sufficient coverage overlap
  Inter-frequency handover (if multiple frequency bands are supported)
  Inter-RAT handover (if 2G/3G coverage is available)
However, it leads to sub-optimal network configuration:
  Unexpected load of the 2G/3G cells
  Service unavailability in case there is no cell to reselect
  Unexpected load of umbrella cell in hotspot scenario (cf. figure on the right side)
Reducing the cell barring duration for the cells at the edge of the coverage would prevent sub-optimal network configuration in commercial networks
Umbrella cell
Hotspot
UE leaves the hotspot coverage and the small cell is considered as barred
Although the UE is back in hotspot coverage, it is unable to re-connect to the small cell and remains connected for 5 minutes to the umbrella cell.

## Slide 12: Benefits of controlling the cell barring duration for a Public Safety LTE network
For a public safety network that is deployed after a major disaster (e.g. hurricane Katerina), the fall-back mechanisms that exists for commercial networks are not available:
  Accurate cell planning to control the cell overlaps cannot be done in an emergency situation where the eNodeB possible locations are limited
  Any types of handover (inter-frequency, inter-RAT…) are not possible since the deployable network is the only one available for the first hours/days.
  Thus, in such scenario,
  There is a significant risk of having a cell barred for 5 minutes
  In emergency situations, this risk is obviously not acceptable
Reducing the cell barring duration and the associated risk of 5 minutes communication unavailability is mandatory for Public Safety usage

## Slide 13: Conclusion
In this contribution, lab test setup and results were presented. They have confirmed that the issue of the 5-minute communication unavailability found during drive tests and described in [1] is not due to the implementation of the Airbus DS UE used during the drive tests:
    Band 20 commercial UE has similar behaviour
    The observed behaviour is aligned with RAN2 opinion
There is a non negligible probability to experience a 5-minute communication unavailability:
    This was found in « live » network during drive-tests
    It was confirmed in lab that the range of the received signal where barring of the cell occurs is 4~5dB (for the two type of UEs which were tested. Values are likely to be implementation dependant)
For Public Safety networks, such risk of communication loss is a significant issue, especially in situation where a fast deployable network shall be used (cf. slide 12)
For commercial networks, adjusting the duration of the cell barring mechanism may have some benefits on overall network capacity (cf. slide 11) e.g. by reducing 2G/3G networks load, and avoiding unexpected overloading/saturation networks
Thus, it is recommended that a standard solution is studied and introduced in future release to reduce the risk of communication unavailability.
A solution was proposed in [1]
    Introduction in the Rel-yy extension an optional Tbarred parameter with 300s as default value

## Slide 14: References
[1] R2-140399, Impact of public safety use case on the cell baring mechanism, EADS
[2] R2-141138, Cell barring due to reception failure of MIB or SIB1, Samsung