## Slide 1: WF on SI update for eDRX
Qualcomm, Ericsson, Sierra Wireless, Gemalto, NTT DOCOMO, Mediatek, Softbank, Interdigital
3GPP TSG RAN WG2 Meeting #92 R2-156930
Anaheim, USA, 16 - 20 November 2015

## Slide 2: Proposal:
If eDRX cycle <= BCCH modification period, SI change notification follows the legacy procedure
If eDRX cycle > BCCH modification period
  UE acquires the systemInfoValueTag just before RRC Connection
  In addition, paging notification of SI update is supported
    Justification: provide notification of upcoming critical (though rare) SI change that impacts UE reachability, such as changes to Pcch-Config or cell barring
  Paging notification mechanism
    A new indication systemInfoModification-eDRX is defined in Paging message
    When receiving the indication, eDRX UE acquires the new SI at the radio frame boundaries defined by
      H-SFN mod m_eDRX = 0, where m_eDRX is configured by System Information
Notes: Notes: RAN2 has already agreed in principle to support paging notification for LC/EC UEs
Paging notification will only be needed in the rare cases, but is needed to ensure that eDRX UEs do not suddenly become unreachable when a critical change happens.