## Slide 1: RAN1-RAN2 sync on Scheduling and HARQ design for NB-IoT
Ericsson
R2-161941
TSG-RAN WG2 meeting #93
15-19 February 2016, St. Julian’s, Malta

## Slide 2: RAN2 Scheduling related agreements from RAN1
RAN1#NB-IoT-adhoc
  NB-PDCCH and NB-PDSCH are multiplexed only based on TDM at subframe level at least per UE
    It means that only cross subframe scheduling is supported
RAN1#84
  DL and UL scheduling delays are indicated in DCI
    number of delay values that can be signalled for the UL scheduling delay is less than the number of values for the DL

## Slide 3: Scheduling assumptions RAN2
Proposal 1: Scheduling information for both downlink and uplink data is transmitted on a downlink physical control channel denoted NB-PDCCH. The scheduled uplink and downlink data is transmitted on shared data channels denoted NB-PUSCH and NB-PDSCH respectively.
  This is common understanding in RAN1 and hard to find any explicit agreements on exactly this aspect.
Proposal 2: NB-IoT supports only cross-subframe scheduling and no same-subframe scheduling.
  1-a-i
Proposal 3: The transmission duration in number of sub-frames for the NB-PDCCH, the NB-PDSCH and the NB-PUSCH is variable.
  There is no explicit agreement of this but it is a result of supporting transport block sizes that are larger than what can be fit in one subframe (1 ms) and the support of enhanced coverage (MCL up to 164 dB).
Proposal 4: The transmission duration in number of sub-frames is semi-static for the NB-PDCCH and is indicated for the NB-PDSCH/NB-PUSCH as part of the scheduling information transmitted on the NB-PDCCH.
  First part is FFS, second part is the result of what MCS/TBS that is indicated in the DCI transmitted on NB-PDCCH
Proposal 5: The start time of the NB-PDSCH/NB-PUSCH relative to the NB-PDCCH is signaled as part of the scheduling message.
  2-a

## Slide 4: RAN2 HARQ related agreements from RAN1
RAN1#NB-IoT-adhoc
  Transmission of ACK and/or NACK corresponding to NB-PDSCH is supported
  For PDSCH:
    Single process HARQ for PDSCH is realized by adaptive and asynchronous timing transmission
RAN1#84
  Adaptive HARQ is supported for uplink.
    The HARQ re-transmissions in the uplink are asynchronous.
    PHICH is not supported for NB-PUSCH

## Slide 5: HARQ assumptions in RAN2
Proposal 6: HARQ feedback information for downlink data is sent on NB-PUSCH. HARQ feedback information for uplink data is sent on NB-PDCCH.
  HARQ feedback for DL is sent on NB-PUSCH: 1-a only provides information that HARQ feedback is transmitted but not on what channel.
  HARQ feedback for UL on NB-PDCCH is a consequence of 2-a-i/ii.
Proposal 7: Adaptive HARQ is supported for downlink and uplink.
  Downlink: 1-b
  Uplink: 2-a-i/ii
Proposal 9: UL HARQ re-transmissions should not be triggered by absence of HARQ feedback on the NB-PDCCH.
  RAN2 assumes this is to be a consequence of 2-a-i/ii
Proposal 10: The HARQ re-transmissions in both downlink and uplink are asynchronous.
  Downlink: 1-b-i
  Uplink: 2-a-i/ii