## Slide 1: Way forward on SI scheduling in NB-IoT
Huawei, Hisilicon, Neul Ltd., Intel, Ericsson?
3GPP TSG-RAN WG2 Meeting #93BIS R2- 163052
Dubrovnik, Croatia, 11 - 15 April, 2016

## Slide 2: Background
In LS from RAN1 [R2-162135],
RAN1 also agreed that NB-PDSCH transmission over 8 subframes supports transport block sizes of 208, 256, 328, 440, 552, and 680 bits. RAN1 invites RAN2 to select appropriate values from this set for TBS1, TBS2, TBS3, and TBS4.
SI scheduling information is provided in NB-SIB1.
One transport block of an SI message is transmitted over 8 consecutive valid DL subframes.
SI scheduling information is given by –
  TBS (2 bits)
    Values to be decided by RAN2, possible values are {208, 256, 328, 440, 552, 680}
  Repetition pattern
    Number(s) of repetitions (set of values up to RAN2)
    Time interval(s) between repetitions (set of values up to RAN2)
Note that which is the first subframe for the repetition pattern relative to the start of the SI window is up to RAN2 to define.

## Slide 3: Background
During online discussion:
  The value range of si-Periodicity for NB-IoT should be extended due to reduced bandwidth by considering the extension of SI-window value range.
  We use the range ENUMERATED {rf64 (FFS), rf128 (FFS), rf256, rf512, rf1024, rf2048, rf4096}.
  the maximum range of BCCH modification period can be set up to FFS s, and the coefficient parameter range is set accordingly (offline).

## Slide 4: Proposal
The value range of si-WindowLength for NB-IoT should be can be
Option 1: ENUMERATED {ms80, ms160, ms240, ms320, ms400, ms560, spare}.
Option 2: ENUMERATED {ms160, ms320, ms640, ms960, ms1280, ms1600, spare}.
The value range of si-Periodicity for NB-IoT can be ENUMERATED {rf256, rf512, rf1024, rf2048, rf4096, rf8192, rf16384}.
The maximum value range of BCCH modification period can be set up to 1310.72.