## Slide 1: Discussion on Light Connection identified FFS
Intel Corporation, Huawei, HiSilicon
3GPP TSG-RAN WG2 Meeting #95bis R2-167304
Kaohsiung, 10 - 14 October 2016

## Slide 2: Points for discussion
The following comeback “CBF: Decide whether to continue the email discussion about the left issues” was agreed in Light Conn. session.
This document summarizes the proposals related to the recommendations 4-5 of the email discussion report on [95#31] (R2-166688), and FFS captured on RAN2#94 meeting” :
Recommendation 4 To confirm the fact that legacy CN TA (as well as, CN TAU procedure) is already available and could be used by default for RAN-based Paging Area (up to network implementation).
Recommendation 5 To discuss and agree on point a) and/or point b).
  Recommendation 5.a. Point a) A RAN-based Paging Area identifier is defined to be indicated to each UE via dedicated signaling and to be broadcasted by the eNB (which would indicate the RAN-based Paging Area that it belongs to).
  Recommendation 5.b. Point b) A global cell identity list is provided by the eNB to each UE via dedicated signalling (the global cell identity list implicitly indicates the cells belonging to the RAN-based Paging Area).
FFS: To define RAN-based paging DRX cycle which is UE specific

## Slide 3: Proposals for agreement
Proposal 1.- RAN2 confirms legacy behaviour that UE always perform TAU when changing TA boarders (which is also applicable for a UE lightly connected).
Take as baseline, Proposal 2.- The eNB could optionally signal a global cell identity list to the UE via RRC dedicated signaling to indicate the RAN-based Paging Area. Detail FFS; the design should aim minimizing signaling and configuration overhead (e.g. cellIdentity could be used instead of global cell id).
FFS - Proposal 3.- The eNB could optionally signal a new defined RAN-based Paging Area identifier via dedicated signaling (to configure the UE with the RAN-based Paging Area to be used) and via broadcasted (for the eNB to indicate the RAN-based Paging Area that it belongs to).
Proposal 4.- A UE in lightly connected can be configured by eNB via dedicated RRC signaling with a specific DRX cycle (which is used during the RAN-initiated paging PO/PF calculation), including at least the values 320, 640, 1280 and, 2560ms, FFS if other values are also defined.