## Slide 1: Discussion on Light Connection identified FFS
Intel Corporation, Huawei, HiSilicon
3GPP TSG-RAN WG2 Meeting #96 R2-168957
Reno, USA 14th – 18th November 2016

## Slide 2: FFS for email discussion (1/2)
The list of FFS to be handled in the agreed RAN2#96 email discussion for light connection (based on the captured and not addressed FFS on RAN2#96 agreements, email discussion [95bis#20], or on running CR to 36.300) are the following
The UE ID conveyed in paging message is FFS between (If RAN2 does not agree on the comeback associated to the [offline#104]) :
  (a) S-TMSI (i.e. the same UE identity as in legacy CN based paging controlled by the MME).
  (b) a RAN indentity allocated by the "anchor eNB", such as, Rel-13 UE Resume ID.
The configured RAN paging area will be one of the following options: a list of cells, a single cell, the same as CN Tracking Area. FFS: paging area which can be indicated by ID
  FFS signaling detail of cell list : ECGI list, or cellIdentity List , any optimization needed to reduce the size.

## Slide 3: FFS for email discussion (2/2)
On the DRX cycle that can be configured to a UE in light connection:
  FFS on the values allowed for the eNB to configure a UE in light connection:
    (a) same values as idle paging DRX cycle (i.e. 32, 64, 128, and 256 radio frames), or
    (b) C-DRX values that are multiple to the idle paging DRX cycle values (i.e. 2, 4, 8, 16, 32, 64, 128, 256 and 512 radio frames).
  FFS on paging DRX cycle is used for the RAN-initiated paging:
    (a) The RAN-configured DRX cycle is always used (which is configured by eNB per UE basis) or
    (b) The shortest of RAN-configured paging DRX cycle, UE specific DRX cycle (if configured by upper layers) and default DRX cycle (which is broadcasted).
To allow eNB prioritization based on the cause values of MO data, MO signaling, and MT access. FFS other values e.g. PAU (paging area update).
FFS if UE NAS needs to be informed when UE is in light connection.
FFS if light connection support indication is needed in SI and if so, associated UE behavior.