## Slide 1: No RLC concatenation in NR
Source: Samsung
R2-169092

## Slide 2: PDU format for no concatenation
Preprocessing up to the last MAC SDU
LCID, L
RLC SN
PDCP SN
PDCP SDU
LCID, L
RLC SN
PDCP SN
PDCP SDU
…
LCID, L
RLC SN
PDCP SN
PDCP SDU
SO
On the fly processing for the last MAC SDU
A PDCP SDU is in general mapped to a PDCP PDU, a RLC PDU and a MAC SDU
PDCP SDU can be preprocessed to MAC SDU

## Slide 3
 |  | No RLC concatenation | RLC concatenation
Implementation | Pre-processing | Up to MAC SDU | Up to RLC payload
 | PHY/MAC parallel Tx: Single TB | Similar | 
 | PHY/MAC parallel Tx: CA/MIMO | Possible | Not possible
 | PHY/MAC parallel Rx | Possible | Not possible
 | Rx processing | single step | Multi-step
 | Discard timer aspect | No difference | 
 | Uplink split bearer support | Some issue | No issue
Modeling | PDCP-RLC interface | Clean | Coupled
Overhead | SN space consumption | More | Less
 | VoIP in cell edge: single pkt per PDU | Better | +50% overhead
 | VoIP in good radio: 2 pkt per PDU | Similar | 
 | High data rate: many pkt per PDU | Similar | 
 | Low data rate: sgmt of a pkt per PDU | Similar | 
Front-Haul | Option 2 support | Possible | X2/Xn impacts
 | Option 3-1 support | Possible | Not efficient

## Slide 4: Conclusion
‘No RLC concatenation’ is better than ‘RLC concatenation’
Proposal
  RLC concatenation is not considered in NR
  Further enhancement can be considered during WI phase w.r.t overhead reduction and split bearer support

## Slide 5: Implementation
PHY/MAC parallel processing: Tx
LCID, L
RLC SN
PDCP SN
PDCP SDU
LCID, L
RLC SN
PDCP SN
PDCP SDU
SO
Forwarded to the PHY immediately
Processed in the RLC/MAC
No RLC concatenation
RLC concatenation
LCID, L
RLC SN
PDCP SN
PDCP SDU
PDCP SN
PDCP SDU
LCID, L
LCID, L
Forwarded to the PHY immediately

## Slide 6: Implementation
PHY/MAC parallel processing: Tx in UL CA/UL MIMO
No RLC concatenation
Parallel processing is possible (since PDCP PDUs multiplexed in one MAC PDU can be determined regardless of the other MAC PDU)
RLC concatenation
Only sequential processing is possible (since PDCP PDUs multiplexed in one RLC PDU can be determined only after of completion of the other RLC PDU)
MAC PDU for UL CC 1
MAC PDU for UL CC 2
Processing can start simultaneously
Processing of RLC PDU for CC 2 start after processing of RLC PDU for CC1

## Slide 7: Implementation
MAC start processing from the first block (possible because the relevant header is in the front)
PHY/MAC parallel processing: Rx
No RLC concatenation
RLC concatenation
MAC start processing after the whole MAC PDU is received

## Slide 8: Implementation
Rx processing
LCID, L
RLC SN
PDCP SN
PDCP SDU
LCID, L
RLC SN
PDCP SN
PDCP SDU
…
LCID, L
RLC SN
PDCP SN
PDCP SDU
SO
No RLC concatenation
Single step sequential processing
RLC concatenation
LCID
L
SN
PDCP SDU
LI
SN
L
PDCP SDU
SN
L
…
1
MAC Payload identification
1
RLC PDU identification
2
3
Sequential processing

## Slide 9: Discard timer aspect
In NR, PDCP reordering is always enabled.
PDCP SN gap cause severe delay (i.e. until reordering timer expiry which should be multiple times of RLC ARQ RTT)
Because of above, both NW and UE shall not allocate PDCP SN too much in advance
  Even in LTE, LTE PDCP specification is already written such that SN allocation to PDCP SDU can be done long after reception.

## Slide 10: Split bearer support
No concatenation supports split bearer with local RLC ARQ based on the double SN (PDCP SN and RLC SN).
In split bearer case, pre-processing up to MAC SDU is supported with the exception of the RLC SN which can only be decided when the Cell Group for transmission is decided.
Limiting UL pre-processing will only be an issue at very high UL data rates. Problem can be overcome by implementation e.g.
  Earlier allocation of PDCP PDU’s to MAC entity (in high data rate transmission case, complete RLC PDU stalling is unlikely).
  In moderate data rate transmission case, stalled PDCP PDU in one leg can be updated so that it is transmitted in the other leg
During Work Item, additional enhancements can be considered e.g. working with PDCP SN in RLC layer (common SN).

## Slide 11: Overhead analysis (1)
VoIP in bad coverage (no bundling)
LCID
L
SN
PDCP SDU
1B
1B
1B
35B
2) Concatenation
Overhead = 6/41 = 14.6%
LI
1B
SN
1B
L
1B
LCID
L
SN
PDCP SDU
1B
1B
1B
35B
1) No concatenation
Overhead = 4/39 = 10.3%
SN
1B

## Slide 12: Overhead analysis (2)
VoIP in good coverage (2 voice packets per MAC PDU)
2) Concatenation
Overhead = 8/78 =10.3%
LCID
L
SN
PDCP SDU
1B
1B
1B
35B
1) No concatenation
Overhead = 8/78 = 10.3%
SN
1B
LCID
L
SN
PDCP SDU
SN
LCID
L
SN
PDCP SDU
1B
1B
1B
35B
LI
1B
SN
1B
L
1B
PDCP SDU
35B
SN
1B
L
1B

## Slide 13: Overhead analysis (3)
High data rate (80 IP packets per MAC PDU)
2) Concatenation
Overhead = 0.36%
LCID
L
SN
PDCP SDU
1B
2B
3B
1500B
1) no concatenation
Overhead = 0.60%
SN
3B
LCID
L
SN
PDCP SDU
SN
LCID
L
SN
PDCP SDU
1500B
LI
SN
L
PDCP SDU
1500B
SN
L
1B
2B
3B
2B
2B
3B
2B
3B

## Slide 14: Overhead analysis (4)
Low data rate: single PDCP SDU is segmented in to a multiple MAC PDUs
In this case, only difference between ‘no concatenation’ and ‘concatenation’ comes from how a PDCP PDU is segmented
According to the last meeting decision, SO-based segmentation shall be used for both options.
There should be no difference if both options use the same segmentation mechanism

## Slide 15: Front-haul: Option 2
PDCP
RLC
MAC
PHY
Scheduling decision
PDCP SDUs received
PDCP PDUs forwarded to the RLC in DU
RLC concatenates PDCP PDUs according to the scheduling decision
MAC PDU is transmitted
PDCP SDUs received
PDCP PDUs forwarded to the RLC in DU
MAC SDUs are concatenated according to the scheduling decision
MAC PDU is transmitted
PDCP
RLC
MAC
PHY
Scheduling decision
No RLC concatenation
RLC concatenation

## Slide 16: Front-haul: Option 3-1 upper RLC doing ARQ and lower RLC doing concatenation
Upper RLC
Lower RLC
MAC
PHY
Scheduling decision
PDCP SDUs received
Upper RLC forwards PDCP PDUs to lower RLC
MAC PDU is transmitted
No RLC concatenation
RLC concatenation
PDCP
Lower RLC makes RLC PDU according to the scheduling decision
PDCP SDUs received
Upper RLC process them to the RLC PDU
RLC PDUs are forwarded to the lower RLC
MAC SDUs are concatenated according to the scheduling decision
MAC PDU is transmitted
Upper RLC
Lower RLC
MAC
PHY
Scheduling decision
PDCP
It is not realistic with RLC concatenation option because lower RLC has to feedback RLC PDU to upper RLC continuously
Feeding back
RLC PDU
Lower RLC forwards RLC PDU to upper RLC so that ARQ is possible