## Slide 1: WF for Inter-PLMN Issues
Huawei, HiSilicon
R2-1702074

## Slide 2
[CB] Find a way to be forward compatible in terms of pool configurations for safety vs. non-safety V2X. RAN2 will not optimize procedures for non-safety in Rel-14.
Only upper layers know whether a V2X message is safety or non-safety related.
1/ an indication of safety or non-safety, a mapping between safety/non-safety and frequencies
2/ Potential agreement 1:
Stage-2 description only: a mapping between service types and V2X frequencies is configured by upper layers. The UE should ensure a service to be transmitted on the corresponding frequency.
An LS should be sent to SA2.
-LG, Qualcomm, Samsung, ZTE, Ericsson, Huawei, CATT

## Slide 3
[CB] For cell selection/reselection, the UEs prioritizes the carrier/cell that provides cross-carrier V2X SL configuration. FFS whether a carrier with V2X resource is prioritized over a cell providing cross-carrier V2X resources.
Potential agreement 2:
For cell selection/reselection, the UEs may prioritize the carrier/cell that provides cross-carrier V2X SL configuration.
The UE shall not use Pre-configuration if the UE detects a cell providing V2X resource configuration or cross-carrier V2X resource configuration.
Uu carriers which may provide V2X sidelink resource configuration or cross-carrier configuration can be pre-configured.
[CB for mode 4 and if the exceptional pool needs to be provided in the handover command]
Potential agreement 3:
The usage of exceptional pools will not be changed. Current specification supports to signal exceptional pool in handover command.

## Slide 4
FFS whether more than one resource pool needs to be configured for mode-3 to allow configuration of pools with different synchronization types.
Potential agreement 4:
When the UE changes its timing from GNSS to eNB timing (i.e., losing GNSS), how does the eNB perform Mode 3 scheduling based on the new synchronization timing:
FFS Option-1: the UE informs the synchronization type change;
FFS what is the maximum number of carriers to be configured for V2x PC5 communication.
Potential agreement 5:
From RRC signalling perspective, up to 8 carriers to be configured for V2X sidelink communication are supported.

## Slide 5
DFN offset can be configured per cell. Details of the formula used by the UE are FFS and how pre-configuration configuration would work is FFS.
Potential agreement 6:
Usage of DFN offset:
option 2) the UE determines DFN timing=(GNSS timing+offsetDFN) if gnss is configured in typeTxSync and offsetDFN is configured.
Both pre-configuration and SIB are used to configure DFN offset.
The formula does not need to be changed, and in the field description, the usage of DFN offset can be described.