## Slide 1: WF LPP support for feMTC OTDOA
Ericsson, …
R2-1702260
3GPP TSG RAN WG2 Meeting #97
Athens, Greece, 13th – 17th Feb 2017
Agenda item 8.12.4

## Slide 2: Background
During RAN1#87 it was agreed to introduce positioning support based on OTDOA for further enhanced MTC. The agreements are summarized in an LS from RAN1#87 to RAN2 [1], see Annex A for details, and the higher layer parameters are provided in an LS from RAN1#87 to RAN2 [2].
There are some alternatives for signalling design in RAN2 to support the RAN1 agreements submitted to RAN2#97 including [3], [4], [5]
This way forward lists the key agreements needed, and a merged draft CR considering [3]-[5] and this WF is provided in [6]
[1] R1-1613760, LS on Rel-14 FeMTC OTDOA enhancements, LS out, RAN1#87
[2] R1-1613781, LS on Higher layer parameters for Rel-14 FeMTC, LS out RAN1#87
[3] R2-1701032, Introduction of positioning for further enhanced MTC , Ericsson
[4] R2-1701033, 36.355 CR0162, Introduction of positioning for further enhanced MTC, Ericsson
[5] R2-1701132, 36.355 CR0164, Introduction of OTDOA enhancements for FeMTC in LPP, Qualcomm
[6] R2-1702257, 36.355 CR0162R1, Introduction of OTDOA enhancements in LPP for feMTC

## Slide 3: Representation of additional PRS configs
The RAN1 agreement includes support for up to three PRS configurations per cell. The signalling additions are limited if reusing the existing PRS-Info. However, some extensions are needed.
Proposal 1: Reuse the existing PRS-Info to represent also the additional PRS configurations
Observation 1: Not all possible configurations of muting, config index and add-numDL-Frames can be considered in light of the RAN1 agreements
Proposal 2: Use the existing fields but with the restrictions from the RAN1 agreements
Proposal 3: Add the following fields to the reference and neighbour cells
  dlBandwidth of the cell; needed to determine the frequency of the narrowbands
  addPRSconfig; one or two additional PRS configurations
Proposal 4: Add the following fields to the PRS-Info IE
  prsConfigIndex; to enable reference to the PRS configurations in the signal meas info report
  finePrsOccInterv; the PRS interval between the multiple PRS occasions within one PRS period
  prsHoppingInfo; one or three narrowbands used in addition to the center band for hopping

## Slide 4: RSTD reports based on multiple PRS configurations
When the target device obtains multiple PRS configurations it may only be able to use a subset of the PRS configurations. To make the network understand what was used, and enable long-term reconfigurations, it is important with feedback from the device about what PRS configurations that was used to determine RSTD.
Proposal 5: Add the following fields to the signal measurement information IE for both reference and neighbor cells
  usedPrsConfigList; list of used PRS configuration indices or all

## Slide 5: New OTDOA capabilities
The RAN1 agreement also lists a set of new capabilities for the target device.
Proposal 6: Add the following OTDOA capabilities
  densePrsConfig; support for more than one PRS occasion per PRS period and an extended number of PRS subframes per PRS occasion
  maxSupportedPrsBandwidth; the maximum PRS bandwidth the target device supports
  prsFrequencyHopping; supports for frequency hopping
  maxSupportedPrsConfigs; the maximum supported number of PRS configurations (2 or 3), 1 if omitted.

## Slide 6: Annex A
On configuration of multiple PRS configurations:
Agreement:
PRS bandwidths include {1.4, 3, 5, 10, 15, 20} MHz
No change w.r.t. legacy LTE PRS bandwidths
One cell can transmit multiple PRS time-frequency configurations with possibly up to [3] different PRS bandwidths
Configuration information multiple PRS time-frequency configurations with possibly up to [3] different PRS bandwidths per cell can be signaled to the UE, each information associated with a set of configuration parameters including PRS configuration index, number of PRS subframes per occasion, muting pattern, and new optional parameters
On more frequent PRS transmissions:
Agreement:
Supported legacy PRS periodicities are {160, 320, 640, 1280} subframes that are jointly signaled with starting subframe offsets in PRS configuration indices
  No change w.r.t. legacy LTE PRS indices
Supported number of PRS subframes per PRS occasion are {1, 2, 4, 6, 10, 20, 40, 80, 160} subframes
Reuse LTE PRS muting mechanism with a bit string of {2, 4, 8, 16} bits, with each bit applied to one legacy PRS period
  No change w.r.t. legacy LTE PRS muting pattern
Add additional configuration parameters to support more frequent PRS transmissions and PRS frequency hopping
To support more frequent PRS transmission in time, add the following parameters to support multiple PRS occasions in a legacy PRS period
  PRS occasion interval in a PRS period: {10, 20, 40, 80} subframes
If this is not configured, there is only one PRS occasion in a legacy PRS period.

## Slide 7: Annex A, cont’d
On PRS frequency hopping:
Agreement:
If activated, PRS frequency hopping is configured with the following parameters (similar to Rel-13 eMTC FH):
  Number of bands for frequency hopping X: {2, 4}
The first band is in the center
  The positions of the remaining X-1 bands:
The starting position of each of X-1 bands is indicated separately: narrowband {0,1,…,max-1}
On UE capability signaling:
Agreement:
Signalling is provided for the UE to indicate the capability information below for OTDOA positioning to the E-SMLC in LPP
Maximal PRS bandwidth for RSTD measurement
PRS-frequency-hopping-based RSTD measurement