## Slide 1: WF OTDOA reporting for multiple PRS configurations
Ericsson, …
R2-1702362
3GPP TSG RAN WG2 Meeting #97
Athens, Greece, 13th – 17th Feb 2017
Agenda item 8.12.4

## Slide 2: Background
RAN1 agreement [1] on feMTC OTDOA positioning allow up to three PRS configurations to be provided to the target device.
[2], [3], [4] proposes to add a configuration index per PRS configuration to enable the device to report which PRS configurations that were used for OTDOA measurements. This enables the operator to understand what PRS configurations are really useful and can adapt the network configuration.
During RAN2 online discussions [5], concerns were raised that “not all UEs need to report this, and not all the time” and therefore “if this enhances the positioning performance, then we should let R1 determine if ti use this”
This affects networks with either feMTC or NB-IoT, since multiple PRS configurations are possible for both
[1] R1-1613760, LS on Rel-14 FeMTC OTDOA enhancements, LS out, RAN1#87
[2] R2-1701032, Introduction of positioning for further enhanced MTC , Ericsson
[3] R2-1701033, 36.355 CR0162, Introduction of positioning for further enhanced MTC, Ericsson
[4] R2-1702260, WF LPP support of feMTC OTDOA, Ericsson
[5] Report from the IoT breakout sessions, RAN2, Mediatek

## Slide 3: Redesign of the PRS Configuration index
The concerns raised in RAN2 can easily be addressed with a minor change:
The location server optionally includes a configuration index per PRS configuration in the OTDOA assistance data
The target device feeds back a list of the used configuration indices, if i) configuration indices have been provided by the location server AND ii) less than all provided configuration have been used
Proposal 1: Add support for on demand feedback of used PRS configuration to LPP

## Slide 4: Detailed changes needed to be introduced
Proposal 2: Add the following to LPP:
  optional prsConfigIndex to the PRS-Info IE
  usedPrsConfigList to the Signal Measurement Information IE
  a description making the usedPrsConfigList mandatory if prsConfigIndex has been configured and less than all PRS configurations have been used