## Slide 1: CB44
Support of keeping the DL UP termination point
on the RAN-CN interface at mobility

## Slide 2: Logical architecture
TS 38.401 states:
  “One physical network element can implement multiple logical nodes.”
  Example of a deployment scenario:
In this scenario it is possible to preform an HO where source CU-UP and target CU-UP are with the same physical network element.
This scenario does not seem to violate the agreed RAN3 logical model and cardinality.
Proposal 1: confirm that the deployment scenario with central UP is possible. Further study and consideration may be needed on possible impact on the logical model (if any) and related specifications.

## Slide 3: Benefits
The scenario described in previous slide, offers the possibility of performing mobility and dual-connectivity procedures where:
  The UP tunnels to the CN are not changed;
  Data forwarding between source and target CU-UPs is avoided.
Keeping the UP tunnels saves signalling in the CN.
Avoiding data forwarding reduces HO latency.
Proposal 2: confirm that the central UP scenario may introduce some benefits for efficient mobility and resource management.

## Slide 4: Impact on specifications
Example of a possible solution to support efficient mobility with central UP:
  One optional IE in some X2 / Xn messages: this allows the source node to inform the target node about the possibility of keeping the UP tunnels toward CN.
  One optional IE in some S1 / NG messages: this allows the target node to inform the CN that the UP tunnels can be kept at mobility.
  One optional IE in the E1 Bearer Context Setup messages: this allows CU-CP to inform the CU-UP about the possibility of keeping the UP tunnels toward CN.
Other solutions can also be considered.
Some companies raised concern on impact on logical architecture and interfaces. If impact is identified, it should be analyzed.

## Slide 5: Way Forward
Agree on the following proposals:
  Ack that the deployment scenario with central UP is possible:
    Proposal 1: confirm that the deployment scenario with central UP is possible. Further study and consideration may be needed on possible impact (if any) on the logical model and related specifications.
  Ack that the scenario with central UP may introduce benefits:
    Proposal 2: confirm that the central UP scenario may introduce some benefits for efficient mobility and resource management.
Continue discussing possible solutions and impact analysis for supporting efficient mobility with central UP.