## Slide 1: SoD for TNL Address Discovery on Option 3
NTT DOCOMO, INC.
R3-187111
3GPP TSG-RAN WG3 RAN3#102
Spokane, Washington, USA, 12th Nov 2018 - 16th Nov 2018

## Slide 2: Tasked work in this CB
CB: # 27_ANRopt3
- further clarify scenario, implications
(NTT)
summary of offline disc R3-187111

## Slide 3: Outline of Option 1 and Option 2
The difference of Option 1 and Option 2 is which “key” is used to find the associated eNB in MME.
  gNB ID for Option 1 and eNB ID for Option 2
Option 2 would be better from MME impact point of view.
gNB ID | eNB ID | eNB S1 AP Address
A | 1 | …
B | 2 | …
… | … | …
X | 2 | …
A | n | …
Note that eNB ID/en-gNB ID may be duplicated as this is several vs several mapping.
Example of table in MME for Option 1
eNB ID | eNB S1 AP Address
1 | …
2 | …
… | …
… | …
n | …
Example of table in MME for Option 2
 | Option 1 | Option 2
Table | Needs to be updated | Reuse the function on LTE
Function |  | 
Frequency of Update | More (eNB connection+en-gNB connection basis) | Less (eNB connection basis)

## Slide 4: Scenario 1:An area is covered by only two eNBs
Both options can find associated eNB if associated eNB is properly configured.
  On Option 1, associated eNB needs to connect same MME with one of eNBs covering en-gNB area
  On Option 2, associated eNB needs to overlap the coverage of en-gNB
eNB1
eNB2
en-gNB A
 | eNB ID picked up from NRT | Reported en-gNB ID | Looked up table | Reachable eNB | Associated eNB
Option 1 | - | A | A-2 | 2 | 2
Option 2 | 2 | A | 2 | 2 | 
UE
ANR reporting
X2

## Slide 5: Scenario 2: An area is covered by more than two eNBs
Both option could work well.
Option 2 may need several attempts.
eNB1
eNB2
en-gNB A
UE
ANR reporting
eNB3
X2
 | eNB ID picked up from NRT | Reported en-gNB ID | Looked up table | Reachable eNB | Associated eNB
Option 1 | - | A | A-2 | 2 | 2
Option 2 | 2,3 | A | 1,2,3 | 2 | 

## Slide 6: Scenario 3: new co-site en-gNB and eNB is deployed
If the associated eNB is not new (i.e. already in the network).
  Both option 1 and option 2 could work well.
If the associated eNB is the new (i.e. eNB co-site with the en-gNB.)
  Option 1 works when the co-site eNB reports the en-gNB to MME.
  Option 2 works when the NRT is updated by e.g. ANR reporting.
eNB1
eNB2
en-gNB A
UE
MR
PCI2, PCI3
ANR reporting (LTE)
eNB2, PCI 2
eNB3
X2
NRT
eNB3 PCI3
eNB2 PCI2
Option 2: NRT update by ANR reporting

## Slide 7: Inter MME routing
Option 1 may have issue on inter-MME case.
  The TAI of LTE cell provided by CGI reporting may not be related with the MME the en-gNB (indirectly) connected to.
  Then, TNL address discovery function may be failed.
  To avoid that, some restriction on the connection to MME is required
    E.g. (1) associated eNB connects to all possible MMEs covering an en-gNB area(2) all eNBs covering an en-gNB area connects to up to one or two MME….
Option 2 doesn’t have such issue.
  relation between the key (eNB ID) and TAI (via X2/CGI reporting) is correct every time.
eNB1
eNB2
en-gNB A
UE
CGI reporting
-eNB3 TAI Z
-en-gNB A
eNB3
X2
Note the clean/complete solution is to standardize the interface between MMEs (SA2 and CT4?)
MME X
MME Y
S1
S1
1. Transfer container to en-gNB A in TAI Z?
2. He doesn’t know en-gNB A
MME Z

## Slide 8: Observation
Following observation is obtained.
By the way, this meeting is last meeting for Rel-15 function freeze.
RAN3 needs to decide solution in this meeting to implement this function in Rel-15.
 | Option 1 | Option 2
MME impact | More | Less
Frequent update of table | More | Less
Attempt | Basically one | May be several
Restriction on Initially configured associated eNB | Same MME with one of eNBs covering en-gNB area | eNB overlaps the coverage of en-gNB
What to be required | -Limitation on MME connection (e.g. one or two in the en-gNB area(*)) | -Configure proper NRT -Ask proper eNB (up to implementation)
*: it may not be strong restriction as MME can cover broad area

## Slide 9: Way forward
RAN3 to adopt either option (i.e. option 1 and option 2)

## Slide 10: <Annex>Call flow for Option 1 and 2
  Example call flow is shown below.
Red: specific for Option 1
Blue: specific for Option 2
UE
eNB1
MME
eNB2
en-gNB A
CGI reporting
(gNB ID (A))
EN-DC X2 setup
S1Setup/eNB Config. Update
(eNB ID (2) and gNB ID (A))
eNB Config. Transfer
Get the eNB2 address
MME Config. Transfer
EN-DC Config Transfer and resp.
eNB Config. Transfer
MME Config. Transfer
EN-DC X2 setup
Measurement reporting
(PCI for eNB ID 1)

## Slide 11: Reference
31.3.3. TNL Address Discovery for Option 3 Specification needs to enable routing of TNL address requests at MME for TNL address discovery of Opt 3 in Rel-15 We use a protocol fn of S1 equivalent to current functionality (e.g. S1 TNL config transfer procedure to start TNL address discovery) Routing function of TNL address requests resides in the MME; further details are FFS Previous summary of offline disc (R3-186141), noted To be continued on the basis of the 2 solutions currently on the table… |  | 
R3-186479 | En-gNB X2 TNL address discovery (Huawei) | discussion noted
R3-186480 | En-gNB X2 TNL address discovery (Huawei) | draftCRr, TS 36.300 v15.3.0, Rel-15, Cat. F
R3-186481 | En-gNB X2 TNL address discovery (Huawei) | CR1634r, TS 36.413 v15.3.0, Rel-15, Cat. F
R3-186482 | En-gNB X2 TNL address discovery (Huawei) | CR1262r, TS 36.423 v15.3.0, Rel-15, Cat. F
R3-186509 | Left issue for ANR of option 3 (ZTE Corporation) | discussion noted Resp in R3-187008, noted
R3-186872 | Introducing X2 TNL Address discovery for en-gNBs for EN-DC (Ericsson) | discussion noted Resp in R3-187009, noted
R3-186873 | Introducing X2 TNL Address discovery for en-gNBs for EN-DC (Ericsson) | draftCRr, TS 36.300 v15.3.0, Rel-15, Cat. F
R3-186782 | Introducing X2 TNL Address discovery for en-gNBs for EN-DC (Ericsson, Vodafone) | CR1599r3, TS 36.413 v15.3.0, Rel-15, Cat. F
R3-186783 | Introducing X2 TNL Address discovery for en-gNBs for EN-D (Ericsson, Vodafone) | CR1228r2, TS 36.423 v15.3.0, Rel-15, Cat. F