## Slide 1: Source: China Telecom, CATT, ZTE
Scenarios and Requirements for Interference Coordination between LTE and NR
3GPP TSG-RAN WG3 #111-e R3-210449
25 January – 4 February 2021 Online
Agenda :31.2.3
Document for: Discussion

## Slide 2: Introduction: Previous Discussion in Rel-17
PRACH Coordination between LTE and NR was discussed as part of SON/MDT WID in RAN3#110e meeting. The scenario mainly concerns about the PRACH Coordination between an LTE cell in an upgraded site and an NR cell in a newly-built NR site [1]. Some initial discussions were reflected in [2] that most companies are interested in this scenario and support to send a LS to RAN1 for requesting feedback on the described scenario and potential solutions for PRACH Coordination between LTE and NR. If confirmed by RAN1, RAN3 would further work on a solution for this problem in Rel-17, while some company consider the interference coordination at every channels, including uplink and downlink, are need to be studied, so it should be treated as a separate and independent topic.
In this paper, we further elaborate more issues on the scenarios and requirements for interference coordination between LTE and NR, and propose further work on this topic.

## Slide 3: Background
Hard to reframing low-band spectrum in short-term:
  In 4G era, some low-band spectrums, such as 1.8GHz, was deployed as the coverage layer in urban area while a second carrier (e.g., 2.1GHz) was deployed as capacity layer in the region with high capacity requirements. Since the downlink/uplink load of LTE cell is still high, it is hard to reframing the low-band spectrum in hotspot region to NR in short-term.
the co-channel interference between existing LTE and newly-built NR should be considered:
  In order to achieve continuous NR coverage for 5G SA network, low-band 5G in FDD spectrum will be introduced in 5G network to rapidly extend coverage without requiring new sites.
  Given that some low-band FDD spectrum(e.g., n1) support up to 50MHz bandwidth in Rel-16, they can provide a fantastic capacity and coverage for low-capacity region.
Co-channel interference
NR Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz
n1 | 15 | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes
 | 30 |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes
 | 60 |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes
n2 | 15 | Yes | Yes | Yes | Yes |  |  |  | 
 | 30 |  | Yes | Yes | Yes |  |  |  | 
 | 60 |  | Yes | Yes | Yes |  |  |  | 
n3 | 15 | Yes | Yes | Yes | Yes | Yes | Yes | Yes | 
 | 30 |  | Yes | Yes | Yes | Yes | Yes | Yes | 
 | 60 |  | Yes | Yes | Yes | Yes | Yes | Yes | 

## Slide 4: Scenario1
Scenario 1: the existing LTE 2.1GHz hotspot sites are upgraded to support DSS function which deliver both 4G and 5G service while more 2.1GHz NR sites without DSS function are built to provide continuous coverage for NR.
20MHz DSS
20MHz DSS
20MHz DSS
40MHz
clear NR
case1
case2
In MR-DC scenario, current specifications support coordination of radio resource allocation between an eNB and en-gNB that are sharing spectrum via E-UTRA – NR Cell Resource Coordination procedure. Since no direct interface exits between eNB and gNB, the existing E-UTRA – NR Cell Resource Coordination procedure cannot be reused in SA scenario.

## Slide 5: Scenario2
Scenario2: LTE FDD and NR FDD are deployed in adjacent region
Outdoor Scenario: some low-band spectrums as 4G capacity layer were deployed in hotspot region while NR FDD spectrum can be deployed in adjacent region to achieve NR continuous coverage
Indoor Scenario: NR TDD(e.g., n77/n78) , due to its propagation characteristics, has difficulties in offering adequate coverage especially in some indoor scenarios. In order to improve the indoor coverage for NR, the low-band NR spectrum was introduced in DAS. The outdoor was also deployed of LTE FDD with low-band spectrum.

## Slide 6: Scenario 3: Remote Interference
Statistics from Suzhou, Jiangsu province
it is observed that the remote interference from LTE FDD, furthest as 4.1 km away with observed record, severely impact the network coverage and capacity.
  LTE FDD eNBs are deployed as a dedicated network along the high-speed rail to provide data and voice service for passengers.
  Given that all the voice services are currently carried by LTE, it is hard to reframing low band spectrum to NR for dedicate network in a short time.
Proposal 1: We kindly ask RAN1 and RAN3 to confirm the scenarios on interference coordination between LTE and NR in Rel-17.

## Slide 7: Uplink Interference Coordination
the PRACH coordination were already supported in Rel-16 SON/MDT:
  The RACH configuration has critical impacts on user experience and overall network performance.
Same PRACH design for LTE and NR in low band:
  The design of Format 0 type preamble is copied from LTE: both RATs has same length, SCS, root sequence and PRB bandwidth.
  operators prefer to configure Format 0 type preamble for both LTE and NR in FDD Band.
  In principle, the necessity of PRACH coordination between LTE and NR is the same as that between intra-system.
RACH Optimization
Interference coordination in other uplink channels
Proposal 2: it is necessary to study Uplink interference coordination between LTE and NR should be considered in Rel-17.
PUSCH coordination: This feature has already been supported in LTE ICIC. The X2AP message Load information is used to exchange the uplink IOT information between nodes.

## Slide 8: Downlink Interference Coordination
CRS Interference Cancellation
PDSCH Interference Coordination
LTE CRS severely impacts the downlink performance of NR UE
  Legacy NR commercial UEs can not support CRS-IC. Therefore, network based /assisted solution is also needed
  The network can configure LTE-CRS Rate-Matching /ZP CSI-RS to mitigate one interference source
Victim NR subframe
Interfering LTE subframe
PDSCH coordination: This feature has already been supported in LTE ICIC. The X2AP message Load information is used to exchange the downlink interference information between nodes.
Proposal 3: Network based/assisted CRS cancellation and PDSCH interference coordination need to be studied in Rel-17.

## Slide 9: Downlink Interference Coordination: Lab Test Results
Observation 2: Without any resource coordination and CRS migration, the downlink throughput of NR significantly decrease
Lab Test Results

## Slide 10: Rel-15 LS from RAN1 to RAN3
LS was to RAN3 from RAN1 to specify the Xn interface and enhanced X2 interface messages that enable coordination between LTE and NR [3], including
  LTE cell on/off configuration with details up to RAN3
  LTE MBSFN subframe configuration
  DL and/or UL carrier center frequency (ARFCN)
  Carrier bandwidth
  Signaling related to timing synchronization and SFN
    Note: this does not require the network to be synchronized and/or SFN aligned and/or radio frame boundary aligned
    Note: It is up to RAN3 if this requires new procedures in addition to signaling support
  Indication of semi-statically used resources (to avoid collisions with, e.g., CSI-RS, SRS, PRACH, PUCCH, DRS, PSS/SSS, PBCH, …)
  Indication of slots/PRBs not intended for transmissions by the eNB and gNB, respectively
RAN3 specified the feature only for the following two scenarios in Rel-15:
  Coordination between eNB and en-gNB
  Coordination between gNB and ng-eNB
LTE-NR coexistence coordination between eNB and gNB in standalone scenario is not supported in Rel-15

## Slide 11: Work Split for RAN WGs
Transfer of reference and control channel resources from LTE to NR(RAN3)
Coordination of Physical resource usage between LTE and NR(RAN3)
Measurement configuration towards UE according to the intended PRB usage of the inter-RAT neighbor cell? (RAN2)
Information transfer from LTE to NR only is not sufficient to address the problem (other WGs needs to be involved)(RAN1,RAN2)?
  Resource coordination (including time and frequency) is rarely useful in practice unless it is intra-vendor
  Neighboring LTE site does not necessarily cause interference to all UEs of a NR cell as shown in following figure. gNB shall not completely reserve the resource used by LTE. This is different from the case that gNB and eNB are co-located.

## Slide 12: Possible RAN3 Signaling Design to support LTE-NR coexistence
Some possible options to support LTE-NR coexistence feature between eNB and gNB are as below:
  Option 1: Coordination between eNB and gNB via core network: extend RIM message?
  Option 2: eNB coordinates with neighbour gNBs via co-located gNB node.
  Option 3: Setup direct interface between gNB and eNB.
Since option 3 has too much impact to RAN3 architecture, we propose to focus on the first two options or only Option2.
No new interface between LTE and NR shall be introduced
Option2: eNB coordinates with neighbour gNBs via co-located gNB node

## Slide 13: Conclusion
Proposal 1: We kindly ask RAN1 and RAN3 to confirm the scenarios on interference coordination between LTE and NR in Rel-17.
Proposal 2: it is necessary to study Uplink interference coordination between LTE and NR should be considered
Proposal 3: Network based/assisted CRS cancellation and PDSCH interference coordination need to be studied.

## Slide 14: Reference
R3-206554,China Telecom,ZTE,Huawei,Discussion on the PRACH Coordination between LTE and NR
R3-207030,Nokia, CB: # 1007_SONMDT_RACH - Summary of email discussion
R1-1715041/R3-173397,LS on RAN3 signaling support for LTE-NR coexistence feature

## Slide 15
THANK YOU .
Notes: 模板来自于 http://docer.wps.cn