## Slide 1: Notes from Tuesday evening session on CB#30_OverallNetworkArch
NTT DOCOMO, INC.
3GPP TSG-RAN WG3 Meeting #96
Hangzhou, China, 15th-19th May, 2017
Agenda Item: 10.11.1
R3-171935

## Slide 2: Copy from Chairman Notes
The node providing NR in option 3 is part of E-UTRAN? A node providing NR in E-UTRAN and a Node NR in NG-RAN are 2 different logical entities? A node providing E-UTRA in E-UTRAN and a Node E-UTRA in NG-RAN are 2 different logical entities? Name the node compare to the radio access? Compare to the interface? Alternative operating mode or a global NG-RAN node CB: # 30_OverallNetworkArch - attempt to respond to respond to question … - attempt to converge on an Overall Network Architecture (including opt 3) (NTT DCM) Rev in R3-171935

## Slide 3: Structure of discussion
It was attempted to first discuss and answer Q1-Q3, then Q4, with the disclaimer that Q1-Q3 and Q4 are to be considered orthogonal (i.e. answers for Q1-Q3 should not influence answer for Q4)
  The node providing NR in option 3 is part of E-UTRAN? (Q1)
  A node providing NR in E-UTRAN and a node providing NR in NG-RAN are 2 different logical nodes? (Q2)
  A node providing E-UTRA in E-UTRAN and a node providing E-UTRA in NG-RAN are 2 different logical nodes? (Q3)
  Name the node compare to the radio access? Compare to the interface? (Q4)

## Slide 4: Outcome of discussion
No consensus for Q1 (see Slide5)
Discussion of Q2&Q3 considered difficult / not worthwhile (see Slide5&7)
Q4 was discussed as this is the main question of interest and as it was suggested that it may not be important to address Q1-Q3 before addressing Q4 (see Slide7)
2 possible answers were provided for Q4 without concluding on which to select (see Slide8)

## Slide 5: Discussion on Q1
The node providing NR in option 3 is part of E-UTRAN? (Q1)
  Case1: Node providing NR in Option is only connected to EPC (S1-U)
    Answer1: Yes (part of E-UTRAN)
    Answer2: No (part of NG-RAN)
    Answer3: No (part of EN-DC, i.e. not part of E-UTRAN nor NG-RAN)
  => No consensus.
  => Views exist that it is part of E-UTRAN, that it is part of NG-RAN or it is part of neither (i.e. it is part of EN-DC)
  Case2: Node providing NR in option 3 is connected to both EPC and 5GC (this is related to Q2)
  => Not worthwhile to go to Q2&Q3? (Since there is not consensus for Q1)

## Slide 6: Discussion on Q2&Q3
A node providing NR in option 3 and a node providing NR in NG-RAN are 2 different logical nodes? (Q2)
A node providing E-UTRA in E-UTRAN and a node providing E-UTRA in NG-RAN are 2 different logical nodes? (Q3)
  Clarifications provided for questions received for Q2&Q3:
    1 physical eNB connected to S1 and NG would be 2 different logical nodes
    It would have two node IDs
    For the broadcast cell ID, so far the necessity to broadcast 2 cell IDs (one for 4G and one for 5G) have not been identified. Both ECGI and PCI can be the same (NOTE: answer is provided in the context of Q3). So this is in general for further study and does not really influence the answer for Q2&Q3.

## Slide 7: Discussion on Q2&Q3
A node providing NR in option 3 and a node providing NR in NG-RAN are 2 different logical nodes? (Q2)
A node providing E-UTRA in E-UTRAN and a node providing E-UTRA in NG-RAN are 2 different logical nodes? (Q3)
  Answer1: Yes
  Answer2: ??
  => Difficult to discussed Q2 when answer to Q1 is not clear?
  For the example of eNB connected to both EPC and 5GC, the operation connected to EPC will be defined in 36series and operation connected to 5GC will be defined in 38series.
  => As long as this is the case, Q1-Q3 may not be important?
  For NR node operation, it will only be defined in 38series

## Slide 8: Discussion on Q4
Name the node compared to the radio access? Compare to the interface? (Q4)
  A) Name for NR node in option 3?
  B) Name for E-UTRA node in NG-RAN?
  C) Name for NR node in NG-RAN?
  Answer1: “gNB” for A), “eNB” for B) and “gNB” for C)
  Answer2: “gNB” for A), “NG-RAN node” for B) and C)
    Explanation for Answer2: Node name is defined based on radio for option 3, and is defined based on NW interface for NG-RAN
    Disclaimer for Answer2: Node ID handling is FFS