## Slide 1: CB: #21_UE_InitAccess
R3-174123
TSG RAN WG3 #97bis meeting
October 9th – 13th, 2017
Prague, Czech Republic

## Slide 2: Scope of come back
Clarify successful scenario
Clarify what happens in CU, DU, UE
Only after successful scenario has been worked out, discuss any failure cases not covered (if any)
In case of multiple options, try to rank them according to the best coverage of possible failure scenarios

## Slide 3: Clarification of the 3 Alternatives and what happens in CU, DU, UE

## Slide 4: “Alternative 3” and “Alternative 1”
“Alternative 3”
  This is the approach which separates RRC message transfer over F1 and DU resource allocation indication (at least for SRB1) over F1
  DU resource allocation is performed when the DU receives from CU, the UE Context Setup Request message
  It takes 2 roundtrips over F1 for RRC Conn. Request ~ RRC Conn. Setup
  DU resource allocation for DRB takes place in following steps
“Alternative 1”
  This is the approach which concatenates RRC message transfer over F1 and DU resource allocation indication (at least for SRB1) over F1
  DU resource allocation is performed when the DU receives from UE, the RRC Conn. Request message
  It takes 1 roundtrip over F1 for RRC Conn. Request ~ RRC Conn. Setup
  DU resource allocation for DRB takes place in following steps

## Slide 5: “Alternative 3”
UE
DU
CU
RRC Conn. Req.
Initial UL RRC message
carries
RRC Conn. Req.
UE Cntxt. Setup Req.
UE Cntxt. Setup Resp.
DU resource allocated
DL RRC Message Xfer
RRC Conn. Setup
carries
RRC Conn. Setup
incl. configuration of DU resource allocated
carries info on
DU resource allocated
DU resource allocated configured to UE
incl. configuration of DU resource allocated
NOTE
DU resource allocated refers to :
- at least SRB1 resource
- possibly semi-static L1
resource (e.g. CQI, SRS)
- but not DRB resource

## Slide 6: “Alternative 1”
UE
DU
CU
RRC Conn. Req.
Initial UL RRC message
DU resource allocated
DL RRC Message Xfer
RRC Conn. Setup
carries
RRC Conn. Setup
incl. configuration of DU resource allocated
DU resource allocated configured to UE
incl. configuration of DU resource allocated
carries both
RRC Conn. Req. and
DU resource allocated
NOTE
DU resource allocated refers to :
- at least SRB1 resource
- possibly semi-static L1
resource (e.g. CQI, SRS)
- but not DRB resource

## Slide 7: “Alternative 2”
“Alternative 2”
  This is similar to “Alternative 1”
  Only difference is that the UE Context Setup Request message is used instead of DL RRC Transfer message. UE Context Setup Request also contains RRC Conn. Setup message.
  As a result, there is a response from DU to CU, i.e. the UE Context Setup Response message. This response message is used for completion of UE context creation.
    It is assumed that DU resource allocation takes place before the UE Context Setup Request message, since otherwise, DU resource allocation cannot be included in the RRC Conn. Setup message

## Slide 8: “Alternative 2”
UE
DU
CU
RRC Conn. Req.
Initial UL RRC message
DU resource allocated
UE Cntxt. Setup Req.
RRC Conn. Setup
carries
RRC Conn. Setup
incl. configuration of DU resource allocated
DU resource allocated configured to UE
incl. configuration of DU resource allocated
carries both
RRC Conn. Req. and
DU resource allocated
UE Cntxt. Setup Resp.
necessity unclear
NOTE
DU resource allocated refers to :
- at least SRB1 resource
- possibly semi-static L1
resource (e.g. CQI, SRS)
- but not DRB resource

## Slide 9: Way forward

## Slide 10: Way forward
Proposal:
  Discuss and select among “Alternative 1”, “Alternative 2” and “Alternative 3” described in slide 3-8 of this document in future meetings

## Slide 11: Initial comparison

## Slide 12: Initial comparison (1/3)
Benefits of “Alternative 1”
  Fast initial access (FFS how critical the delay is)
  Possibility to extend Initial RRC Message with DU indication on admission/ rejection and trigger admission/rejection via first DL RRC Message Transfer (FFS if this is a benefit or just a disclaimer)
  Alignment with NG Initial Context Setup procedure, i.e. create a full context and perform DRB admission control at the same time (FFS if this itself is a benefit)
  No concerns on not being able to send the RRC Connection Reject message, due to UE Context Setup Failure after SRB1 DU resource allocation failure (FFS if this is not the case for other alternatives)

## Slide 13: Initial comparison (2/3)
Benefits of “Alternative 3”
  RRC Connection Request decoding at gNB-DU not needed (FFS if it is needed for other alternatives)
  Admission Control failure at gNB-DU can be relayed to gNB-CU (FFS if relaying Admission Control failure is an issue for other alternatives)
  Clear function separation of RRC message transfer & DU resource allocation (FFS if this itself is a benefit)
  Unified signalling flow for different case of initial access, i.e. Attach, Idle -> Connected, Inactive -> Connected (FFS if this is not the case for other alternatives)
  Clean handling of failure possible (FFS for which failure cases and if this is not the case for other alternatives)

## Slide 14: Initial comparison (3/3)
Benefits of “Alternative 2”
  FFS if any benefit in addition to “Alternative 1”