## Slide 1: Response to R3-174864
Tdoc R3-174871
AI 10.6.5
For Decision
Nokia, Nokia Shanghai Bell, Huawei, CATT, Qualcomm Incorporated, NEC
3GPP TSG-RAN WG3 Meeting #98
Reno, NV, U.S, 27th November – 1st December 2017

## Slide 2: Background
The RRC_INACTIVE properties state shall meet the following objectives:
TR 38.804:
  A UE in RRC_INACTIVE should incur minimum signalling to fulfil the control latency requirement and minimise power consumption comparable to LTE RRC_IDLE and resource costs in the RAN/CN making it possible to maximise the number of UEs utilising and benefiting from this state.
TR 23.799:
  RAN WG2 is expected to define means for a UE in MM Registered CN Connected state not transmitting or receiving data to achieve a comparable power efficiency to that of a UE in CN Idle state.

## Slide 3: Realization
RRC Inactive state properties:
  NG-C and NG-U kept connected while UE in RRC Inactive state;
    MT User/Control plane data triggers RAN Paging.
  To minimize signaling, Access Stratum Context stored in RAN and the UE;
  1. RAN approach is that RAN paging shall be as reliable as CN paging.
    This requires that RAN paging covers UE location
   2. In order to avoid degraded latency, and keep the signalling with CN low, the AS Context needs to be transfer-able from the old serving RAN node to the RAN node over Xn interface in RNA.

## Slide 4: Requirements (1)
Old RAN node holding AS Context, terminating NG-C and NG-U
New RAN node where UE enters RRC-CONNECTED and AS Context is needed
AS Context transferred from old to new RAN node enabling signaling overhead with CN and latency reduction => Xn transfer required
To enable benefits from RRC Inactive state at UE mobility in RRC Inactive, support for AS Context transfer between old and new RAN node is required over Xn.

## Slide 5: Requirements (2)
Old RAN node holding AS Context, terminating NG-C and NG-U. RAN Paging triggering node.
New RAN node configured with the cell that UE is currently camping on while in RRC Inactive state.
RAN Paging from old to new RAN node enabling UE reachability while in RRC Inactive state.
To enable UE reachability while in RRC Inactive state for MT sessions, support for RAN Paging from old to RAN node(s) providing radio coverage for that UE is required. RAN paging occurs over Xn !

## Slide 6: Solutions
RAN Paging reliability and AS Context transfer relies on connectivity between old and new RAN.
Two solutions:
  RAN Notification Area* limited by Xn connectivity;
  RAN Notification Area extending beyond Xn connectivity by CN relay, if Xn not available (Ericsson);
*“RAN Notification Area”: configured by serving RAN node, either list of cells, or RAN Area (broadcast) or List of TAIs (Ericsson).

## Slide 7: Solution-1 (1)
RAN Paging reliability relies on Xn connectivity between the old RAN node and any an arbitrary RAN node within the RNA.
Consequences:
this requires anchor gNB to configure an RNA in the UE with neighbor gNBs with which anchor gNB has Xn connectivity
Can limit size of RNA based on Tx/speed ratio and this meets realistic deployments with Xn connectivity: if the ratio Tx/speed is very low, the UE should be placed in idle mode (no need to have huge RNAs for these UEs).
Also: there is no clear relationship between # of Xn relationship and size or RNA (a single RAN node may cover a large number of cells and a good number of TAs)
The picture above from Ericsson paper assumes lots of RAN nodes are involved all the time to form a RNA – this is a very unlikely scenario.

## Slide 8: Solution-1 (2)
Xn connectivity within the RNA meets the requirements of slide 1:
Successful paging because UE is in the RNA.
Short latency paging because Paging limited to Xn.
Short latency context retrieval over Xn
Reduces the RAN-CN signaling because NG not involved in the paging and the context retrieval
CN Registration Area
if the ratio Tx/speed is very low CN Registration Area tends to become bigger and Xn relationships existence among all RAN nodes in CN Registration Area could become more challenging => then use idle mode

## Slide 9: Solution-2 (1)
RAN Notification Area extended beyond Xn connectivity by CN relay :
Ericsson proposes RRC inactive includes the case where Xn connectivity not available in RNA
In this case RNA = CN Registration Area as a RAN node does not know of other RAN nodes unless they have a Xn relationship (assuming we establish Xn with all neighbors when RRC inactive is used in a PLMN) and:
  AS Context transfer delayed is via CN (via a non serving AMF, followed by a Path Switch with serving AMF: i.e. one more CN interaction than RAN transfer).
  RAN Paging delayed via CN
  Solution unclear: is CN relay in parallel of Xn paging or after paging failure?
CN Registration Area
CN Registration Area are in general not fully Xn connected -> RAN shall not configure RNA simply by matching CN Registration Area also for cases where CN registration area is not fully covered by Xn relationships. The Ericsson assumption RNA shall be configured as CN registration area with no consideration for Xn availability is not valid.
CN

## Slide 10: Summary
Main requirements | Solution-1 | Solution-2 (Ericsson)
minimise signalling and power consumption Minimize latency Compatible with realistic RAN deployments | minimizes signalling load by paging and context transfer always over Xn Minimizes latency by paging and context transfer over Xn limited RNA size is not a problem because if Tx/speed ratio is very low and drives large CN registration areas for the UE, then use Idle mode | Increases signaling load by systematic paging relayed over CN (loop via a non-serving AMF for context transfer and paging) Increases latency by paging over CN Increases signaling by context transfer over CN (8 messages + 2 Path Switch) Does not work across pool areas
Conclusion: By trying to cover very large RNAs matching large CN Registrations Areas with no consideration for Xn availability, solution 2 becomes inefficient whereas UEs that may require large RNA (i.e. UEs with ratio Tx/speed which is low ) can be more efficiently handled by idle mode. The RAN shall consider Xn availability when Configuring the RNA.