## Slide 1: Summary of offline discussions on UE inactivity monitoring
Samsung, Ericsson, Nokia
3GPP TSG-RAN WG3 #99bis R3-182461
Sanya, China, 16~20 April, 2018

## Slide 2: F1
CU  DU (UE Context Setup/Modification Request)
  Inactivity Monitoring Request IE (Optional)
DU CU
  Alt1 (UE Context Setup/Modification Response):
    Inactivity Monitoring response IE (Optional): enumerate {not supported, …} (Criticality: reject)
  Alt2: add a cause value for rejection
    Cause value: Inactivity Monitoring not supported
  Note: both Alt 1 and Alt 2 in stage 3 for now are put as FFS, and the selection between them depends on the discussions in the next meeting

## Slide 3: E1
The details are FFS

## Slide 4: Inactivity reporting over F1
Class 2 procedure: DU to CU (F1)
IE/Group Name | Presence | Range | IE type and reference | Semantics description | Criticality | Assigned Criticality
Message Type | M |  | 9.3.1.1 |  | YES | reject
gNB-CU UE F1AP ID | M |  | 9.3.1.4 |  | YES | reject
gNB-DU UE F1AP ID | M |  | 9.3.1.5 |  | YES | reject
DRB Activity List |  | 1 |  |  | YES | reject
>DRB Activity List Item |  | 1 .. <maxnoofDRBs> |  |  | EACH | ignore
>>DRB ID | M |  | 9.3.1.8 |  | - | -
>>DRB Activity | M |  | ENUMERATED (Re-active, Not-active) | The DRB is considered Not-active if it has not been used for data transmission for a predefined amount of time. | - | -

## Slide 5: WF: CR/TP details
E1 stg2 (TS38.460): Add Bearer Context Inactivity Notification Procedure
F1 stg2 (TS38.470): Add UE Inactivity Notification Procedure
F1 stg3 (TS38.473): Ready
E1 stg3 (TS38.463): FFS
Stg 2 (TS38.401) : FFS