## Slide 1: Way forward on TNL Address Discovery for Option 3
NTT DOCOMO, INC.
R3-183906
3GPP TSG-RAN WG3 RAN3-AH-1807
Montreal, Canada, 2nd-6th July 2018
Agenda 31.3.3

## Slide 2: Background
TNL address discovery function is very beneficial from operators as discussed in [1].
  e.g. ANR function, which relieve the operator from the burden of manually managing neighbor Relations (NRs).
Considering multi-vendor operability, it is desirable for operators to introduce standardized approach i.e. C-plane solution.
However, there was no agreement for C-plane solutions.
Note that this paper is revised from [2] based on proposals in RAN3#100.

## Slide 3: Options over C-plane and comment for them
Several options were discussed in previous meetings.
  eNB proxy (eNB serve as proxy towards the MME)
    Proposed in [3] and [4]
  Direct connection between gNB and MME
    No one proposes currently.
      May be religious war as mentioned in [3]?
  X2 GW
    Proposed in [5]-[10]
MME
Forwarding
table
gNB
eNB
gNB
X2 GW
Forwarding
table
eNB
gNB
MME
Forwarding
table
eNB
Registration:
TNL address discovery:

## Slide 4: Comparison of options
Following table compares each option considering related papers (i.e. [3]-[10])
 |  | 1. eNB Proxy | 3. X2GW
Registration | gNB Configuration of TNL address | No addition | One more (X2GW)
 | Additional interface | No addition | One more (X2 between X2 GW and en-gNB)
 | Impact on current message | Modify “S1 setup req. /eNB config. update” over S1 | No impact
 | New node | No | Maybe (Not necessarily to be new node; anywhere as far as X2 connection)
Address discovery | Additional interface | No addition | One more (X2 between X2 GW and eNB)
 | Impact on current message | Modify “eNB/MME config. transfer” over S1 | Modify “X2 Message Transfer” over X2
 | Message delay | No | Yes if all X2 messages are transferred via X2 GW
Others |  | Need to consider when the peer eNB is not working (e.g. by reset) | Need to consider when the X2GW not working (e.g. by reset)
Note1: “2.Direct connection between gNB and MME” is omitted as there was no supporter.
Note2: RAN2 impact in [10] is omitted as both methods seem to require RAN2 impact (i.e. mechanism for UE to report broadcasted NR cell id.)

## Slide 5: Wayforward
RAN3 to specify at least one C-plane solution for TNL address discovery of Option 3 in Rel-15.
RAN3 to agree which option(s) to be specified in Rel-15 in RAN3-AH-1807.
  If RAN3 specifies “X2 GW” solution, following clarification/conditions are required at least.
    Only TNL address discovery related messages are transferred via “X2 GW”.
    “X2 GW” function can be included in a current logical node as far as connected with X2.
    Exact name of this solution (i.e. whether to call this function as “X2 GW”) is FFS

## Slide 6: Reference
[1] R3-180319, “TNL address discovery for NSA”, NTT DOCOMO, INC.
[2] R3-182894, “Way forward on TNL Address Discovery for Option 3”, NTT DOCOMO, INC.
[3] R3-183296, “Response Paper to R3-182542, R3-182894, R3-182979 and R3-183176”, Ericsson
[4] R3-183297, “Response to R3-182543 and R3-183177”, Ericsson
[5] R3-183176, “Specification impact for TNL address discovery based on intermediate node”, Nokia, Nokia Shanghai Bell
[6] R3-183177, “TNL address discovery involving en-gNB”, Nokia, Nokia Shanghai Bell
[7] R3-182542, “En-gNB X2 TNL Address Discovery”, Huawei
[8] R3-182543, “Stage 2 CR for en-gNB X2 TNL Address Discovery”, Huawei
[9] R3-182544, “Stage 3 CR for en-gNB X2 TNL address discovery”, Huawei
[10] R3-182979, “TNL address discovery for EN-DC”, LG Electronics Inc., KT Corp.