## Slide 1: Summary of offline discussion on RRC version handling
NTT DOCOMO, INC.
R3-182429
3GPP TSG-RAN WG3 RAN3-AH-1807
Montreal, Canada, 2nd-6th July 2018

## Slide 2: Tasked work for come back
CB: # 16_RRC_Version_handling
- clarify usage
- list of supported versions vs. highest supported version?
- is OAM coordiation enough?
(NTT)
R3-184249 Summary of offline disc

## Slide 3: Introduction
Supported RRC version of gNB-CU and gNB-DU may be different considering multi-vendor operation.
  For example, updating timing may be different between vendors.
So, it is necessary to identify how to handle this issue.

## Slide 4: When issue would happen?(1/2)
Current structure of CG-config is as follows.
For or EN-DC, following transfer of this container is assumed.
In this case, RRC version alignment is not required.
  gNB-CU doesn’t decode DU part as it is octet string; CU can include it as it is transparently.
CG-Config
RB-Config:OCTET STRING
CellGroupConfig:OCTET STRING
…
Generated in CU
Generated in DU
CU
DU
CG-Config
RB-Config
CellGroupConfig
…
CG-Config
CellGroupConfig
…
MeNB
1.
2.

## Slide 5: When issue would happen?(2/2)
Current structure of MeasConfig is as follows.
For example, following transfer of this container is assumed.
In this case, RRC version alignment is required.
  gNB-DU needs to decode and encode RRC container adding DU part; CU just transfer it as it is.
MeasConfig
MeasObjectToAddMod/Remove list:
Sequence
MeasGapConfig:Sequence
…
Generated in CU
Generated in DU
CU
DU
1.
MeasConfig
MeasObjectToAddMod/Remove list
…
MeasConfig
MeasObjectToAddMod/Remove list
MeasGapConfig
…
2.

## Slide 6: Common understanding
RRC version for a UE between gNB-CU and gNB-DU needs to be aligned.
  Within one RRC container, some part is configured by gNB-CU and the other part is configured by gNB-DU (e.g. Measurement Configuration and so on)
  It implies RRC container encoded by a node needs to be decoded and re-encoded by the other node.
  If RRC version is not aligned between gNB-CU and gNB-DU, there is a risk that the other node cannot decode and re-encoded correctly; the RRC configuration for a UE may not work properly.
    Note that even if backward compatible changes are introduced between the releases, this issue would happen; the other node cannot decode and re-encode IEs which the node doesn’t support.

## Slide 7: Possible solution
Solution 1: OAM (for gNB-CU and gNB-DU ) coordination
  Not specified in 3GPP; Not sure whether it can work properly on multi-vendor operation.
Solution 2: F1-C coordination
  Specified in 3GPP; As far as 3GPP compliant, this solution would work.
RAN3 to specify Solution 2

## Slide 8: Further detail of solution 2 (F1-C coordination)
list of supported versions vs. highest supported version
  There would be only two RRC versions at maximum in principle; as far as non-backward compatible change, the latest one covers older ones.
    If there is non-backward compatible change, the supported version may need to be increased.
    However, RAN2 should define as backward compatible as much as possible; not sure non-backward compatible change needs to be considered.
  However, there was no conclusion whether highest supported version per release is necessary.
    E.g. whether supporting v16.1.0 means supporting v15.2.0 if some IE is introduced v15.2.0 after v16.1.0 was published.
  RAN3 to apply either of following options
    Highest supported version
    Highest supported version per release
UE associated signalling vs non-UE associated signalling
  Non-UE associated signaling may be enough as both nodes (i.e. gNB-CU and gNB-DU) can read UE capability; both nodes can identify which release/function is supported by the UE.
  However, there was opinion that it would be better to check whether UE associated signalling is not needed completely (e.g. in some reasons, gNB-CU and gNB-DU uses lower version than highest supported version in common.).
  RAN3 to apply non-UE associated signaling at least.

## Slide 9: Possible WF
RAN 3 to specify Solution 2 (i.e. F1-C coordination)
  Either of following options
    Highest supported version
    Highest supported version per release
  Non-UE associated signalling
  FFS on the necessity of UE associated signalling.

## Slide 10: Reference
[1] R3-183828, “Discussion on F1 RRC version handling”, Nokia, Nokia Shanghai Bell
[2] R3-183829, “Introduction of F1 RRC version handling”, Nokia, Nokia Shanghai Bell
[3]R3-184104, RRC version handling, Ericsson