## Slide 1: Views on RAN4 Rel-18 scope
3GPP TSG RAN WG4 Meeting #101-bis-e R4-2200545
Electronic Meeting, 17th – 25th January 2022
Agenda Item: 10
Source: Intel Corporation
Document for: Information

## Slide 2: RAN4 Rel-18 package
Key principles for RAN4 WI package contents
Balance the needs of the industry and the RAN4 workload constraints
Balance work among in-field issues, leftover issues from early release(s), and new enhancement
Meet the commercial demand for practical deployment and open the opportunities for further network evolution
Rel-18 RAN4-centric evolution areas based on pre-RAN #94 email discussion (non-spectrum)
Device (cross-area)
FR2 UEs with multi-beam RX (4 MIMO layer)
RF
UE FR1 & FR2 RF evolution
RRM
NR FR2 enhancements
Measurement Gap enhancements
Demodulation
UE & BS advanced RX
General & Leftovers
OTA
BS & UE enhancements
Use Cases (cross area)
NR FR1 non-co-located intra-band EN-DC/NR-CA
NR ATG (air-to-ground)
NR FR2 HST enhancement
FR2 UEs with multi-beam/chain RX
EMC
BS RF evolution
Dynamic OTA testing
Rel-17 SI continuation (Irregular CBW, pi/2 BPSK)
FR1 UEs 6RX and 8 RX
New FR2 devices
See next slides for detailed views on candidate scope for different areas

## Slide 3: Device Enhancements (cross-area)
FR2 UEs with multi-beam/chain simultaneous DL reception capabilities [see R4-2200546 and draft WID R4-2200549]
  Enhanced FR2 UEs with multi-beam simultaneous reception and multiple RX chains can provide a meaningful performance improvement in FR2 improving both demodulation performance (4-layer DL MIMO), RRM performance and improve RF spherical coverage.
  Key objectives: Define requirements for FR2 UEs capable of multi-beam/chain simultaneous DL reception on a single component carrier
      Enhanced RF requirements: spherical coverage requirements for devices with 2 panels
      Enhanced RRM requirements: measurement delay reduction, FR2-FR2 DAPS HO
      UE demodulation requirements: simultaneous reception from different directions, 4 DL MIMO layers.
      Study OTA test methodology
Single TRP + Multi-beam RX
Multi-TRP TX + Multi-beam RX

## Slide 4: Device Enhancements (cross-area)
FR1 UEs with 6RX and 8RX antennas
  LTE support operation with up to 8RX antennas for CPE/FWA type of devices. Further enhancement of the number of RX antennas at the UE side for NR can be considered to meet the market requests. To allow more flexibility for UE implementations both 6RX and 8RX shall be considered.
  Key objectives
    Enable 8Rx for FWA/CPE on higher frequency bands
      Specify the UE RF requirements to support 8Rx
      Specify RLM test cases with 8Rx
      Specify UE demodulation performance and CSI requirements to support 8Rx (up to 4 MIMO layers)
    Enable 6Rx targeting at support of smartphone/CPE/FWA form factors on higher frequency bands
      Specify the UE RF requirements to support 6Rx
      Specify RLM test cases with 6Rx
      Specify UE demodulation performance and CSI requirements to support 6Rx

## Slide 5: Use Case Enhancements (cross-area)
Background
Different coexistence conditions apply for different part of the same frequency band, so collocated Tx is not always available even for intra-band EN-DC and CA
RAN concluded MRTD or MTTD are not specified in Rel-16 or Rel-17
RRM requirements are missing for type 2 UE (Rel-16 RAN4 UE feature 2-19) when it supports intra-band NC MR-DC with the same assumption that it handles well MRTD larger than 3us
B42
n77
Non-co-located scenario for FR1 intra-band non-contiguous EN-DC and NR-CA
Candidate objectives
    Study and if feasible, support non-co-located scenario for FR1 intra-band non-contiguous EN-DC/NR-CA
      MRTD/MTTD requirements
      PDSCH demodulation performance requirement based on the applicable MRTD and power imbalance
      Consider UEs capable and not capable of supporting intra-band non-contiguous NR-CA and EN-DC in the same way to support inter-band CA, i.e., UE indicating / not capable of interBandMRDC-WithOverlapDL-Bands-r16

## Slide 6: Use Case Enhancements (cross-area)
NR FR2 HST enhancements
  Further evolution of FR2 HST requirements is recommended to allow improved NR operation under a new promising scenario
  Key objectives:
    Support HST velocity of up to a maximum of 500km/h, with carrier frequency up to 30GHz (RRM/Demod)
    Enable HST FR2 multi-panel reception CPEs (RF/RRM/Demod)
    Requirements for FR2 HST tunnel deployment scenario
    Enhanced UL timing adjustment mechanisms with large propagation delays from different TRPs to UE (if not supported in Rel-17)
NR ATG (Air-to-Ground)
  New scenario to extend 5G technology reach.
  Extensive scope discussion in Rel-17 timeframe with stable objectives.
  WI objectives in RP-212682 can be used as baseline

## Slide 7: UE RF Enhancements
FR2 RF enhancements
    FR2-2 intra-band DL/UL CA based on CBM/IBM and FR2-1/FR2-2 inter-band CA based on IBM
    CA support for FR2-2 may not be introduced in Rel-17 and can be considered for Rel-18. Comparing to FR2-1 the max frequency separation in FR2-2 band is much larger and IBM can be considered for intra-band CA on top of CBM.
  FR2 ON/ON switching time enhancements
    ON/ON transient time has a big impact on the overall spectral efficiency of FR2-1 and FR2-2. Further tightening of RF requirements can be beneficial to improve the performance and enable operation with high order modulations.
  Note: Rel-17 WI is ongoing and additional objectives can be considered subject to RAN4 progress
FR1 RF enhancements
  MSD improvement
    Improved MSD performance will have a positive impact on the overall network performance and can be considered as one of the key improvements in Rel-18. The work is expected to have relatively large scope and recommended to be performed in Rel-18 (rather than in Rel-17)
  > 2 TX antennas
    Further enhancement of UE antenna performance is possible including 3TX and/or 4TX
Further UE RF technology evolution shall be considered with a focus on enabling new use cases and performance improvement

## Slide 8: RRM and MG Enhancements
FR2 enhancements
FR2 delay reduction
Network controlled gaps for UE Rx beam switching
FR2-FR2 DAPS HO
FR2-2 enhancements & leftovers (e.g., NR-DC and FR2-1 - FR2-2 NR CA/DC)
General/leftovers
FR1 + FR1 NR-DC RRM requirements
CMTC
RLM enhancements
TCI state switch enhancements
MG related
NeedForGap requirements
Per-FR gap UE capability enhancement
MG sharing enhancements
Rel-17 leftovers (MG Enhancements and MUSIM)
RRM performance improvements are critical to ensure optimized UE in-field performance. Potential RRM enhancements scope of Rel-18 items shall balance between Rel-15/16/17 RRM “leftovers” (i.e., items deprioritized in previous releases due to TU constraints) and new RRM areas
Candidate enhancements (see details in R4-2200547 and draft WIDs R4-2200550/51)

## Slide 9: Demodulation Enhancements
UE advanced receivers
MMSE-IRC for time-selective inter-cell interference
Enhanced DL MU-MIMO receivers based on E-MMSE-IRC or R-ML
CRS-IC processing for scenarios with overlapping spectrum for LTE and NR
Enhanced DL multi-DCI multi-TRP receivers
Soft IC receivers for DL SU-MIMO
BS advanced receivers
MMSE-IRC for inter-cell interference
Demodulation performance improvements are required to optimize UE/BS performance under practical scenarios. Recommend to focus enhancements on UE/BS receiver evolution
Candidate enhancements (see details in R4-2200548 and draft WID R4-2200552)

## Slide 10: OTA Testing Enhancements
Further OTA testing enhancements can be considered to ensure proper UE device testing.
The following areas can be considered:
FR2 OTA test methods for new device types
  Current FR2 OTA test methods are focused on PC3 handheld type of devices and further extension to additional device types is beneficial to ensure proper testing of FR2 devices including PC1/PC5 FWA devices, PC3 UEs with large form factors
  FR2 OTA test methods for UEs with multi-beam/chain simultaneous DL RX
  FR2 dynamic OTA testing method