## Slide 1: Views on RAN4 Rel-18: Demodulation enhancements
3GPP TSG RAN WG4 Meeting #101-bis-e R4-2200548
Electronic Meeting, 17th – 25th January 2022
Agenda Item: 10
Source: Intel Corporation
Document for: Information

## Slide 2: Introduction
Initial discussion on Rel-18 Demodulation enhancements took place in Rel-18 workshop, pre-RAN #93 Rel-18 [RP-211667] and pre-RAN #94 Rel-18 email discussion [RP-212682].
In this contribution we provide views on candidate topics to be considered for RAN4 Rel-18 work in the UE/BS demodulation requirements area.
UE advanced receivers
  MMSE-IRC for time selective inter-cell interference
  Enhanced DL MU-MIMO receivers based on E-MMSE-IRC or R-ML
  CRS-IC processing for scenarios with overlapping spectrum for LTE and NR
  Enhanced DL multi-DCI multi-TRP receivers
  Soft IC receivers for DL SU-MIMO
BS advanced receivers
  MMSE-IRC for inter-cell interference
HST FR2 enhancements

## Slide 3: UE Advanced Receivers MMSE-IRC for time selective inter-cell interference
Motivation
Baseline UE MMSE-IRC receivers are based on DMRS-based interference estimation and rely on a constant interference structure on a full slot duration
Time-selective interference can become a bottleneck for DL performance in scenarios with a mix of SCS in different cells and for URLLC scenarios with sub-slot transmissions due to mismatched interference estimate
The definition of requirements for a time-selective interference with MMSE-IRC with DMRS-based interference-plus-noise covariance matrix estimation is under discussion in Rel-17 Perf Enhancements WI [RP-210920] as the 2nd priority objective
Enhanced MMSE-IRC receivers with data-based interference estimation or other enhancements can be considered to improve the performance under time-selective interference scenarios
Candidate objectives
Study and define enhanced UE demodulation requirements for MMSE-IRC receivers with data-based interference-plus-noise covariance matrix estimation for time-selective NR-NR inter-cell interference handling
Study whether additional network assistance is required
Time-selective NR-NR inter-cell interference
DMRS-based estimation doesn’t work
Data-based estimation provides substantial improvement

## Slide 4: UE Advanced Receivers Enhanced DL MU-MIMO receivers
Motivation
Definition of DL MU-MIMO performance requirements is under discussion in Rel-17 Enhanced Perf WI [RP-210920]. A basic MMSE-IRC receiver with serving signal demodulation and DMRS-based interference covariance matrix estimation is prioritized in Rel-17
In LTE MUST WI several receiver enhancements including E-MMSE-IRC and R-ML were studied and defined to improve the performance for MU-MIMO DMRS-based TMs (MUST Case 3) exploiting the knowledge of co-scheduled UE parameters (presence and modulation)
DL MU-MIMO Interference
Rel-15 NR design guarantees alignment of DMRS parameters and PRG grids across co-scheduled UEs (TS 38.214 5.1.6.2)
Enhanced receivers like LTE MUST Case 3 can be studied with the goal to further improve the demodulation performance for DL MU-MIMO scenarios
  Enhanced MMSE-IRC (E-MMSE-IRC) receivers with joint serving & interference signal demodulation exploiting the knowledge on co-scheduled UE presence
  R-ML receivers exploiting the knowledge on co-scheduled UE modulation
Candidate objectives
Study the performance benefits and feasibility of enhanced DL MU-MIMO receivers including E-MMSE-IRC and R-ML and required network assistance.

## Slide 5: UE Advanced Receivers CRS-IC receiver
Motivation
CRS-IM requirements for scenarios with overlapping spectrum for LTE and NR are under discussion in the Rel-17
LLR weighting was agreed as baseline algorithm for CRS-IM processing in Rel-17
CRS-IC provides significant performance improvement (up to 2 dB) in comparison to LLR weighting for various scenarios
Candidate objectives
Define NR PDSCH demodulation requirements for neighbouring cell LTE CRS-IC in scenarios with overlapping spectrum for LTE and NR
Discuss whether assumptions on network assistance signalling for LLR weighting can be reused for CRS-IC
CRS interference scenarios with overlapping spectrum for LTE and NR

## Slide 6: UE Advanced Receivers Enhancements for other scenarios
Enhanced DL multi-DCI multi-TRP receivers
    Motivation: Rel-16 eMIMO requirements for multi-DCI multi TRP scenario are defined for scenarios with non-overlapping PDSCH allocation and MMSE-IRC receiver. IC receiver can be used to improve PDSCH performance for multi-DCI multi TRP scenario with overlapping or partially overlapping PDSCH allocations.
    Candidate objectives: Study performance benefits of IC receiver for multi-DCI multi TRP scenario and define UE demodulation requirements
Soft IC receivers for DL SU-MIMO
    Motivation: DL SU-MIMO requirements are defined for MMSE-IRC and R-ML receivers. Further possible performance enhancement are possible in case of using of IC receivers.
    Candidate objectives: Study performance benefits of Soft IC receiver for DL SU-MIMO scenario

## Slide 7: BS Advanced Receivers MMSE-IRC for inter-cell interference
Motivation
Existing BS requirements are defined for noise limited conditions and do not allow verification of BS interference rejection capabilities under practical conditions
Interference-limited conditions are quite typical for 5G deployments and support of MMSE-IRC processing is important to guarantee good performance in the field (see typical LTE profiles on the right)
In RAN #89e (RP-202092) the definition MMSE-IRC for inter-cell interference was discussed and received a strong support, but was eventually deprioritized
Candidate objectives
Study typical NR UL inter-cell interference profiles
Define BS MMSE-IRC demodulation requirements for inter-cell interference scenarios
Focus on FR1 deployment scenarios
 | HomoNet |  | HetNet | 
 | DIP | INR | DIP | INR
Interf UE1 | -1.11 | 7.29 | -0.43 | 12.38
Interf UE2 | -10.91 | -2.51 | -13.78 | -0.97
UL inter-cell interference
Typical UL DIP/INR values for 85% DIP CDF based on TR 36.884

## Slide 8: FR2 HST Enhancements
Motivation
Rel-17 HST FR2 requirements are specified only for single carrier operation.
To increase DL throughput for limited number of CPEs per train and provide sufficient QoS for UEs inside the train carrier aggregation (CA) will be used in practice.
Current CA requirements cover only normal low speed scenarios and HST FR1 deployments.
Candidate objectives
Specify the UE demodulation requirements for HST FR2 CA scenario with the target speed up to 350 km/h and carrier frequency up to 30 GHz.