## Slide 1: Motivation of New WID on High Altitude Platform Station (HAPS) for NR
3GPP TSG-RAN WG4 Meeting #101bis-e
Electronic Meeting, January 17th – 25th, 2022
R4-2201675
Agenda Item: 10
Source: China Unicom

## Slide 2: Background
Background
  HAPS is expected to be deployed in remote / wide area to provide services where it is impractical to deploy ground base stations.

## Slide 3: Background
Background
  China Unicom deployed a field trial in the altitude of 1km in 2020
  Configurations
    Altitude：1km （because of the limitation of aircrafts and the instability of feeder link, 3km is tried but the data are not included in statistics）
    Frequency band： 20MHz@2.1GHz， 100MHz@3.5GHz
 | 2.1GHz | 3.5GHz
Work mode | FDD | TDD DDDSU/DDSUU
GP | - | 10:2:2 /8:4:2(for long distance)
Antenna | 4T 4R | 64T64R
Output Power | 320W | 200W
Antenna gain |  | 25dBi
5GC
Network Management System

## Slide 4: Background
Background
  Road test & fixed test
 | 3.5GHz |  | 2.1GHz | 
 | Distance | throughput | Distance | throughput
UL | 11km | 20Mbps | 11km | 50Mbps
DL | 11km | >120Mbps | 11km | 100Mbps
  There are terrestrial gNBs deployed at a distance of 8km. The city is about 11-12km away from the HAPS.
  According to the trial, the Rel-15 NR can work in HAPS scenarios but the performance is not stable and enhancements are needed.

## Slide 5: Background
Interference from the terrestrial network has an impact on the performance for the UEs
  Adjacent channel interference
    In Rel-17 HAPS coexistence study, only adjacent channel case between HAPS and TN was considered.
  Co-channel interference
    Lower Frequency band, especially below 3GHz is valuable for Terrestrial network operator.
    It is proposed for 3GPP to evaluate the Co-channel interference issue between HAPS and TN
    As shown in Figure, when the UE got into suburban area where terrestrial gNBs were deployed, the RSRP was relative similar but the PDCP data rate decreased quickly.

## Slide 6: Background
  Unstable gNB antenna surface cause inaccurate beam measurement
  The HAPS gNB antenna surface is not stable in the stratosphere and may jerk up and down by 1° even the stabilizing device is already deployed at the HAPS in the trial in the altitude of 1km.
  The outer beam may depart the original direction by kms, which may cause inaccurate beam measurement and then unnecessary handover between beams in one HAPS/between HAPS/ between HAPS and TN or cause beam failure.
Vertical Azimuth Angle
Horizon Azimuth Angle
Vertical Azimuth Angle
Horizon Azimuth Angle

## Slide 7: Objectives
The objective of the core part of the work item is to complete the left-over issues in Rel-17 RAN4 HAPS, and to specify the necessary features to support NR deployment for HAPS in Rel-18.
  Identify RF requirements for coexistence between HAPS and IMT terrestrial network
    Identify the FR1 potential band(s) to be used as example for HAPS, and FR2 bands can also be considered as example band if needed
    Co-existence evaluation for HAPS network (e.g. ACLR, ACS)
    Identify UE/BS requirements for HAPS network if necessary
  Specify test procedures for HAPS BS conformance testing.
The objective of the performance part of the work:
  RRM performance requirements and test cases for HAPS UE type, if needed.
  Demodulation performance requirements and test cases for HAPS UE/BS.