## Slide 1
3GPP TSG-RAN WG4 Meeting # 101-e R4-2117080
Electronic Meeting, November 01-12, 2021
Motivation for new WID on Home Base Station for NR
CMCC

## Slide 2: Justification
Considering that Wide Area BS and indoor power distribution system in some scenarios cannot meet the coverage of 5G network deployment, the home base station (HBS) can be utilized to enhance indoor coverage without requiring high base station output power. The application of Home Base Station for NR is a cost-effective solution in some scenarios.
However, the existing NR BS class does not specify the RF requirements of HBS. In order to meet the increasing popularity of large capacity and high reliability of data services and indoor deep coverage deployment applications, the intention of this Work Item is to introduce HBS and specify related RF specifications in Rel-18.
It is proposed to specify RF requirements for NR FR1 supporting Home Baste Station (HBS) in R18. The Work Item is to develop a new feature to enable HBS application in home scenarios for NR FR1.

## Slide 3
Core Objectives: Home BS scenarios and RF requirements
The core objectives of the work item is to specify the necessary features to support NR deployment for Home Base Station (HBS) application in Rel-18.
Specify features to core specifications of RF requirements for Home BS [RAN4]
                Identify the frequency range (FR1) and operating bands to be used for HBS
                Identify key characteristics where it is absolutely necessary to introduce HBS
                Perform FR1 co-existence evaluation for HBS network (e.g. ACLR, ACS)
                Specify new BS type(s) for HBS if necessary
                Specify RF requirements for HBS in TS 38.104 and TS 37.104
    Considering the results of co-existence evaluation in terms of impact on Tx and Rx requirements, cell sizes and link budgets, likely BS architectures, synchronization requirements and other relevant aspects
            Specify HBS conformance testing
                Determine at an early phase whether conducted, OTA or both types of testing are needed
                Specify the RF requirements for NR HBS in TS38.104 and TS37.104, and the corresponding updates on the test specification in TS38.141-1/TS38.141-2.

## Slide 4
Thanks!