## Slide 1: Title: Transmitter performance for pi/2 BPSK with spectral shaping
Source: Nokia, Nokia Shanghai Bell
Agenda item: 9.4.2 UE Tx power and related issues
Document for: Discussion
3GPP TSG-RAN WG4#101-e Meeting R4-2117473
Electronic Meeting, 1st –12th November, 2021

## Slide 2: 1- Introduction
This contribution relates to a study item agreed in RAN#91-e, namely “optimizations of pi/2 BPSK uplink power in NR” [1]. In this paper we study the transmitter performance with different shaping filters. This work is related to the following study item objective:
Identify shaping filter characteristics necessary to enable the new power capability while ensuring good and robust BS receiver performance.
  Justify specification of a pulse shaping filter for this new identified UE power capability if it differs from filter impulse response specification in TS38.101-1 clause 6.4.2.4.1.E
  Identify if necessary changes are needed to EVM equalizer flatness mask requirements to capture necessary filter shaping. Changes to the existing 14 dB p-p baseline to be assessed in relation to any potential gains in UL link performance while still ensuring robust BS receiver performance for all UEs in a cell.

## Slide 3: 2- Discussion
According to the agreed way forward after RAN4#99e [2], different filters that conform to 38.101-1 Rel-16 are tested to study the transmitter performance. In this document, three different 3-tap filters (namely [-0.2 1 -0.2], [-0.28 1 -0.28] and [-0.335 1 -0.335]) are tested, as well as two triangular windows with different design parameters. For the filters mentioned, the DMRS are also shaped, following the assumption in the current specification that the spectral shaping is transparent to the gNB receiver, agreed in the way forward [3].
Additionally, the [1+D] filter is included in the evaluations with two different configurations, in one, the DMRS are shaped (as the rest of the filters) and in another, the DMRS are not shaped.
Table 1 shows the simulation parameters.
Following the agreed way forward after RAN4#100e [3], PC2 is addressed in the evaluations.
Parameter | Value
Pulse shaping filter | Filter configuration conforms to 38.101-1 Rel-16
Waveform | DFTS OFDM with pi/2 BPSK with Rel-16 DMRS
PRB/LCRB | Full sweep of all possible combinations of RB starting locations and RB lengths
# of DMRS symbols/slot | 2
# of data symbols/slot | 12
BW | [10, 15, 20, 30, 40, 50, 60, 80, 90, 100] MHz
SCS | 30 kHz
Table 1: Simulation parameters

## Slide 4: 2- Discussion
The figure shows the tested filters. The triangular filters are generated in such a way that the slope is the maximum slope that fits the maximum attenuation in the two frequency ranges that separate one half of the allocation (same frequency ranges as the EVM equalizer flatness mask). For the evaluations, the number in brackets corresponds to the attenuation (in dB) of the first and second frequency range.
In the continuation, the filters are referred as:
[-0.2 1 -0.2]  0.2
[-0.28 1 -0.28]  0.28
[-0.335 1 -0.335]  0.335
[1+D]  [1+D]
Triangular window [6 14]  Triang A
Triangular window [6 8]  Triang B
0.335 is the most aggressive 3-tap filter that meets the current spectral flatness requirements, less aggressive 3-tap filters are included too.
Triang A is the most aggressive triangular window that meets the current spectral flatness requirements, and Triang B is a less aggressive triangular window, with frequency shape quite similar as the 0.2 3-tap filter.

## Slide 5: 2.1- Discussion. Delta w.r.t. [1+D] with the DMRS shaped
The following slides show the delta in output power for all the filters, CBW and allocations with respect to the [1+D] filter with the DMRS shaped.
Green colors mean more output power for the compared filter with respect to the [1+D], red colors mean less output power for the compared filter with respect to the [1+D].

## Slide 6: 2.1- Discussion. 10 MHz CBW. Delta w.r.t. [1+D]
The 0.335 filter gives larger output power (up to 0.8 dB) than the [1+D] filter in almost all the configurations for the 10 MHz CBW.

## Slide 7: 2.1- Discussion. 15 MHz CBW. Delta w.r.t. [1+D]
The 0.28 filter gives larger output power (up to 0.7 dB) than the [1+D] filter in almost all the configurations for the 15 MHz CBW.

## Slide 8: 2.1- Discussion. 20 MHz CBW. Delta w.r.t. [1+D]
The Triang A filter gives larger output power (up to 0.8 dB) than the [1+D] filter in almost all the configurations for the 20 MHz CBW, and the 0.335 filter provides up to 1 dB more output power for edge allocations.

## Slide 9: 2.1- Discussion. 30 MHz CBW. Delta w.r.t. [1+D]
The [1+D] filter offers the largest output power in the central and small allocations, but only up to 0.2 dB more than the 0.335 filter. For edge and medium-large allocations, the 0.335 filter offers up to 1 dB more output power.

## Slide 10: 2.1- Discussion. 40 MHz CBW. Delta w.r.t. [1+D]
The [1+D] filter offers the largest output power in the central and small allocations, but only up to 0.3 dB more than the 0.335 filter. For edge and medium-large allocations, the 0.335 filter offers up to 1.1 dB more output power.

## Slide 11: 2.1- Discussion. 50 MHz CBW. Delta w.r.t. [1+D]
The [1+D] filter offers the largest output power in the central and small allocations, but only up to 0.2 dB more than the 0.335 filter. For edge and medium-large allocations, the 0.335 filter offers up to 1.2 dB more output power.

## Slide 12: 2.1- Discussion. 60 MHz CBW. Delta w.r.t. [1+D]
The 0.335 filter gives larger output power (up to 1.4 dB) than the [1+D] filter in almost all the configurations for the 60 MHz CBW.

## Slide 13: 2.1- Discussion. 80 MHz CBW. Delta w.r.t. [1+D]
The Triang A filter gives larger output power (up to 1.1 dB) than the [1+D] filter in almost all the configurations for the 80 MHz CBW.

## Slide 14: 2.1- Discussion. 90 MHz CBW. Delta w.r.t. [1+D]
The 0.2, 0.335 and Triang A filters give larger output power (up to 1.3 dB) than the [1+D] filter in almost all the configurations for the 90 MHz CBW.

## Slide 15: 2.1- Discussion. 100 MHz CBW. Delta w.r.t. [1+D]
The 0.28, 0.335 and Triang A filters give larger output power (up to 1.3 dB) than the [1+D] filter in almost all the configurations for the 90 MHz CBW.

## Slide 16: 2.1- Discussion. Delta w.r.t. [1+D] with the DMRS shaped
Observation 1: For all the tested channel bandwidth, and allocation configurations, there are filters that conform to 38.101-1 Rel-16 requirements that offer larger or same output power than the [1+D] filter with DMRS shaping.

## Slide 17: 2.2- Discussion. Delta w.r.t. [1+D] with the DMRS not shaped
The following slides show the delta in output power for all the filters, CBW and allocations with respect to the [1+D] filter with the DMRS not shaped.
Green colors mean more output power for the compared filter with respect to the [1+D] with DMRS not shaped, red colors mean less output power for the compared filter with respect to the [1+D] with DMRS not shaped.

## Slide 18: 2.2- Discussion. 10 MHz CBW. Delta w.r.t. [1+D] DMRS not shaped

## Slide 19: 2.2- Discussion. 15 MHz CBW. Delta w.r.t. [1+D] DMRS not shaped

## Slide 20: 2.2- Discussion. 20 MHz CBW. Delta w.r.t. [1+D] DMRS not shaped

## Slide 21: 2.2- Discussion. 30 MHz CBW. Delta w.r.t. [1+D] DMRS not shaped

## Slide 22: 2.2- Discussion. 40 MHz CBW. Delta w.r.t. [1+D] DMRS not shaped

## Slide 23: 2.2- Discussion. 50 MHz CBW. Delta w.r.t. [1+D] DMRS not shaped

## Slide 24: 2.2- Discussion. 60 MHz CBW. Delta w.r.t. [1+D] DMRS not shaped

## Slide 25: 2.2- Discussion. 80 MHz CBW. Delta w.r.t. [1+D] DMRS not shaped

## Slide 26: 2.2- Discussion. 90 MHz CBW. Delta w.r.t. [1+D] DMRS not shaped

## Slide 27: 2.2- Discussion. 100 MHz CBW. Delta w.r.t. [1+D] DMRS not shaped

## Slide 28: 2.2- Discussion. Delta w.r.t. [1+D] with the DMRS not shaped
Observation 2: For all the tested channel bandwidth, and allocation configurations, there are filters that conform to 38.101-1 Rel-16 requirements that offer larger or same output power than the [1+D] filter without DMRS shaping.
Observation 3: When comparing [1+D] results with and without DMRS shaping, it can be noted that in most of the cases DMRS without shaping offers smaller output power.

## Slide 29: 2.3- Discussion. Best filters per channel bandwidth.
The following slides show the best filter per channel BW and transmission configuration. The criteria followed is to select the filter that offers the highest output power, and in case there are more than one filter with the same highest output power, the one with lower EVM is chosen.

## Slide 30: 2.3- Discussion. Best filters per channel bandwidth.
10 MHz: For central and small-medium size transmission, 0.2 and Triang B (less aggressive filters) offer best performance. For edge transmission, 0.335 and 0.28 (more aggressive than Triang B and 0.2) are best. For the small allocations, less aggressive filters perform better.
15 MHz: Central and small-medium allocations, 0.2 and Triang B are best. For edge and medium-large allocations, small difference between 0.335, 0.28.

## Slide 31: 2.3- Discussion. Best filters per channel bandwidth.
20 MHz: Small and medium allocations, less aggressive filters perform better (0.2 and Triang B). For larger (and edge) allocations, more aggressive filters (0.28, 0.335 and Triang A). [1+D] is barely ever the best filter.
30 MHz: Small and medium allocations, less aggressive filters perform better (0.2 and Triang B). For larger allocations, closer to the edge, 0.335 is best, and 0.28 for allocations further from the edge.

## Slide 32: 2.3- Discussion. Best filters per channel bandwidth
40 MHz: For small and central allocations, 0.2 and Triang B are the best. For 1 PRB allocation, closer to the edges, [1+D] is the best. Again, for larger allocations, and edge allocations, more aggressive filters perform better.
50 MHz: For small and central allocations, 0.2 and Triang B are the best. Again, for larger allocations, and edge allocations, more aggressive filters perform better.

## Slide 33: 2.3- Discussion. Best filters per channel bandwidth
60 MHz: For small and central allocations, 0.2 and Triang B are the best. For 1 PRB allocation, closer to the edges, 0.335 is the best. Again, for larger allocations, and edge allocations, more aggressive filters perform better.
80 MHz: For small and central allocations, 0.2 and Triang B are the best. Again, for larger allocations, and edge allocations, more aggressive filters perform better.

## Slide 34: 2.3- Discussion. Best filters per channel bandwidth
90 MHz: For small and central allocations, Triang B and 0.2 are the best. Again, for larger allocations, and edge allocations, more aggressive filters perform better.
100 MHz: For small and central allocations, 0.2 and Triang B are the best. Again, for larger allocations, and edge allocations, more aggressive filters perform better. For closer to the edge allocations, 0.335 is the best, then 0.28 and Triang A are better for large allocations not next to the edge of the channel.

## Slide 35: 2.3- Discussion. Best filters per channel bandwidth
Observation 4: Triangular filters have very similar performance to their closer 3-tap filter in frequency shape.
Observation 5: There is not a single solution for all the evaluated cases. Depending on the allocation configuration, different filters (i.e., more or less aggressive) perform differently.
Observation 6: For smaller allocations (e.g., ≤ 16 PRB), less aggressive filters show the best performance in terms of output power.
Observation 7: [1+D] filter with or without DMRS shaping does not present transmitter gain.

## Slide 36: 3- Conclusion
Observation 1: For all the tested channel bandwidth, and allocation configurations, there are filters that conform to 38.101-1 Rel-16 requirements that offer larger or same output power than the [1+D] filter with DMRS shaping.
Observation 2: For all the tested channel bandwidth, and allocation configurations, there are filters that conform to 38.101-1 Rel-16 requirements that offer larger or same output power than the [1+D] filter without DMRS shaping.
Observation 3: When comparing [1+D] results with and without DMRS shaping, it can be noted that in most of the cases DMRS without shaping offers smaller output power.
Observation 4: Triangular filters have very similar performance to their closer 3-tap filter in frequency shape.
Observation 5: There is not a single solution for all the evaluated cases. Depending on the allocation configuration, different filters (i.e., more or less aggressive) perform differently.
Observation 6: For smaller allocations (e.g., ≤ 16 PRB), less aggressive filters show the best performance in terms of output power.
Observation 7: [1+D] filter with or without DMRS shaping does not present transmitter gain.

## Slide 37: References
[1] RP-210910, Optimizations of pi/2 BPSK uplink power in NR, Moderator (Huawei)
[2] R4-2108018, WF on Waveform configuration, parameters for link simulations and agreements, Qualcomm
[3] R4-2115064, WF on ’Optimizations of pi/2 BPSK uplink power in NR’ in Rel-17, Nokia

## Slide 38: Appendix OBO results

## Slide 39: 10 MHz CBW. DMRS shaped

## Slide 40: 15 MHz CBW. DMRS shaped

## Slide 41: 20 MHz CBW. DMRS shaped

## Slide 42: 30 MHz CBW. DMRS shaped

## Slide 43: 40 MHz CBW. DMRS shaped

## Slide 44: 50 MHz CBW. DMRS shaped

## Slide 45: 60 MHz CBW. DMRS shaped

## Slide 46: 80 MHz CBW. DMRS shaped

## Slide 47: 90 MHz CBW. DMRS shaped

## Slide 48: 100 MHz CBW. DMRS shaped

## Slide 49: [1+D] DMRS not shaped. OBO results for all tested CBW

## Slide 50: [1+D] DMRS not shaped. OBO results for all tested CBW